## Slide 1
JVET-Q0601:
Extension of JVET-P0325
A. Robert, T. Poirier, F. Le-Léannec

## Slide 2: Predictor lists in VTM-6.0 and before JVET-Q0601
All coding modes use a predictor list
  Containing spatial neighboring candidates
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial A1 - Spatial B1 + pruned A1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial A1 - Spatial B1 + pruned A1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial A0/A1 - Spatial B0/B1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine A0/A1 + rounding AMVR -> Spatial inherited affine B0/B1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial A1 -> SbTMVP -> Spatial inherited affine A0/A1 -> Spatial inherited affine B0/B1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine

## Slide 3: Predictor lists in VTM-6.0 and before JVET-Q0601
All coding modes use a predictor list
  Containing spatial neighboring candidates
The 2 fist spatial neighbors are always left then top
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial A1 - Spatial B1 + pruned A1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial A1 - Spatial B1 + pruned A1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial A0/A1 - Spatial B0/B1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine A0/A1 + rounding AMVR -> Spatial inherited affine B0/B1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial A1 -> SbTMVP -> Spatial inherited affine A0/A1 -> Spatial inherited affine B0/B1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Left/Top scanning

## Slide 4: Predictor lists in VTM-7.0 JVET-Q0601
In VTM-7.0, JVET-P0325 has been adopted
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial A1 - Spatial B1 + pruned A1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial A0/A1 - Spatial B0/B1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine A0/A1 + rounding AMVR -> Spatial inherited affine B0/B1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial A1 -> SbTMVP -> Spatial inherited affine A0/A1 -> Spatial inherited affine B0/B1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine

## Slide 5: Predictor lists in VTM-7.0 JVET-Q0601
In VTM-7.0, JVET-P0325 has been adopted
  It switches left and top spatial candidates of the merge list
Top/Left scanning
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial A1 - Spatial B1 + pruned A1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial A0/A1 - Spatial B0/B1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine A0/A1 + rounding AMVR -> Spatial inherited affine B0/B1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial A1 -> SbTMVP -> Spatial inherited affine A0/A1 -> Spatial inherited affine B0/B1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine

## Slide 6: Predictor lists in VTM-7.0 JVET-Q0601
In VTM-7.0, JVET-P0325 has been adopted
  It switches left and top spatial candidates of the merge list
  Other coding modes remains unchanged
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial A1 - Spatial B1 + pruned A1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial A0/A1 - Spatial B0/B1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine A0/A1 + rounding AMVR -> Spatial inherited affine B0/B1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial A1 -> SbTMVP -> Spatial inherited affine A0/A1 -> Spatial inherited affine B0/B1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning
Left/Top scanning

## Slide 7: JVET-P0325 results JVET-Q0601
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.05% | -0.05% | 100% | 100%
Class A2 | 0.01% | -0.04% | -0.01% | 100% | 100%
Class B | -0.05% | 0.08% | -0.01% | 100% | 100%
Class C | -0.09% | -0.07% | -0.05% | 100% | 100%
Overall | -0.05% | -0.01% | -0.03% | 100% | 100%
Class D | -0.09% | 0.04% | 0.21% | 100% | 100%
Class F | -0.04% | -0.05% | -0.02% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.06% | -0.09% | -0.24% | 100% | 100%
Class C | -0.18% | -0.15% | -0.06% | 100% | 100%
Class E | -0.50% | -0.10% | -0.43% | 100% | 100%
Overall | -0.21% | -0.11% | -0.23% | 100% | 100%
Class D | -0.11% | -0.02% | 0.42% | 100% | 100%
Class F | 0.08% | 0.00% | 1.50% | 100% | 100%
JVET-P0325 brings gains on top of VTM-6.0

## Slide 8: Proposed unified spatial scanning JVET-Q0601
Extend JVET-P0325 to all coding modes
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1/B2 - Spatial A0/A1 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1/B2 + rounding AMVR -> Spatial inherited affine A0/A1 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1/B2 -> Spatial inherited affine A0/A1 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 9: Proposed unified spatial scanning JVET-Q0601
Extend JVET-P0325 to all coding modes
  IBC uses a light merge list -> should use a top/left scanning
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1/B2 - Spatial A0/A1 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1/B2 + rounding AMVR -> Spatial inherited affine A0/A1 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1/B2 -> Spatial inherited affine A0/A1 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 10: Proposed unified spatial scanning JVET-Q0601
Extend JVET-P0325 to all coding modes
  IBC uses a light merge list -> should use a top/left scanning
  SbTMVP uses first spatial merge cand as input -> should be top cand
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1/B2 - Spatial A0/A1 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1/B2 + rounding AMVR -> Spatial inherited affine A0/A1 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1/B2 -> Spatial inherited affine A0/A1 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 11: Proposed unified spatial scanning JVET-Q0601
Extend JVET-P0325 to all coding modes
  IBC uses a light merge list -> should use a top/left scanning
  SbTMVP uses first spatial merge cand as input -> should be top cand
  AMVP and inherited affine can be chosen from top then left positions
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1/B2 - Spatial A0/A1 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1/B2 + rounding AMVR -> Spatial inherited affine A0/A1 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1/B2 -> Spatial inherited affine A0/A1 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 12: Proposed unified spatial scanning JVET-Q0601
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | -0.01% | 0.01% | 100% | 100%
Class A2 | -0.01% | -0.01% | 0.01% | 101% | 100%
Class B | 0.02% | 0.04% | 0.02% | 101% | 101%
Class C | 0.02% | -0.06% | 0.02% | 100% | 100%
Overall | 0.02% | -0.01% | 0.01% | 100% | 100%
Class D | -0.01% | 0.00% | -0.04% | 100% | 99%
Class F | -0.01% | 0.03% | -0.02% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.00% | -0.03% | -0.26% | 99% | 99%
Class C | -0.02% | -0.35% | 0.17% | 101% | 101%
Class E | 0.04% | 0.11% | -0.41% | 100% | 100%
Overall | 0.00% | -0.10% | -0.16% | 100% | 100%
Class D | 0.01% | 0.34% | -0.11% | 101% | 100%
Class F | 0.09% | -0.54% | 0.74% | 100% | 100%

## Slide 13: Consider top-left B2 as left candidate JVET-Q0601
Extend JVET-P0325 to all coding modes
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1 - Spatial A0/A1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1 + rounding AMVR -> Spatial inherited affine A0/A1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1 -> Spatial inherited affine A0/A1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 14: Consider top-left B2 as left candidate JVET-Q0601
Extend JVET-P0325 to all coding modes
For AMVP and inherited affine models
  Top-left B2 spatial candidate is considered as a left candidate
  It remains the last spatial scanned position
List | Merge/CIIP/MMVD/ TPM/GEO | IBC | AMVP | Affine AMVP | Sub-block Merge
Candidates | - Spatial B1 - Spatial A1 + pruned B1 - Spatial B0 + pruned B1 - Spatial A0 + pruned A1 - Spatial B2 + pruned A1/B1 - TMVP C0/C1 - HMVP + 2 first pruned A1/B1 + let one space for pairwise - Pairwise of cand {0,1} - Fulfill with zero | - Spatial B1 - Spatial A1 + pruned B1 - HMVP + 2 first pruned A1/B1 - Fulfill with zero | - Spatial B0/B1 - Spatial A0/A1/B2 - Rounding AMVR - Prune spatial cand - TMVP C0/C1 + rounding AMVR - HMVP + rounding AMVR - Fulfill with zero | -> Spatial inherited affine B0/B1 + rounding AMVR -> Spatial inherited affine A0/A1/B2 + rounding AMVR - Spatial LT B2/B3/A2 + rounding AMVR - Spatial RT B1/B0 + rounding AMVR - Spatial LB A1/A0 + rounding AMVR -> Virtual affine with {LT,RT,LB}, {LT,RT} -> Translational with LB, RT, LT -> Translational with TMVP C0/C1 -> Fulfill with zero affine | - Spatial B1 -> SbTMVP -> Spatial inherited affine B0/B1 -> Spatial inherited affine A0/A1/B2 - Spatial LT B2/B3/A2 - Spatial RT B1/B0 - Spatial LB A1/A0 - TMVP RB C0 -> Virtual affine with {LT,RT,LB}, {LT,RT,RB}, {LT,LB,RB}, {RT,LB,RB}, {LT,RT}, {LT,LB} -> Fulfill with zero affine
Top/Left scanning

## Slide 15: Proposed unified spatial scanning JVET-Q0601
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.01% | 0.03% | 101% | 100%
Class A2 | 0.00% | 0.01% | 0.07% | 101% | 98%
Class B | 0.01% | 0.02% | 0.05% | 100% | 101%
Class C | 0.01% | 0.06% | -0.02% | 100% | 99%
Overall | 0.01% | 0.02% | 0.03% | 100% | 100%
Class D | -0.01% | 0.09% | 0.00% | 100% | 101%
Class F | -0.02% | 0.00% | -0.07% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.00% | -0.23% | 0.21% | 100% | 100%
Class C | 0.00% | -0.25% | 0.05% | 101% | 101%
Class E | 0.04% | 0.22% | -0.56% | 100% | 101%
Overall | 0.01% | -0.12% | -0.03% | 100% | 100%
Class D | -0.01% | 0.35% | -0.14% | 101% | 101%
Class F | 0.07% | -0.16% | 1.05% | 100% | 100%

## Slide 16: Conclusion JVET-Q0601
Unification of spatial neighbors scanning
  By extending JVET-P0325
    0.02% in RA (with a max of 0.06% in class A1)
    Keep performances in LDB
  By extending JVET-P0325 and considering top-left cand B2 as a left cand
    0.01% in RA (with a max of 0.04% in class A1)
    0.01% in LDB (with 0.00% in class B and C)
  Both methods have same complexity as VTM-7.0
Allow unification of the design with negligible loss
  Thanks to xxx for cross-checking

## Slide 17: Thank you