## Slide 1: AHG2: On minimum QT size, maximum BT size and maximum TT size
Han Huang, Jianle Chen, Wei-Jung Chien, Marta Karczewicz
Location
Date
@qualcomm

## Slide 2: Problem statement
Dual-tree
  Implicit QT split for a block with width/height larger than 64
    128 is equivalent to 64 for the minQtSize, maxBtSize and maxTtSize
VPDU constrain
  TT is not allow for a block with width/height larger than 64
    128 is equivalent to 64 for the maxTtSize
minQtSizeIntraLuma : [minLumaCbSize, ctuSize]
maxBtSizeIntraLuma : [minQtSizeIntraLuma, ctuSize]
maxTtSizeIntraLuma : [minQtSizeIntraLuma, ctuSize]
minQtSizeIntraChroma : [minLumaCbSize, ctuSize]
maxBtSizeIntraChroma : [minQtSizeIntraChroma, ctuSize]
maxTtSizeIntraChroma : [minQtSizeIntraChoma, ctuSize]
Intra Slice
Inter Slice
ctuSize : [32, 128]
minLumaCbSize : [4, min(64,ctuSize)]
minQtSizeInter : [minLumaCbSize, ctuSize]
maxBtSizeInter : [minQtSizeInter, ctuSize]
maxTtSizeInter : [minQtSizeInter, ctuSize]
Range of partitioning related sizes

## Slide 3: Solution
Set the upper limit of minQtSize and maxTtSize to 64
Set the upper limit of maxBtSize to 64 in dual-tree

## Slide 4: Test results
MinQTChromaISlice : 64
MinQTLumaISlice : 128
MinQTNonISlice : 128
MaxBTLumaISlice : 128
MaxBTChromaISlice : 128
MaxBTNonISlice : 128
MaxTTLumaISlice : 128
MaxTTChromaISlice : 128
MaxTTNonISlice : 128
 |  |  | All Intra Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | 6.04% | 30.20% | 32.89% | 80% | 78% | 11.85%
Class A2 | 3.93% | 14.91% | 10.05% | 55% | 82% | 5.51%
Class B | 5.92% | 14.12% | 16.64% | 56% | 73% | 7.73%
Class C | 13.23% | 23.83% | 25.82% | 45% | 68% | 15.45%
Class E | 8.98% | 7.52% | 8.38% | 54% | 78% | 8.75%
Overall | 7.74% | 17.99% | 18.91% | 56% | 75% | 9.93%
Class D | 12.34% | 21.20% | 22.26% | 44% | 66% | 14.04%
Class F | 25.63% | 34.10% | 39.98% | 35% | 70% | 27.98%
 |  |  | Random access Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | 14.84% | 21.05% | 24.63% | 26% | 83% | 17.15%
Class A2 | 23.72% | 32.21% | 27.40% | 25% | 88% | 24.79%
Class B | 29.81% | 31.52% | 32.73% | 26% | 82% | 30.29%
Class C | 62.52% | 54.00% | 61.77% | 33% | 85% | 61.70%
Class E |  |  |  |  |  | 
Overall | 34.32% | 35.56% | 37.79% | 27% | 84% | 34.94%
Class D | 53.11% | 50.54% | 52.56% | 44% | 89% | 52.79%
Class F | 56.60% | 54.26% | 59.36% | 31% | 92% | 56.65%
 |  |  | Low delay B Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 29.54% | 24.06% | 24.41% | 24% | 74% | 28.76%
Class C | 70.26% | 45.04% | 50.74% | 34% | 84% | 66.21%
Class E | 30.19% | 22.93% | 24.56% | 37% | 107% | 28.80%
Overall | 43.27% | 30.77% | 33.23% | 30% | 85% | 41.25%
Class D | 59.61% | 42.48% | 47.68% | 49% | 90% | 57.12%
Class F | 97.28% | 68.84% | 73.67% | 33% | 98% | 91.97%

## Slide 5: Test results
MinQTChromaISlice : 32
MinQTLumaISlice : 64
MinQTNonISlice : 64
MaxBTLumaISlice : 128
MaxBTChromaISlice : 128
MaxBTNonISlice : 128
MaxTTLumaISlice : 128
MaxTTChromaISlice : 128
MaxTTNonISlice : 128
 |  |  | All Intra Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V |  | EncT | DecT
Class A1 | 6.05% | 30.20% | 32.89% | 11.85% | 80% | 78%
Class A2 | 3.93% | 14.91% | 10.05% | 5.51% | 55% | 81%
Class B | 5.92% | 14.13% | 16.64% | 7.73% | 56% | 73%
Class C | 13.23% | 23.83% | 25.83% | 15.46% | 46% | 68%
Class E | 8.99% | 7.54% | 8.39% | 12.36% | 54% | 76%
Overall | 7.75% | 17.99% | 18.92% | 9.94% | 56% | 74%
Class D | 12.36% | 21.23% | 22.28% | 14.06% | 44% | 67%
Class F | 25.63% | 34.10% | 39.99% | 27.99% | 35% | 69%
 |  |  | Random Access Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 2.70% | 6.97% | 7.33% | 3.99% | 63% | 86%
Class A2 | 3.84% | 10.41% | 7.46% | 4.88% | 60% | 91%
Class B | 5.05% | 10.50% | 10.64% | 6.14% | 62% | 88%
Class C | 12.33% | 16.32% | 18.44% | 13.35% | 60% | 87%
Class E |  |  |  |  |  | 
Overall | 6.28% | 11.33% | 11.42% | 7.38% | 61% | 88%
Class D | 13.32% | 20.95% | 22.27% | 14.86% | 63% | 95%
Class F | 21.68% | 24.39% | 27.32% | 22.57% | 52% | 95%
 |  |  | Low Delay B Main10 |  |  | 
 |  |  | Over VTM-8.0 |  |  | 
 | Y | U | V |  | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 3.05% | 4.36% | 3.94% | 3.30% | 61% | 84%
Class C | 8.00% | 9.98% | 11.33% | 8.55% | 62% | 87%
Class E | 3.05% | 3.50% | 5.03% | 8.11% | 67% | 103%
Overall | 4.70% | 6.02% | 6.67% | 5.05% | 63% | 90%
Class D | 9.54% | 11.91% | 13.72% | 8.11% | 67% | 93%
Class F | 13.50% | 15.08% | 16.45% | 14.00% | 61% | 99%

## Slide 6: Test results
 |  |  | All Intra Main10 |  |  | 
 |  |  | Test 2 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00%
Class A2 | 0.00% | 0.00% | 0.00% | 99% | 98% | 0.00%
Class B | 0.00% | 0.00% | 0.00% | 100% | 99% | 0.00%
Class C | 0.00% | 0.00% | 0.00% | 100% | 99% | 0.00%
Class E | 0.01% | 0.01% | 0.01% | 100% | 97% | 0.01%
Overall | 0.00% | 0.00% | 0.00% | 100% | 99% | 0.00%
Class D | 0.02% | 0.02% | 0.02% | 100% | 101% | 0.02%
Class F | 0.01% | 0.01% | 0.01% | 100% | 100% | 0.01%
 |  |  | Random access Main10 |  |  | 
 |  |  | Test 2 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | -10.43% | -11.19% | -13.31% | 246% | 105% | -11.00%
Class A2 | -15.96% | -16.13% | -15.47% | 238% | 104% | -15.82%
Class B | -18.76% | -15.46% | -16.11% | 242% | 106% | -18.24%
Class C | -30.42% | -23.80% | -26.12% | 184% | 103% | -29.42%
Class E |  |  |  |  |  | 
Overall | -19.65% | -16.96% | -18.09% | 225% | 105% | -19.29%
Class D | -25.52% | -18.25% | -18.53% | 143% | 107% | -24.24%
Class F | -22.26% | -18.72% | -19.33% | 171% | 103% | -21.56%
 |  |  | Low delay B Main10 |  |  | 
 |  |  | Test 2 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | -20.29% | -15.45% | -16.05% | 252% | 114% | -19.60%
Class C | -36.21% | -23.64% | -25.61% | 180% | 103% | -34.39%
Class E | -20.47% | -15.51% | -15.19% | 183% | 96% | -19.42%
Overall | -25.64% | -18.19% | -19.02% | 208% | 106% | -24.48%
Class D | -31.30% | -20.38% | -22.08% | 136% | 104% | -29.79%
Class F | -39.99% | -30.80% | -31.81% | 184% | 100% | -38.45%
minQtSize64 v.s. minQtSize128
QT only and minQtSize 8 v.s. minQtSize128
 |  |  | All Intra Main10 |  |  | 
 |  |  | Test 3 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | -1.52% | -14.26% | -15.69% | 14% | 103% | -5.23%
Class A2 | 1.20% | -0.61% | 1.97% | 14% | 104% | 1.16%
Class B | 0.64% | -0.18% | -0.71% | 13% | 113% | 0.25%
Class C | -3.21% | -8.63% | -8.88% | 13% | 128% | -4.38%
Class E | 1.38% | 5.51% | 4.83% | 16% | 122% | 2.18%
Overall | -0.36% | -3.53% | -3.65% | 14% | 114% | -1.22%
Class D | -3.13% | -6.62% | -7.32% | 15% | 123% | -3.87%
Class F | -6.65% | -10.48% | -13.20% | 21% | 122% | -7.81%
 |  |  | Random access Main10 |  |  | 
 |  |  | Test 3 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | -4.48% | -7.03% | -7.48% | 46% | 106% | -5.39%
Class A2 | -8.41% | -8.66% | -6.90% | 51% | 108% | -8.10%
Class B | -13.60% | -8.62% | -8.60% | 50% | 114% | -12.67%
Class C | -29.49% | -23.62% | -26.11% | 38% | 115% | -28.70%
Class E |  |  |  |  |  | 
Overall | -14.97% | -12.31% | -12.71% | 46% | 111% | -14.57%
Class D | -25.80% | -19.57% | -20.25% | 37% | 111% | -24.74%
Class F | -22.61% | -19.97% | -21.87% | 53% | 111% | -22.27%
 |  |  | Low delay B Main10 |  |  | 
 |  |  | Test 3 over Test 1 |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | -14.32% | -4.15% | -3.77% | 55% | 122% | -12.66%
Class C | -33.70% | -19.45% | -21.19% | 41% | 124% | -31.63%
Class E | -13.73% | -4.88% | -5.01% | 68% | 116% | -11.91%
Overall | -20.63% | -9.43% | -9.89% | 53% | 121% | -18.80%
Class D | -29.84% | -15.85% | -17.55% | 37% | 112% | -27.82%
Class F | -35.06% | -22.73% | -24.09% | 66% | 113% | -32.97%