## Slide 1: JVET-R0378 TU split for ACT
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: JVET-R0378
Introduce the proposal
Experiment results
Conclusion
Entropy decoding
IQ + IT
Inverse ACT
Memory
+
Prediction
Bitstream
Y/Cg/Co
G/B/R
Reconstruction
JVET-Q0162
Large memory and latency

## Slide 3: Proposal
ACT
  JVET-Q0162
    Proposed to restrict 64-points transform in SPS level.
      But, 64-points transform is restricted even if ACT is not used in the CU.
  This proposal is to restrict when only ACT flag is enabled in CU level.
    It allows to use 64-points transform when ACT is disabled at the CU.
    When ACT is enabled, transform is split if the size is larger than 32.
Max of transform size |  | SPS ACT flag: 1 | 
 |  | VTM-8.0 | Proposal
CU ACT flag | 0 | 32 | 64
 | 1 | 32 | 32

## Slide 4: Syntax change
SPS
  Allow to present the flag, sps_act_enabled_flag even if MaxTbSize is 64.
seq_parameter_set_rbsp( ) { | Descriptor
… | 
sps_max_luma_transform_size_64_flag | u(1)
… | 
if( ChromaArrayType = = 3 && ! sps_max_luma_transform_size_64_flag ) | 
sps_act_enabled_flag | u(1)
… | 
} | 

## Slide 5: Syntax change
Transform tree
  When only ACT is enabled in CU level, the transform size is limited to 32.
  When ACT is not enabled, the transform size is allowed up to MaxTbSize.
transform_tree( x0, y0, tbWidth, tbHeight , treeType, chType ) { | Descriptor
… | 
if( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !cu_sbt_flag ) { | 
if( tbWidth > MaxTbSizeY ¦ ¦ tbHeight > MaxTbSizeY ¦ ¦ (cu_act_enabled_flag && ( tbWidth > 32 ¦ ¦ tbHeight > 32 ) ) ) { | 
verSplitFirst = ( ( tbWidth > MaxTbSizeY ¦ ¦ (cu_act_enabled_flag && tbWidth > 32 ) ) && tbWidth > tbHeight ) ? 1 : 0 | 
… | 
} else if( cu_sbt_flag ) { | 
if(cu_act_enabled_flag && ( tbWidth > 32 ¦ ¦ tbHeight > 32 ) ) { | 
verSplitFirst = ( (cu_act_enabled_flag && tbWidth > 32 ) && tbWidth > tbHeight ) ? 1 : 0 | 
trafoWidth = verSplitFirst ? ( tbWidth / 2 ) : tbWidth | 
trafoHeight = !verSplitFirst ? ( tbHeight / 2 ) : tbHeight | 
transform_tree( x0, y0, trafoWidth, trafoHeight, treeType, chType ) | 
if( verSplitFirst ) | 
transform_tree( x0 + trafoWidth, y0, trafoWidth, trafoHeight, treeType, chType ) | 
else | 
transform_tree( x0, y0 + trafoHeight, trafoWidth, trafoHeight, treeType, chType ) | 
} | 

## Slide 6: Test results, vs CTC (JVET-Q2013)
 | All Intra Main10 |  |  |  | 
 | RGB 4:4:4 |  |  |  | 
 | G | B | R | EncT | DecT
TGM 1080p | 0.06% | -0.18% | -0.17% | 96% | 101%
TGM 720p | -0.01% | -0.26% | -0.23% | 95% | 99%
Animation | 0.02% | -0.30% | -0.28% | 98% | 100%
Mixed content | -0.01% | -0.34% | -0.38% | 96% | 100%
Overall | 0.01% | -0.26% | -0.25% | 96% | 100%
 | Random access Main10 |  |  |  | 
 | RGB 4:4:4 |  |  |  | 
 | G | B | R | EncT | DecT
TGM 1080p | -0.02% | -0.24% | -0.21% | 102% | 100%
TGM 720p | 0.11% | -0.31% | -0.27% | 98% | 100%
Animation | 0.17% | -0.57% | -0.47% | 103% | 100%
Mixed content | 0.10% | -0.29% | -0.41% | 99% | 100%
Overall | 0.08% | -0.34% | -0.33% | 101% | 100%
Screen contents
Encoding time is not reliable.
 | Low delay B Main10 |  |  |  | 
 | RGB 4:4:4 |  |  |  | 
 | G | B | R | EncT | DecT
TGM 1080p | -0.20% | -0.40% | -0.36% | 106% | 99%
TGM 720p | -0.44% | -0.24% | -0.31% | 105% | 101%
Animation | 0.23% | -0.72% | -0.61% | 105% | 100%
Mixed content | 0.16% | -0.72% | -0.52% | 104% | 99%
Overall | -0.10% | -0.49% | -0.43% | 105% | 100%
 | All Intra Main10 |  |  |  | 
 | VTM8.0 |  |  |  | 
 | G | B | R | EncT | DecT
RGB 4:4:4 | -0.57% | -0.25% | -0.43% | 99% | 99%
 | Random access Main10 |  |  |  | 
 | VTM8.0 |  |  |  | 
 | G | B | R | EncT | DecT
RGB 4:4:4 | 0.20% | -0.27% | -0.24% | 104% | 100%
 | Low delay B Main10 |  |  |  | 
 | VTM8.0 |  |  |  | 
 | G | B | R | EncT | DecT
RGB 4:4:4 | #VALUE! | #VALUE! | #VALUE! | #DIV | #DIV
Natural contents

## Slide 7: Test results, vs JVET-R0321 proposal
Additional test
It was tested on proposed setting by JVET-R0321.
UseIdentityTableForNon420Chroma : 0
SameCQPTablesForAllChroma : 1
QpInValCb : 22 62
QpOutValCb : 22 62
For this comparison, the anchor data is brought from proposal data of JVET-R0321.
 | All Intra Main10 |  |  |  | 
 | Over JVET-R0321 proposal |  |  |  | 
 | R | G | B | EncT | DecT
TGM1080p | -0.05% | -0.20% | -0.20% | #NUM! | #NUM!
TGM720p | -0.02% | -0.19% | -0.13% | #NUM! | #NUM!
Animation | -0.02% | -0.23% | -0.27% | #NUM! | #NUM!
Mixed Content | -0.13% | -0.38% | -0.40% | #NUM! | #NUM!
Natural | -0.60% | -0.26% | -0.39% | #NUM! | #NUM!
Overall | -0.25% | -0.25% | -0.29% | #NUM! | #NUM!
Avg. for SCC | -0.05% | -0.25% | -0.25% |  | 
 | Random Access Main 10 |  |  |  | 
 | Over JVET-R0321 proposal |  |  |  | 
 | R | G | B | EncT | DecT
TGM1080p | -0.07% | -0.26% | -0.20% | #NUM! | #NUM!
TGM720p | -0.03% | -0.37% | -0.25% | #NUM! | #NUM!
Animation | 0.00% | -0.60% | -0.51% | #NUM! | #NUM!
Mixed Content | -0.06% | -0.40% | -0.45% | #NUM! | #NUM!
Natural | -1.59% | -0.02% | -1.23% | #NUM! | #NUM!
Overall | -0.61% | -0.26% | -0.66% | #NUM! | #NUM!
Avg. for SCC | -0.04% | -0.41% | -0.35% |  | 
Natural | Traffic | 22 | 55520.72 | 41.97 | 38.50 | 42.21 | 503141.51 | 139.76 | 139.76 |  | 55332.48 | 42.21 | 38.37 | 42.32 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 |  | -12.12% | 1.95% | -7.16%
RGB |  | 27 | 17760.76 | 39.67 | 35.45 | 39.93 | 217552.61 | 92.29 | 60.43 |  | 17536.70 | 39.95 | 35.36 | 40.07 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 |  |  |  | 
 |  | 32 | 6796.92 | 37.69 | 33.44 | 37.91 | 113291.42 | 69.16 | 31.47 |  | 6742.73 | 37.96 | 33.41 | 38.07 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 |  |  |  | 
 |  | 37 | 2786.14 | 35.55 | 31.66 | 35.67 | 66078.47 | 51.41 | 18.36 |  | 2802.22 | 35.74 | 31.69 | 35.82 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 |  |  |  | 

## Slide 8: ACT flag map
Blue blocks are ACT flag 1.
TU 64x64
ACT flag:0
With proposal
VTM-8.0

## Slide 9: Software change
Need to modify early termination
  In almost all blocks, ACT mode was chosen for Kimono QP:22.
    RD-curve
  Problem related to early termination
    RD cost TU:4x32x32 is very small than TU:64x64
      Skip mode decisions for non-ACT.
CU:64x64, TU: 4x32x32, ACT: ON
CU:64x64, TU: 64x64, ACT: OFF
Mode decision
The ET algorithm aborts consequent mode decision for ACT off.
Finally, the 64x64+ACT are always selected.
To solve this problem, the algorithm early termination was modified.
When TU is split by this proposal, it doesn’t use the cost to terminate.
Cost(CU:64x64, TU:4x32x32, ACT:ON) << cost(CU,TU:64x64, ACT:OFF)

## Slide 10: Conclusion
Propose to allow 64-points transform when ACT is disabled in the CU.
Thank to Tencent for cross-check.
 | All Intra Main10 |  |  |  | 
 | RGB 4:4:4 |  |  |  | 
 | G | B | R | EncT | DecT
TGM 1080p | 0.06% | -0.18% | -0.17% |  | 101%
TGM 720p | -0.01% | -0.26% | -0.23% |  | 99%
Animation | 0.02% | -0.30% | -0.28% |  | 100%
Mixed content | -0.01% | -0.34% | -0.38% |  | 100%
Overall | 0.01% | -0.26% | -0.25% |  | 100%
 | Random access Main10 |  |  |  | 
 | RGB 4:4:4 |  |  |  | 
 | G | B | R | EncT | DecT
TGM 1080p | -0.02% | -0.24% | -0.21% |  | 100%
TGM 720p | 0.11% | -0.31% | -0.27% |  | 100%
Animation | 0.17% | -0.57% | -0.47% |  | 100%
Mixed content | 0.10% | -0.29% | -0.41% |  | 100%
Overall | 0.08% | -0.34% | -0.33% |  | 100%
CTC in JVET-Q2013
 | All Intra Main10 |  |  |  | 
 | Over JVET-R0321 proposal |  |  |  | 
 | R | G | B | EncT | DecT
TGM1080p | -0.05% | -0.20% | -0.20% |  | 
TGM720p | -0.02% | -0.19% | -0.13% |  | 
Animation | -0.02% | -0.23% | -0.27% |  | 
Mixed Content | -0.13% | -0.38% | -0.40% |  | 
Natural | -0.60% | -0.26% | -0.39% |  | 
Overall | -0.25% | -0.25% | -0.29% |  | 
 | Random Access Main 10 |  |  |  | 
 | Over JVET-R0321 proposal |  |  |  | 
 | R | G | B | EncT | DecT
TGM1080p | -0.07% | -0.26% | -0.20% |  | 
TGM720p | -0.03% | -0.37% | -0.25% |  | 
Animation | 0.00% | -0.60% | -0.51% |  | 
Mixed Content | -0.06% | -0.40% | -0.45% |  | 
Natural | -1.59% | -0.02% | -1.23% |  | 
Overall | -0.61% | -0.26% | -0.66% |  | 
Setting by JVET-R0321

## Slide 11
Notes: 11