## Slide 1: GOP-Based Temporal Filter Improvements
Per Wennersten
Ericsson

## Slide 2: Agenda
Existing temporal filter
Additions
  Block error weighting
  Block frequency weighting
  Reference frame weighting
  Misc. changes
Results & conclusion

## Slide 3: Existing temporal filter
Motivation: if a coded pixel value is re-used in several frames, its optimal value is the average of the original in those frames
Filters frames 0, 8, 16, …
When possible, uses two frames before and after
  Motion compensation on these frames to match frame to be filtered
Filter using five collocated pixels based on intensity difference, QP and POC
Creates new original pictures for encoder, but final PSNR still measured against unfiltered original

## Slide 4: Existing temporal filter
Filter weights for collocated pixel i are determined by
depends on POC depends on distance between reference and frame to be filtered base weight bw and sigma weight sw constants
Theme to additions: Still filter single pixel using collocated pixels, but change base weight and sigma weight based on surrounding 8x8 blocks

## Slide 5: Block error weighting
Compute variance of block to be filtered, then compute SSD between it and collocated block
Next, calculate
Then modify weights of pixels in collocated block:
  If E < 50, base weight is multiplied by 1.2
  If E > 50, sigma weight is multiplied by 0.8
  If E > 100, base weight is multiplied by 0.6

## Slide 6: Block frequency weighting
Let D be the pixel-wise difference between a block in the frame to be filtered and a reference frame
Compute HSD as the sum of squared differences between horisontally neighboring pixels in D
Similarly for vertical difference VSD
Compute F as
If F >= 25, multiply base weight by 0.6 and sigma weight by 0.8

## Slide 7: Reference frame weigthing
Went up to four frames on either side of frame to be filtered
Decrease weight if other collocated blocks match our block better
Multiply base weight by

## Slide 8: Misc. changes
Tweaked motion estimation to be less complex and give slightly improved compression performance
Re-optimized various parameters

## Slide 9: Results
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1,79% | -1,77% | -2,56% | 89% | 104%
Class A2 | -1,03% | -0,70% | -0,76% | 94% | 120%
Class B | -1,32% | -1,08% | -1,07% | 87% | 100%
Class C | -1,04% | -0,53% | -0,34% | 98% | 108%
Class E |  |  |  |  | 
Overall | -1,28% | -0,99% | -1,11% | 92% | 107%
Class D | -1,31% | 0,01% | 0,25% | 100% | 111%
Class F | 0,00% | 0,00% | 0,00% | 96% | 119%
 | Over VTM-11.0 with MCTF = 0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4,50% | -8,81% | -8,66% | 86% | 89%
Class A2 | -6,17% | -10,76% | -10,56% | 89% | 101%
Class B | -7,60% | -9,30% | -9,47% | 87% | 92%
Class C | -2,68% | -4,33% | -3,89% | 98% | 94%
Class E |  |  |  |  | 
Overall | -5,38% | -8,17% | -8,04% | 90% | 94%
Class D | -0,64% | -3,44% | -3,09% | 99% | 96%
Class F | 0,00% | 0,00% | 0,00% | 99% | 100%
Note: enc/dec times are unreliable

## Slide 10: Conclusions
We would like to thank HHI for crosschecking!
They had a different result when there are only 3 frames left in the sequence after the frame to be filtered
We recommend adopting these modifications into VTM once this issue is resolved

## Slide 12: Motion estimation changes
Always consider 0-vector at each hierarchical level
Consider using MVs from above or left blocks as final step
Used to perform full-pel search on downsampled frames, then for 16x16 blocks at full res, then again for 8x8 blocks at full res, then fractional pel search for 8x8. Removed 8x8 full-pel stage.
  Small performance gain, large complexity reduction