## Slide 1: JVET-U0066: CE-3.5 and CE-3.6: Combination of CE-1.2, CE-1.4/1.5 and CE-1.3
D. Rusanovskyy, L. P. Van, M. Coban, M. Karczewicz (Qualcomm)
@qualcomm
01/2/2021
AV

## Slide 2: Content
Introduction.
Proposed methods:
- CE3.5 test: Combo of CE1.2.a, CE1.2.b and CE1.5.
- CE3.6 test: Combo of CE1.3, CE1.2.b and CE1.5.
Experimental results.
Conclusion.

## Slide 3: VVC Rice parameter derivation
locSumAbs is estimated over five coefficients template (Fig. 1).
locSumAbs is then offsetted and clipped to a range from 0.. 31
locSumAbs = Clip3( 0, 31, locSumAbs - baseLevel * 5 )
The Rice parameter is derived from Table 128 using locSumAbs as index.
Problem: Range of the Rice parameters is limited to 3, thus lead to non-optimality for HBD.
locSumAbs | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
cRiceParam | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2
locSumAbs | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
cRiceParam | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3
Fig. 1: Template using in calculation of locSumAbs
Table. 1: Table to be used in cRiceParam using locSumAbs

## Slide 4: CE-3.5 description
CE-1.2.a: Changes to template-based Rice derivation
CE-1.2.b: Rice history maintenance:
- Single history update per TU.
- History value is used for the next TU.
CE-1.5: 3 separate classes for RRC.
- Single counter for 3 classes of samples.
CE1.5 classification CE3.5 classification
C1
C2
C3
C2

## Slide 5: CE-3.5 changes to template-based Rice derivation
Parametrized normalization of rice template output.
  normSum = sumAbs * rScale >> 3, rScale = 0, 1, 2.
  normShift = ( normSum > 0) ? floorLog2(normSum) : 0
  sumAbs = sumAbs >> normShift
cRiceParam derived with normalized sumAbs as per VVC is updated:
cRiceParam = cRiceParam + normShift
Max rice param is extended from 3 to 14.
Parameter rScale is encoder derived and signaled at the slice level.

## Slide 6: CE-3.5 history concept
History usage:
  History is integrated with Rice template.
History update:
  Update from the first rice-decoded coefficient.
  Exponential moving average for counter accumulation.
  Reset at each CTU.
TU
-1
-2
-3
-4
-5
-6
-7

## Slide 7: CE-3.5 Complexity analysis
Number of additional operations to Rice derivation of VVC
Dependencies and memory requirements

## Slide 8: CE-3.6 description
CE-1.3: Changes to template-based Rice derivation
cRiceParam derivation through Table 128, as in VVC, is removed.
cRiceParam = Max(0, floorLog2(a * locSumAbs0 + b) – 5)
  a = 4, b = 0 for abs_remainder [ n ]
  a = 9, b = 20 for abs_decoded_level [ n ]
CE-1.2.b: Rice history maintenance:
- Single history update per TU.
- History value is used for the next TU.
CE-1.5: 3 separate classes for RRC.
- Single counter for 3 classes of samples.

## Slide 9: CE-3.6 Complexity analysis
Number of additional operations to Rice derivation of VVC
Dependencies and memory requirements

## Slide 10: Simulation results
Simulation according to HBD/HBR CTC, JVET-T2018
CE-3.5 CE results.
CE-3.5-related (JVET-U0070) results.
CE-3.6 CE results.
Qualcomm thanks Kwai and Sharp for cross-check of said tests.
- Kwai cross-check of CE-3.5 and CE3.6 is available in JVET-U0111.
- Kwai cross-check of CE-3.5 is available in JVET-U0113.
- Sharp cross-check of CE-3.6 is available in JVET-U0117.

## Slide 11: CE-3.5 Simulation results
CE-3.5 vs Anchor, HBD/HBR CTC, JVET-T2018

## Slide 12: CE-3.5 Simulation results (Additional test in JVET-U0070)
JVET-U0070 vs Anchor, HBD/HBR CTC, JVET-T2018

## Slide 13: CE-3.6 Simulation results
CE-3.6 vs Anchor, HBD/HBR CTC, JVET-T2018

## Slide 14: Conclusion
Algorithms descriptions for CE3.5 and CE3.6 are presented.
CE3.5: Combination of CE1.2.a, CE1.2.b and CE1.5.
CE3.6: Combination of CE1.3, CE1.2.b and CE1.5.
Performance:
- Tests demonstrate leading coding performance in CE.
- Tests add 3 additional ops. per Rice, (CE3.5 has less complex type).
- No added dependencies within TU and across CTU.
Proposal to consider a proposed method for adoption.