## Slide 1
JVET-U0069
AHG8: CABAC-bypass alignment for high bit-depth coding
2021/1/7

## Slide 2
Problem statement
The decoding process of a bypass coded bin is not so straight forward and may impact throughput of the CABAC at high-bit rate.
At high bit-depth, the significant portions of the bitstream is bypass coded.
 | Number of context coded bins/pixel | Number of by-pass coded bins/pixel
All Intra | 5.218 | 34.394
Low delay | 5.375 | 29.985
Randomaccess | 5.150 | 36.845
Number of context and bypass coded bins of SVT16 sequences
( QP = -33)
Fig: Decoding process of the bypass coded bins in VVC

## Slide 3
HEVC range extension: CABAC bypass alignment
HEVC range extension supports aligning the CABAC process prior to coding of bypass data, which allows easy, simultaneous decoding of multiple bypass bins.
Set ivlCurrRange to 256 before starting bypass coding of each coefficient group.
Decoding process of the bypass coded bins in VVC
Decoding of a bypass coded bin while ivlCurrRange == 256.
The figure is extracted from JCTVC-N0190
Benefits of bypass alignment:
  Bypass coded bins are directly visible from ivlOffset
  The bypass decoding process can be implemented using a shift register
  Multiple bypass coded bins can be decoded in parallel

## Slide 4
Proposed methods
Align: Set ivlCurrRange to 256.
Option1: In the first option, only the bypass alignment is applied only to coefficient coding within a coefficient group (CG), without affecting the coding of sb_coded_flag of a transform block (TB).
Option2: In the second option, in addition to CABAC bypass alignment, it is also proposed to switch to bypass coding of sb_coded_flag after the limit of context coded bins has been reached for the current TB.
Proposed Option1
Proposed Option2

## Slide 5
Proposed methods: High level control
Both SPS and picture level control
seq_parameter_set_rbsp( ) { | Descriptor
…. | 
sps_extension_flag | u(1)
if (sps_extension_flag) | 
{ | 
sps_range_extension_flag | u(1)
sps_extension_7bits | u(7)
} | 
if (sps_range_extension_flag) | 
sps_range_extension( ) | 
if( sps_extension_7bits ) | 
while( more_rbsp_data( ) ) | 
sps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
sps_range_extension( ) { | Descriptor
sps_cabac_bypass_alignment_enabled_flag | u(1)
} | 
picture_header_structure( ) { | 
if( pps_dbf_info_in_ph_flag ) { | 
ph_deblocking_params_present_flag | u(1)
if( ph_deblocking_params_present_flag ) { | 
if( !pps_deblocking_filter_disabled_flag ) | 
ph_deblocking_filter_disabled_flag | u(1)
if( !ph_deblocking_filter_disabled_flag ) { | 
ph_luma_beta_offset_div2 | se(v)
ph_luma_tc_offset_div2 | se(v)
if( pps_chroma_tool_offsets_present_flag ) { | 
ph_cb_beta_offset_div2 | se(v)
ph_cb_tc_offset_div2 | se(v)
ph_cr_beta_offset_div2 | se(v)
ph_cr_tc_offset_div2 | se(v)
} | 
} | 
} | 
} | 
if(sps_cabac_bypass_alignment_enabled_flag) | 
ph_cabac_bypass_alignment_flag | u(1)
if( pps_picture_header_extension_present_flag ) { | 
ph_extension_length | ue(v)
for( i = 0; i < ph_extension_length; i++) | 
ph_extension_data_byte[ i ] | u(8)
} | 
} | 

## Slide 6
Simulations: Test settings
Based on VTM-11.0 anchor:
  Option1 is applied to whole sequence
  Option2 is applied to whole sequence
  Option1 is applied to frames with temporal ID is equal to 0
  Option2 is applied to frames with temporal ID is equal to 0
Based on CE-1.2.a anchor:
  Option1 is applied to whole sequence
  Option2 is applied to whole sequence
  Option1 is applied to frames with temporal ID is equal to 0
  Option2 is applied to frames with temporal ID is equal to 0

## Slide 7
Simulation results: Anchor VTM-11.0
Option 1 – whole sequence
Option1 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.12% | 101% | 99% | 0.96% | 1.02% | 1.01% | 100% | 99% | 0.36% | 0.41% | 0.41% | 100% | 102%
LDB | 1.36% | 1.80% | 1.72% | 100% | 99% | 1.47% | 1.44% | 1.47% | 100% | 99% | 0.57% | 0.58% | 0.58% | 101% | 102%
RA | 1.33% | 1.74% | 1.65% | 100% | 99% | 1.49% | 1.46% | 1.50% | 98% | 98% | 0.57% | 0.58% | 0.59% | 100% | 103%
Overall | 1.24% | 1.55% | 1.50% | 101% | 99% | 1.31% | 1.30% | 1.33% | 100% | 99% | 0.50% | 0.52% | 0.53% | 100% | 102%
Option2 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.09% | 1.10% | 101% | 99% | 0.96% | 1.02% | 1.01% | 100% | 99% | 0.36% | 0.41% | 0.41% | 100% | 102%
LDB | 1.37% | 1.79% | 1.70% | 100% | 98% | 1.48% | 1.44% | 1.48% | 100% | 99% | 0.57% | 0.58% | 0.58% | 100% | 102%
RA | 1.32% | 1.75% | 1.65% | 100% | 98% | 1.49% | 1.46% | 1.49% | 98% | 97% | 0.57% | 0.58% | 0.59% | 100% | 102%
Overall | 1.24% | 1.54% | 1.49% | 101% | 99% | 1.31% | 1.30% | 1.33% | 100% | 98% | 0.50% | 0.52% | 0.53% | 100% | 102%
Option1 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.12% | 101% | 99% | 0.96% | 1.02% | 1.01% | 100% | 99% | 0.36% | 0.41% | 0.41% | 100% | 102%
LDB | 1.36% | 1.80% | 1.72% | 100% | 99% | 1.47% | 1.44% | 1.47% | 100% | 99% | 0.57% | 0.58% | 0.58% | 101% | 102%
RA | 0.10% | 0.10% | 0.10% | 101% | 100% | 0.10% | 0.10% | 0.10% | 99% | 99% | 0.02% | 0.02% | 0.02% | 101% | 102%
Overall | 0.83% | 1.00% | 0.98% | 101% | 99% | 0.84% | 0.85% | 0.86% | 100% | 99% | 0.32% | 0.34% | 0.34% | 101% | 101%
Option2 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.09% | 1.10% | 101% | 99% | 0.96% | 1.02% | 1.01% | 100% | 99% | 0.36% | 0.41% | 0.41% | 100% | 102%
LDB | 1.37% | 1.79% | 1.70% | 100% | 98% | 1.48% | 1.44% | 1.48% | 100% | 99% | 0.57% | 0.58% | 0.58% | 100% | 102%
RA | 0.10% | 0.10% | 0.10% | 100% | 100% | 0.09% | 0.09% | 0.09% | 98% | 99% | 0.02% | 0.02% | 0.02% | 100% | 102%
Overall | 0.83% | 1.00% | 0.97% | 100% | 99% | 0.84% | 0.85% | 0.86% | 99% | 99% | 0.32% | 0.34% | 0.34% | 100% | 102%
Option 1 - frames with Temporal id == 0
Option 2 - frames with Temporal id == 0
Option 2 – whole sequence

## Slide 8
Simulation results: Anchor CE-1.2.a
Option1 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.10% | 101% | 100% | 0.96% | 1.02% | 1.02% | 100% | 99% | 0.48% | 0.52% | 0.52% | 99% | 95%
LDB | 1.36% | 1.82% | 1.72% | 101% | 100% | 1.47% | 1.44% | 1.47% | 100% | 98% | 0.62% | 0.63% | 0.63% | 100% | 95%
RA | 1.32% | 1.76% | 1.66% | 101% | 99% | 1.49% | 1.46% | 1.49% | 100% | 98% | 0.62% | 0.64% | 0.64% | 100% | 95%
Overall | 1.24% | 1.56% | 1.49% | 101% | 100% | 1.30% | 1.31% | 1.33% | 100% | 98% | 0.58% | 0.60% | 0.60% | 100% | 95%
Option2 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.10% | 101% | 100% | 0.96% | 1.02% | 1.02% | 100% | 99% | 0.48% | 0.52% | 0.52% | 99% | 95%
LDB | 1.36% | 1.82% | 1.72% | 101% | 99% | 1.47% | 1.44% | 1.47% | 100% | 99% | 0.62% | 0.63% | 0.63% | 100% | 96%
RA | 1.32% | 1.75% | 1.66% | 101% | 99% | 1.49% | 1.46% | 1.50% | 100% | 99% | 0.62% | 0.64% | 0.64% | 100% | 96%
Overall | 1.24% | 1.56% | 1.49% | 101% | 99% | 1.31% | 1.31% | 1.33% | 100% | 99% | 0.58% | 0.60% | 0.60% | 100% | 96%
Option1 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.10% | 101% | 100% | 0.96% | 1.02% | 1.02% | 100% | 99% | 0.48% | 0.52% | 0.52% | 99% | 95%
LDB | 1.36% | 1.82% | 1.72% | 101% | 100% | 1.47% | 1.44% | 1.47% | 100% | 98% | 0.62% | 0.63% | 0.63% | 100% | 95%
RA | 0.10% | 0.11% | 0.11% | 100% | 100% | 0.09% | 0.10% | 0.10% | 100% | 100% | 0.03% | 0.02% | 0.02% | 100% | 100%
Overall | 0.83% | 1.01% | 0.98% | 100% | 100% | 0.84% | 0.85% | 0.86% | 100% | 99% | 0.38% | 0.39% | 0.39% | 100% | 97%
Option2 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 1.03% | 1.10% | 1.10% | 101% | 100% | 0.96% | 1.02% | 1.02% | 100% | 99% | 0.48% | 0.52% | 0.52% | 99% | 95%
LDB | 1.36% | 1.82% | 1.72% | 101% | 99% | 1.47% | 1.44% | 1.47% | 100% | 99% | 0.62% | 0.63% | 0.63% | 100% | 96%
RA | 0.09% | 0.10% | 0.11% | 100% | 100% | 0.09% | 0.10% | 0.09% | 100% | 100% | 0.02% | 0.02% | 0.02% | 99% | 100%
Overall | 0.83% | 1.01% | 0.98% | 100% | 100% | 0.84% | 0.85% | 0.86% | 100% | 99% | 0.38% | 0.39% | 0.39% | 100% | 97%
Option 1 + frames with Temporal id == 0
Option 2 + frames with Temporal id == 0
Option 1 – whole sequence
Option 2 – whole sequence

## Slide 9
Conclusions
Two options of bypass alignment is proposed.
  In the first option, only the bypass alignment is applied without affecting the coding of sb_coded_flag of a transform block (TB).
  In the second option, in addition to CABAC bypass alignment, it is also proposed to switch to bypass coding of sb_coded_flag after the limit of context coded bins has been reached.
SPS and PH flags are proposed for high level control
Benefits:
  Bypass coded bins are directly visible from ivlOffset
  The bypass decoding process can be implemented using a shift register
  Improve the throughput at high bit-rate

## Slide 10
Thanks Kwai and Sony for cross-checking.

## Slide 11: Back-up

## Slide 12
In case of regular residual coding:
remBinsPass1 = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  context_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (remBinsPass1 >= 4 )
      Pass 1:
        sig_coeff_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 0 ] ; remBinsPass1--;
        par_level_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 1 ] ; remBinsPass1--;
    if (bypass_alignment_enable_flag)
      CABAC bypass alignment (i.e.set ivlCurrRange to 256)
    Pass 2: abs_remainder, dec_abs_level
    Pass 3: coeff_sign_flag
In case of transform-skip residual coding:
RemCcbs = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  context_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (RemCcbs >= 4)
      Pass 1:
        sig_coeff_flag; RemCcbs--;
        coeff_sign_flag; RemCcbs--;
        abs_level_gtx_flag[ ][ 0 ] ; RemCcbs--;
        par_level_flag; RemCcbs--;
    if (RemCcbs >= 4)
      Pass 2:
        abs_level_gtx_flag [ ][ 1 ]; RemCcbs--;
        abs_level_gtx_flag [ ][ 2 ] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 3] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 4 ] ; RemCcbs--;
    if (bypass_alignment_enable_flag)
      CABAC-bypass alignment (i.e.set ivlCurrRange to 256)
    pass 3: abs_remainder, coeff_sign_flag
Pseudo code: Option 1

## Slide 13
Pseudo code: Option 2
In case of regular residual coding:
remBinsPass1 = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  if (remBinsPass1 >= 4 || bypass_alignment_enable_flag == 0)
    CABACBypasIntervalAlign = 0
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (remBinsPass1 >= 4)
      Pass 1:
        sig_coeff_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 0 ] ; remBinsPass1--;
        par_level_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 1 ] ; remBinsPass1--;
    If (CABACBypasIntervalAlign == 0 && bypass_alignment_enable_flag)
      CABAC bypass alignment (i.e.set ivlCurrRange to 256)
      CABACBypasIntervalAlign = 1
    Pass 2: abs_remainder, dec_abs_level
    Pass 3: coeff_sign_flag
In case of transform-skip residual coding:
RemCcbs = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  if (RemCcbs >= 4 || bypass_alignment_enable_flag == 0)
    CABACBypasIntervalAlign = 0
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (RemCcbs >= 4)
      Pass 1:
        sig_coeff_flag; RemCcbs--;
        coeff_sign_flag; RemCcbs--;
        abs_level_gtx_flag[ ][ 0 ] ; RemCcbs--;
        par_level_flag; RemCcbs--;
    if (RemCcbs >= 4)
      Pass 2:
        abs_level_gtx_flag [ ][ 1 ]; RemCcbs--;
        abs_level_gtx_flag [ ][ 2 ] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 3] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 4 ] ; RemCcbs--;
    If (CABACBypasIntervalAlign == 0 && bypass_alignment_enable_flag)
      CABAC-bypass alignment (i.e.set ivlCurrRange to 256)
      CABACBypasIntervalAlign = 1
    Pass 3: abs_remainder, coeff_sign_flag