## Slide 1: Investigation on CNN-based Intra Prediction
Maria Meyer, Christian Rohlfing

## Slide 2: Introduction and Dataset
Investigation on mid-size intra prediction CNN
Alternative to regular intra modes
Training methods
Architecture and complexity
Dataset
Coded and raw reference areas for training
  best for complete QP-range
Reduced number of low variance training samples
Figure 1: Comparison of training sets with different percentages of coded reference areas
Figure 2: Illustration of a block to be predicted with its mandatory and optional reference area parts

## Slide 3: Training Procedure
Reference Area
Optionally available parts masked
Larger reference area
  Better prediction, higher complexity
  Improvement steadily decreasing
Loss function
Comparison: SATD, DCT and Log
Loss function |  |  | 
Class B | -2.62% | -2.62% | -2.54%
Class C | -2.14% | -2.14% | -2.10%
Class D | -2.09% | -2.06% | -2.01%
AVG All | -2.31% | -2.30% | -2.24%
Loss function |  |  | 
Class B | -2.62% | -2.62% | -2.54%
Class C | -2.14% | -2.14% | -2.10%
Class D | -2.09% | -2.06% | -2.01%
AVG All | -2.31% | -2.30% | -2.24%
Table 1 Average Y BD-rate gains for different loss functions

## Slide 4: Architecture and Complexity
Architecture
Luma
  CNN outperforms FCN at same complexity
  FCN better for noisy content
  No padding, one line remaining, larger first kernel
Chroma
  Additional conv. branch for luma
  Predicting both chroma channels at once
Pruning
Better than unpruned networks at same complexity
Even at 87.5% pruning only 0.33% less BD-gain
Figure 4: Example of a network architecture for the prediction of a 4x4 luma block using 2 convolutional and 4 fully connected layers
Figure 5: Example of a network architecture for a 4x4 chroma block using both the available reference area from the luma and chroma surrounding

## Slide 5: Integration and Results
Integration
In HM 16.9 as additional intra mode
Extended MPM-list to 4 elements
Settings
4 reference lines
2 conv, 4 dense layer
Kernel sizes: 3 and 2
Results
Gains most likely lower in VTM
Architecture and training findings mostly independent of codec
 | All-Intra |  | 
Channel | Y | U | V
BQ Terrace | -1.77 | -0.27 | 0.29
Basketball Drive | -2.79 | -1.75 | -2.09
Cactus | -2.98 | -2.08 | -2.20
Kimono | -2.82 | -2.46 | -2.78
Park Scene | -2.71 | -1.95 | -2.56
AVG Class B | -2.61 | -1.70 | -1.87
BQ Mall | -3.00 | -2.60 | -2.92
Basketball Drill | -2.62 | -3.18 | -3.21
Party Scene | -1.75 | -1.07 | -1.21
Race Horses | -2.19 | -1.70 | -1.90
AVG Class C | -2.39 | -2.14 | -2.31
BQ Square | -1.21 | -0.38 | -0.26
Basketball Pass | -2.69 | -2.56 | -2.58
Blowing Bubbles | -1.81 | -1.38 | -1.34
Race Horses | -2.70 | -2.55 | -2.32
AVG Class D | -2.10 | -1.72 | -1.63
AVG All Classes | -2.39 | -1.84 | -1.93

## Slide 6
Questions?