## Slide 1
JVET-V0059
AHG8: CABAC-bypass alignment for high bit-depth coding
2021/4/20

## Slide 2
Problem statement
At high bit-depth, the significant portions of the bitstream is bypass coded.
The decoding process of a bypass coded bin is not so straight forward and may impact throughput of the CABAC at high-bit rate.
Decoding process of the bypass coded bins in VVC

## Slide 3
HEVC High Throughput 4:4:4 16 Intra Profile: CABAC bypass alignment
HEVC High Throughput 4:4:4 16 Intra Profile supports aligning the CABAC process prior to coding of bypass data, which allows easy, simultaneous decoding of multiple bypass bins.
Set ivlCurrRange to 256 before starting bypass coding of each coefficient group.
Decoding process of the bypass coded bins in VVC
Decoding of a bypass coded bin while ivlCurrRange == 256.
The figure is extracted from JCTVC-N0190
Benefits of bypass alignment:
  Bypass coded bins are directly visible from ivlOffset
  The bypass decoding process can be implemented using a shift register
  Multiple bypass coded bins can be decoded in parallel

## Slide 4
Proposed CABAC bypass alignment
In the In the last JVET meeting, a CABAC bypass alignment flag (similar to HEVC range extension) was proposed in JVET-U0069.
It was generally agreed that CABAC bypass alignment method in JVET-U0069 could improve the throughput in very high bit-rate professional applications, however, further study was recommended to investigate at which level (i.e. profile level, sequence level etc) this functionality is desirable.
This contribution proposed to enable CABAC bypass alignment method in VVC High Throughput 4:4:4 16 Intra Profile.
The low level algorithm is same as JVET-U0069.

## Slide 5
Proposed methods
Align: Set ivlCurrRange to 256.
Option1: In the first option, only the bypass alignment is applied only to coefficient coding within a coefficient group (CG), without affecting the coding of sb_coded_flag of a transform block (TB).
Option2: In the second option, in addition to CABAC bypass alignment, it is also proposed to switch to bypass coding of sb_coded_flag after the limit of context coded bins has been reached for the current TB.
Proposed Option1
Proposed Option2

## Slide 6
Simulations: Test settings
Only SVT 16-bit sequences will be affected by the proposed changes as all other sequences are 12-bit sequences.
SVT RGB |  |  | AI |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.47% | 0.49% | 0.49% | 100% | 93%
 |  |  | LDB |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.55% | 0.55% | 0.55% | 100% | 94%
 |  |  | RA |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.57% | 0.56% | 0.56% | 100% | 93%
Option 1
SVT RGB |  |  | AI |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.47% | 0.49% | 0.49% | 99% | 94%
 |  |  | LDB |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.55% | 0.54% | 0.54% | 100% | 94%
 |  |  | RA |  | 
 |  |  | Over CE-1 anchor |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.57% | 0.56% | 0.56% | 100% | 94%
Option 2

## Slide 7
Conclusions
Two options of bypass alignment is proposed.
  In the first option, only the bypass alignment is applied without affecting the coding of sb_coded_flag of a transform block (TB).
  In the second option, in addition to CABAC bypass alignment, it is also proposed to switch to bypass coding of sb_coded_flag after the limit of context coded bins has been reached.
Proposed to enable in High Throughput 4:4:4 16 Intra Profile.
Benefits:
  Bypass coded bins are directly visible from ivlOffset
  The bypass decoding process can be implemented using a shift register
  Improve the throughput at high bit-rate

## Slide 8
Thanks Qualcomm for cross-checking.

## Slide 9: Back-up

## Slide 10
In case of regular residual coding:
remBinsPass1 = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  context_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (remBinsPass1 >= 4 )
      Pass 1:
        sig_coeff_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 0 ] ; remBinsPass1--;
        par_level_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 1 ] ; remBinsPass1--;
    if (bypass_alignment_enable_flag)
      CABAC bypass alignment (i.e.set ivlCurrRange to 256)
    Pass 2: abs_remainder, dec_abs_level
    Pass 3: coeff_sign_flag
In case of transform-skip residual coding:
RemCcbs = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  context_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (RemCcbs >= 4)
      Pass 1:
        sig_coeff_flag; RemCcbs--;
        coeff_sign_flag; RemCcbs--;
        abs_level_gtx_flag[ ][ 0 ] ; RemCcbs--;
        par_level_flag; RemCcbs--;
    if (RemCcbs >= 4)
      Pass 2:
        abs_level_gtx_flag [ ][ 1 ]; RemCcbs--;
        abs_level_gtx_flag [ ][ 2 ] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 3] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 4 ] ; RemCcbs--;
    if (bypass_alignment_enable_flag)
      CABAC-bypass alignment (i.e.set ivlCurrRange to 256)
    pass 3: abs_remainder, coeff_sign_flag
Pseudo code: Option 1

## Slide 11
Pseudo code: Option 2
In case of regular residual coding:
remBinsPass1 = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  if (remBinsPass1 >= 4 || bypass_alignment_enable_flag == 0)
    CABACBypasIntervalAlign = 0
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (remBinsPass1 >= 4)
      Pass 1:
        sig_coeff_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 0 ] ; remBinsPass1--;
        par_level_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 1 ] ; remBinsPass1--;
    If (CABACBypasIntervalAlign == 0 && bypass_alignment_enable_flag)
      CABAC bypass alignment (i.e.set ivlCurrRange to 256)
      CABACBypasIntervalAlign = 1
    Pass 2: abs_remainder, dec_abs_level
    Pass 3: coeff_sign_flag
In case of transform-skip residual coding:
RemCcbs = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
For each coefficient group
  if (RemCcbs >= 4 || bypass_alignment_enable_flag == 0)
    CABACBypasIntervalAlign = 0
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (RemCcbs >= 4)
      Pass 1:
        sig_coeff_flag; RemCcbs--;
        coeff_sign_flag; RemCcbs--;
        abs_level_gtx_flag[ ][ 0 ] ; RemCcbs--;
        par_level_flag; RemCcbs--;
    if (RemCcbs >= 4)
      Pass 2:
        abs_level_gtx_flag [ ][ 1 ]; RemCcbs--;
        abs_level_gtx_flag [ ][ 2 ] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 3] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 4 ] ; RemCcbs--;
    If (CABACBypasIntervalAlign == 0 && bypass_alignment_enable_flag)
      CABAC-bypass alignment (i.e.set ivlCurrRange to 256)
      CABACBypasIntervalAlign = 1
    Pass 3: abs_remainder, coeff_sign_flag