## Slide 1: CE-related: On Rice parameter selection for regular residual coding (RRC) at high bit depths
JVET-V0084
Advanced Technology Team
European Professional Engineering
Sony Europe BV
Adrian Browne, Steve Keating, Karl Sharman
Sony Group Corporation

## Slide 2: Aims
Re-examination and refinement of CE-1.6
  Reduce complexity and make implementation simpler
    Reduce instructions added to VVC v1
    Reduce memory footprint for LUTs
    Reduce coupling
  Maintain, or if possible, increase gains

## Slide 3: CE-1.6
Rice coding modification for RRC
Uses series of counters (4 for luma, 4 for chroma)
  Counters selected by coefficient position in TU
From each counter 4 values are computed per TU
  Two shift values dependent on whether the coefficient is coded with the parity flag
  An upper and lower threshold
When coding, if a value is coded with Golomb-Rice on the leading diagonal,
  If value >= upper threshold, increment counter
  If (2 * value) < lowerThreshold, decrement counter
Rice parameter computed by addition of a shift and add
  locSumAbs = Min( 31, Max( locSumAbs − baseLevel * 5, 0 ) >> shift)
  rice = g_auiGoRiceParsCoeff[idx] + shift;

## Slide 4: Update modification
Replace double threshold with single threshold
  If value > threshold, increment, otherwise decrement
Remove update from rice coding loops (2nd and 3rd passes)
  Now uses full coefficient value – not just remainder
  Reduces instructions in rice coding loop
  Removes need to check if coefficient is on leading diagonal
  Simplifies implementation
Reduce 4 updates per sub-TU to 2 at fixed scan positions
  Plus DC for top left sub-block in TU
Allow counters to be negative – clip to zero at beginning of each TU

## Slide 5: Counter selection modification
CE-1.6 selects counter based on coefficient position
JVET-V0084 counter based on sub-TU index
Almost equivalent, but sub-TU index allows LUT simplification
  LUT for sub-TU can now be set using 2 conditionals
Index | Description
0 | Transform-skip
1 (Red) | DC coefficient in top left sub-TB
2 (Blue) | Coefficients within distance of 3 from DC coefficient (inclusive)
3 (Yellow) | All other coefficients
Index | Description
0 | Transform-skip
1 (Red) | DC coefficient in top left sub-block
2 (Blue) | Remaining coefficients in top left sub-block
3 (Yellow) | All other coefficients

## Slide 6: Template modification (optional)
When computing Rice parameter, value of 5 neighbouring coefficients is used.
  In VVC v1 if coefficient is outside TU (red) then value of 0 is used in calculation
  In JVET-V0084, two variants
    First same as VVC v1, use value 0
    Second use 1 << shift
  Small additional gain for second variant

## Slide 7: Results
Without template modification (vs VTM U CE) :
  Low QP (AI)
    PQ -0.26% / -0.16% / -0.16%
    HLG -0.53% / -0.33% / -0.34%
    SVT 12 -1.65% / -1.26% / -1.26%
    SVT 16 -2.94% / -2.10% / -2.08%
With template modification (vs VTM U CE) :
  Low QP
    PQ -0.29% / -0.18% / -0.18%
    HLG -0.56% / -0.34% / -0.35%
    SVT 12 -1.67% / -1.26% / -1.27%
    SVT 16 -2.94% / -2.09% / -2.07%
Improved gains over CE-1.6 for all classes

## Slide 8: Complexity
Modifications assessed to use:
  8 * 10 bit memory for counters
  16 * 2 bit for LUT
  62 instructions in addition to VVC v1 for 4x4 TU
    32 in 2nd / 3rd coding passes
  183 instructions in addition to VVC v1 for 8x8 TU
    128 in 2nd / 3rd coding passes
Additional instructions would be required to implement template modification
  Seeking further clarification (similar in concept to CE-1.4)

## Slide 9: Conclusions
Improved gains over CE-1.6
Simplified counter selection and update
Should be considered alongside CE proposals
With thanks to Alibaba for cross-checking