## Slide 1: EE2-Related: Improvements of Decoder-Side Intra Mode Derivation (JVET-V0087)
Jie Zhao, Seethal Pauliri, and Seung Hwan Kim
LG Ectronics

## Slide 2: Background: DIMD in JVET-U0100
Decoder-Side Intra Mode Derivation (DIMD) derives intra mode(s) from the reconstructed neighbouring samples to save signalling overhead.
In JVET-U0100, it uses Histogram of Gradients (HoG) Analysis to derive two intra modes. (based on JVET-O0449)
Final intra prediction is done by blending the predictions from the two derived intra modes and planar mode, i.e. weighted averaged of three modes.
Planar is assigned a weight of 1/3 and the remaining weight of 2/3 is split between the first and second mode in proportion to their HoG amplitude.
Fig. DIMD in JVET-U0100/JVET-O0449

## Slide 3: Proposed Methods
Aspect 1: not allowing the combination of DIMD and ISP.
  Based on our testing, it shows combination of DIMD and ISP does not give gain, but gives small coding loss instead.
  Propose to not allow combination of DIMD and ISP. Then, for CU with DIMD on, no need to signal ISP flag.
  This simple restriction brings small gain and also slightly reduces encoder complexity.
Aspect 2: Allow multiple DIMD blend modes
  In JVET-U0100, there is only one way to blend the two intra modes and planar.
  In this contribution, we further allow multiple ways to blend (e.g. 3).
  These 3 blend modes have different weights when blending from the two decoder derived intra modes and planar mode.
  An index is signaled to indicate which DIMD blend mode is to be used.
DIMD Index | DIMD blend mode
0 | No DIMD
1 | Blend predictions of Mode1 and Mode2
2 | Blend predictions of Mode2 and Planar (wP = 1/3)
3 | Blend predictions of Mode1, Mode2 and Planar(wP = 5/9)

## Slide 4: Experimental Results (Aspect 1)
Test setting:
  Reference: EE2 Tool on Base + DIMD
  BASE_ENCODER = 0
  BASE_NORMATIVE = 0
  TOOLS = 0
  ENABLE_DIMD =1
Aspect 1: Disallowing combination of DIMD and ISP
  This simple restriction brings DIMD additional gain of 0.07% in AI and 0.04% in RA

## Slide 5: Experimental Results (Aspect 1)
Test results if using VTM11 as anchor
For comparison, here is U0100 DIMD Tool On vs. VTM 11 (i.e. EE2 Test 2.6)
U0100 DIMD Tool On + Proposed Aspect 1 vs. VTM 11

## Slide 6: Experimental results (Aspect 2)
Test setting:
Reference: EE2 Tool on Base + DIMD
  BASE_ENCODER = 0
  BASE_NORMATIVE = 0
  TOOLS = 0
  ENABLE_DIMD =1
Aspect 2: Multiple DIMD blend modes (+ aspect 1)
  Brings DIMD additional gain of 0.23% in AI and 0.12% in RA
  It shows DIMD with flexible blending weights could get more gains, but currently there is large encoding time increase due to more RD checks.

## Slide 7: Experimental Results (Aspect 2)
Test results if using VTM11 as anchor
For comparison, here is U0100 DIMD Tool On vs. VTM 11 (i.e. EE2 Test 2.6)
U0100 DIMD Tool On + Proposed Aspect 1 & 2 vs. VTM 11

## Slide 8: Conclusion
Presented two methods to further improve coding efficiency of Decoder Side Intra Mode Derivation (DIMD) in EE2 common software/JVET-U0100.
First aspect:
  Not allow combinations DIMD and ISP.
  This simple restriction has a gain of 0.07% in AI, and gain of 0.04% in RA, and brings gain of DIMD to 0.51% in AI and 0.3% in RA.
  Thanks Qualcomm for cross-check aspect 1 (JVET-V0165) .
  Propose to include this aspect into the next EE common software.
Second aspect:
  Proposes DIMD with multiple blend modes.
  Together with aspect one, the approach achieves gain of 0.23% in AI, and 0.12% in RA. This brings gain of DIMD to 0.67% in AI and 0.38% in RA.
  It shows DIMD with flexible blending weights could get more gains, and we’d like further study on this approach.