## Slide 1: Two addition reference sample sets for CCLM
JVET-V0110

## Slide 2: Introduction
There are three LM modes in CCLM: LM_LT, LM_L and LM_T
The reference samples for deriving the LM parameters (α, β) for each mode:
LM_LT: [-1, N/4], [-1, 3N/4], [M/4, -1], [3M/4, -1]
LM_L: [-1, N’/8], [-1, 3N’/8], [-1, 5N’/8], [-1, 7N’/8]
LM_T: [M’/8, -1], [3M’/8, -1], [5M’/8, -1], [7M’/8, -1]

## Slide 3: Proposal
Propose two addition LM modes, LM_LA1 and LM_LA2, with different reference samples from current VVC:
LM_LA1: [-1, N’/8], [-1, 7N’/8], [M’/8, -1], [7M’/8, -1]
LM_LA2: [-1, 3N’/8], [-1, 5N’/8], [3M’/8, -1], [5M’/8, -1]

## Slide 4: Experiment results
Anchor: VTM11
Test: VTM11+Proposed
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.05% | -2.10% | -1.93% | 99% | 99%
Class A2 | 0.00% | -1.08% | -0.64% | 100% | 99%
Class B | 0.01% | -0.83% | -1.05% | 100% | 99%
Class C | 0.00% | -0.79% | -0.82% | 100% | 99%
Class E | -0.01% | -0.45% | -0.47% | 100% | 99%
Overall | 0.01% | -1.01% | -0.98% | 100% | 99%
Class D | 0.02% | -0.74% | -0.59% | 100% | 100%
Class F | 0.01% | -1.17% | -1.22% | 100% | 100%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.08% | -1.03% | -1.06% | 100% | 100%
Class A2 | -0.03% | -0.62% | -0.33% | 100% | 100%
Class B | 0.02% | -0.95% | -0.74% | 100% | 100%
Class C | -0.03% | -0.53% | -0.38% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | -0.79% | -0.63% | 100% | 100%
Class D | 0.00% | -0.30% | -0.22% | 100% | 100%
Class F | -0.03% | -0.83% | -0.67% | 100% | 100%

## Slide 5: Experiment results
Anchor: VTM11
Test: U0100+Proposed
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -5.35% | -10.75% | -12.59% | 227% | 233%
Class A2 | -4.91% | -8.80% | -7.04% | 219% | 212%
Class B | -4.63% | -8.12% | -8.72% | 225% | 212%
Class C | -5.40% | -7.95% | -8.36% | 227% | 189%
Class E | -5.62% | -8.06% | -7.19% | 232% | 222%
Overall | -5.13% | -8.63% | -8.75% | 226% | 212%
Class D | -4.28% | -5.94% | -5.75% | 242% | 194%
Class F | -8.14% | -10.98% | -11.54% | 170% | 188%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -11.25% | -12.36% | -15.62% | 248% | 384%
Class A2 | -12.36% | -13.88% | -13.68% | 242% | 452%
Class B | -10.71% | -12.17% | -11.79% | 245% | 390%
Class C | -12.41% | -12.80% | -13.00% | 256% | 369%
Class E |  |  |  |  | 
Overall | -11.60% | -12.72% | -13.26% | 248% | 395%
Class D | -13.52% | -13.18% | -13.17% | 273% | 389%
Class F | -10.44% | -12.56% | -12.78% | 214% | 278%

## Slide 6: Experiment results
Anchor: U0100
Test: U0100+Proposed
 |  |  | All Intra Main10 |  | 
 |  | Over EE common software | Over EE common software |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.20% | -1.29% | -1.67% | 101% | 99%
Class A2 | -0.02% | -0.64% | -0.41% | 101% | 100%
Class B | 0.00% | -0.72% | -0.99% | 101% | 100%
Class C | -0.01% | -0.44% | -0.53% | 100% | 100%
Class E | 0.01% | 0.11% | -0.33% | 101% | 100%
Overall | -0.04% | -0.61% | -0.80% | 101% | 100%
Class D | 0.02% | -0.20% | -0.19% | 101% | 100%
Class F | -0.06% | -0.55% | -0.72% | 100% | 100%
 |  |  | Random access Main10 |  | 
 |  | Over EE common software | Over EE common software |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.28% | -0.39% | -1.37% | 100% | 100%
Class A2 | -0.03% | -0.50% | -0.27% | 100% | 100%
Class B | -0.01% | -0.19% | -0.38% | 100% | 100%
Class C | 0.00% | 0.06% | -0.27% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.06% | -0.23% | -0.53% | 100% | 100%
Class D | -0.05% | 0.27% | 0.02% | 100% | 100%
Class F | 0.04% | -0.10% | -0.02% | 100% | 100%

## Slide 7: Conclusion
This proposal presents the results of two addition LM modes for CCLM.
Compare with VTM11, the simulation results report 0.01/-1.01/-0.98 BD-rate in AI configuration and 0.01/-0.79/-0.63 BD-rate in RA configuration.
The encoding/decoding time of the proposed method is negligible increase.
It is suggested to integrate into the EE software.

## Slide 8: Thank you for your attention