## Slide 1: EE2-related: Extension of template matching to Affine, CIIP, GPM merge modes, and boundary sub-blocks
Chun-Chi Chen, Vadim Seregin, Yao-Jen Chang, Zhi Zhang, Han Huang, Yan Zhang, Marta Karczewicz
April 22, 2021
JVET-V0118

## Slide 2: Introduction
    Template matching (TM) is applied to CIIP/GPM/Affine merge modes and boundary subblocks of regular merge mode
      TM CIIP: selected merge candidate is refined using TM
      TM GPM: selected GPM candidates are refined separately using TM
      TM Affine: each CPMV is refined by using 8-point search
      TM subblocks: boundary 4x4 subblocks are further refined separately
    The use of these TM-based merge modes is indicated at CU level, while last one is enabled implicitly when a merge CU is not CIIP/GPM/Subblock merge modes and is with uni-directional motion and TM enabled
    The performance change of RA relative to EE2 tool-off anchor is (Y) -0.33% (U) -0.45% (V) -0.49% (EncT.) 118% (DecT.) 102%

## Slide 3: Boundary subblock refinement with TM
    Regular merge candidate is further refined at boundary 4x4 subblocks located at the top or at the left in the current CU
    This mode is enabled implicitly when a merge CU is not CIIP/GPM/Subblock merge modes and is with uni-directional motion and TM enabled
    Each 4x4 subblocks are refined separately

## Slide 4: Affine with TM
    Assume template subblocks are on the same affine motion field as current CU
    CPMVs are searched in the same way as 8-point search in VTM (i.e., searching hor/ver 4 and then diagonal 4 points conditionally) with 3 iterations at most
Reference tpl is not located at immediately next to boundary 4x4 subblocks

## Slide 5: Proposed methods vs. Tool-off Anchor of EE2 SW