## Slide 1: JVET-V121 AHG8: on coding of last significant coefficient position for high bit depth and high bit rate extensions Fan Wang L. Xu, Z. Xie, Y. Yu, H. Yu, D. Wang

## Slide 2: Introduction
The last significant coefficient coordinates are measured in reference to the top-left corner in current VVC specification;
The last significant coefficient position tends to be closer to the bottom-right corner for high bit-rate, high bit-depth coding.

## Slide 3: Proposed method (1/3)
A set of alternative coordinates of last significant coefficient is measured and coded in reference to the bottom-right corner;
The final coordinates are calculated by subtracting the alternative coordinates from the width minus 1 or height minus 1.
(a).definition in VVC version1 (b)proposed alternative definition

## Slide 4: Proposed method (2/3)
The usage of the proposed alternative coordinates is signaled by a flag sh_reverse_last_sig_coeff_flag in the slice header;
The rest of syntax remains unchanged.
7.3.7 Slice header syntax

## Slide 5: Proposed method (3/3)
The proposed semantic modifications are highlighted in red below.

## Slide 6: Encoder setting
The following adaptive method is implemented in the encoder for specifying the sh_reverse_last_sig_coeff_flag for each slice:
  If QP > 12, sh_reverse_last_sig_coeff_flag is set equal to 0 for the current slice;
  Otherwise, if, in the last coded slice, the number of blocks with last significant coefficient position closer to the top-left corner is greater than that with last significant coefficient position closer to the bottom-right corner, sh_reverse_last_sig_coeff_flag is set equal to 0 for the current slice;
  Otherwise, sh_reverse_last_sig_coeff_flag is set equal to 1 for the current slice.

## Slide 7: Simulation results
The CTC specified for high bit depth and high bit rate video coding in [1] were used in the simulations;
The “anchor” is produced by the CE base software [2];
The “test” is produced by the proposed method implemented in the CE base software.
[1] A. Browne, T. Ikai, D. Rusanovskyy, M. Sarwer, X. Xiu “Common test conditions for high bit depth and high bit rate video coding”, JVET-U2018
[2] A. Browne, T. Hashimoto, H.-J. Jhu, D. Rusanovskyy, K. Kawamura, T. Zhou “CE on entropy coding for high bit depth and high bit rate coding”, JVET-U2022

## Slide 8: Simulation results
Low QP:

## Slide 9: Simulation results
Lossless:

## Slide 10: Conclusion
This contribution proposes a modification to the derivation method of last significant coefficient position for regular residual coding (RRC), for consideration in VVC version 2;
It is reported that the average coding efficiency as shown below is achieved
  lowQP:
    PQ AI -0.01%, -0.04%, -0.04% LD 0.00%, -0.01%, 0.03% RA 0.01%, -0.02%, 0.01%
    HLG AI -0.20%, -0.26%, -0.33% LD -0.22%, -0.27%, -0.35% RA -0.22%, -0.28%, -0.38%
    SVT AI -0.21%, -0.20%, -0.21% LD -0.20%, -0.19%, -0.20% RA -0.14%, -0.12%, -0.12%
  lossless:
    PQ AI -0.27% LD -0.36% RA -0.35%
    HLG AI -0.26% LD -0.29% RA -0.27%
    SVT AI -0.11% LD -0.10% RA -0.09%
It is recommended to conduct core experiment on this method

## Slide 11
Thanks to Alibaba for crosschecking !