## Slide 1: JVET-V122 AHG8: a full-bypass mode in residual coding for high bit depth and high bit rate extensions Fan Wang Z. Xie, Y. Yu, H. Yu, D. Wang

## Slide 2: Introduction
For high quality video applications, codecs running at high bit-rates demand high throughput;
A full-bypass mode is added to the residual coding, in both RRC and TSRC modes, where a coefficient level or residual level is coded through the bypass mode without using context-coded bins at all;
This mode is primarily designed for high quality applications with high bit-depth video signals, such as content capture, creation, and editing.

## Slide 3: Entropy coding of coefficients in VVC Main 10 profile
To guarantee the throughput, the maximum number of context coded bins for each block is limited by the initial value of “remBinsPass1” or “RemCcbs”in VVC version 1;
For RRC:
  each coefficient level may yield up to 4 context coded bins
  remaining level above 3 is bypass-coded via abs_remainder
  coefficient levels are bypass-coded via dec_abs_level if total number of ccbs reaches the limit
  coeff_sign_flag is always bypass-coded
For TSRC:
  each coefficient level may yield up to 8 context coded bins
  remaining level is bypass-coded via abs_remainder
  residual levels are bypass-coded via abs_remainder if total number of ccbs reaches the limit
  coeff_sign_flag is bypass-coded if total number of ccbs reaches the limit

## Slide 4: Proposed method (1/4)
A new syntax element sps_level_ccbs_disabled_flag is added in SPS which enables/disables the proposed method
7.3.2.4 Sequence parameter set RBSP syntax

## Slide 5: Proposed method (2/4)
The initialization methods of remBinsPass1 in RRC and RemCcbs in TSRC are modified as follows highlighted with red color:
    ( note: the proposed method is enabled by sps_level_ccbs_diabled_flag equal to 1 )
For RRC:
7.3.11.11Residual coding syntax
For TSRC:
7.3.11.11Residual coding syntax

## Slide 6: Proposed method (3/4)
For RRC, if the sps_level_ccbs_disabled_flag is equal to 1, all context coded bins are always skipped. The coefficient levels at all positions are always coded by dec_abs_level and coeff_sign_flag in bypass mode;
For TSRC, if the sps_level_ccbs_disabled_flag is equal to 1, all context coded bins are always skipped. The coefficient levels at all positions are coded by abs_remainder and coeff_sign_flag in bypass mode.

## Slide 7: Proposed method (4/4)
Proposed semantics for sps_level_ccbs_disabled_flag:
  sps_level_ccbs_disabled flag equal to 1 specifies that parameters remBinsPass1 and RemCcbs in 7.3.11.11 Residual Coding syntax are set to 0, and the coefficient levels and residual levels, at all positions, are coded in the bypass mode through dec_abs_level, coeff_sign_flag, and abs_reminder accordingly. When sps_level_ccbs_disabled_flag is equal to 0, parameters remBinsPass1 and RemCcbs in 7.3.11.11 Residual Coding syntax define the maximum number of context-coded bins for each transform block, and the coefficient levels and residual levels are coded through context-coded bins together with “bypass-coded” bins. When sps_level_ccbs_disabled_flag is not present, its value is inferred to be equal to 0.

## Slide 8: Simulation results
Test1:
  The CTC specified for high bit depth and high bit rate video coding in [1] were used in the simulations;
  The “anchor” is produced by the CE base software [2];
  The “test” is produced by the proposed method implemented in the CE base software
[1] A. Browne, T. Ikai, D. Rusanovskyy, M. Sarwer, X. Xiu “Common test conditions for high bit depth and high bit rate video coding”, JVET-U2018
[2] A. Browne, T. Hashimoto, H.-J. Jhu, D. Rusanovskyy, K. Kawamura, T. Zhou “CE on entropy coding for high bit depth and high bit rate coding”, JVET-U2022

## Slide 9: Simulation results
Low QP

## Slide 10: Simulation results
Lossless

## Slide 11: Simulation results
Test2:
  The CTC specified for high bit depth and high bit rate video coding in [1] were used in the simulations;
  The “anchor” is produced by the CE-1.5 software [2];
  The “test” is produced by the proposed method implemented in the CE-1.5 software
[1] A. Browne, T. Ikai, D. Rusanovskyy, M. Sarwer, X. Xiu “Common test conditions for high bit depth and high bit rate video coding”, JVET-U2018
[2] A. Browne, T. Hashimoto, H.-J. Jhu, D. Rusanovskyy, K. Kawamura, T. Zhou “CE on entropy coding for high bit depth and high bit rate coding”, JVET-U2022

## Slide 12: Simulation results
Low QP

## Slide 13: Simulation results
Lossless

## Slide 14: Conclusion
This contribution proposes a full-bypass mode in residual coding for high bit depth and high bit rate coding, aiming at high quality video coding applications.
It is observed that the proposed method brings over 15% saving in both encoding and decoding time, even with a slight coding efficiency gain, from the 16-bit SVT sequences.
It is recommended to conduct core experiment on this method.

## Slide 15
Thanks to Sony for crosschecking !