## Slide 1: JVET-W0117 CE-3 related: a slice level high throughput mode Fan Wang Z. Xie, Y. Yu, H. Yu, D. Wang

## Slide 2: Introduction
The high throughput mode in CE-3.2:
  A SPS level syntax element sps_high_throughput_flag is used to enable/disable the proposed method. If sps_high_throughput_flag is equal to 1, the following aspects are changed:
    The initial value of remBinsPass1 in RRC and RemCcbs in TSRC are set to 0
      the coefficient or residual levels at all positions are coded only in the bypass mode
    The sb_coded_flag is always coded in bypass mode.
      Syntax elements in sub-blocks are coded only in the bypass mode
    The alignment happens before going into sub-block
      after coding of last significant coefficient position in RRC
      at the very beginning of residual_ts_coding in TSRC

## Slide 3: Introduction
The performance of the high throughput mode depends on the video content and QP
  For high bitrate cases, it provides significant reduction in BD-bin rate, bin-to-bit ratio and decoding time
  For less throughput demanding cases, it may not be a good choice
Bitrate may change significantly when scene-cut occurs
  Especially scenes with different complexity
It is desirable to enable/disable the high throughput mode at slice level
  when a slice expected to produce a great amount of bits, enabled
  Otherwise, disabled
 |  | sequece | QP | 1st frame bits
12-bit | PQ-AI444 | BalloonFestival | -13 | 12028928
 | HLG-AI444 | DayStreet | -13 | 30470656
 | SVT-AI12 | OldTownCross | -13 | 49198072
16-bit | SVT-AI16 | OldTownCross | -33 | 70225400
Example of slice bit consuming in CTC

## Slide 4: Proposed Method
An SPS level syntax element sps_high_throughput_mode_enabled_flag is used to enable/disable the high throughput mode for current sequence.
A slice level syntax element sh_high_throughput_mode_flag is used to signal whether the high throughput mode is invoked in the current slice.

## Slide 5: Encoder setting
For the first slice, the initial setting of sh_high_throughput_mode_flag is based on the slice QP and input bitdepth.
  If the input bitdepth is 16 and QP is not greater than -5, sh_high_throughput_mode_flag is set to be 1.
  Otherwise, sh_high_throughput_mode_flag is set to be 0.
For other slices, the setting of sh_high_throughput_mode_flag is based on the previous coded slice
  if the bits consumed in the previous coded slice is greater than a threshold, sh_high_throughput_mode_flag is set to be 1
  where width and height are the width and height of that slice; format_para is 12 for 4:4:4 coding and 8 for 4:2:2 coding; thr_para is 1.5.
  otherwise, sh_high_throughput_mode_flag is set to be 0.

## Slide 6: Simulation results
CTC low QP test: the QP range in {-33,-28,-23,-18,-13,-8} for 16-bit and {-13,-8,-3,2,7,12} for 12-bit
Additional lower QP test: the QP range in {-47,-44,-41,-38,-35,-32} for 16-bit and {-23,-21,-19,-17,-15,-13} for 12-bit

## Slide 7: CTC low QP test:
SVT
PQ
HLG

## Slide 8: additional lower QP test:
SVT
PQ
HLG
the QP range in {-47,-44,-41,-38,-35,-32} for 16-bit and {-23,-21,-19,-17,-15,-13} for 12-bit

## Slide 9: Conclusion
This contribution proposes a slice level control mothed over the CE-3.2 high throughput mode.
It is suggested to adopt the proposed method in VVC operation range extensions.

## Slide 10
Thanks to Interdigital for crosschecking !