## Slide 1: JVET-W0128: AHG12: Alternative classifiers for ALF
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: Luma ALF in ECM-1.0
Filter sets are signaled in ALF_APSs
A signaled filter set can contain up to 25 luma filters
For each luma CTB, a filter set is selected
Laplacian based classifier is applied 2x2 block level to determine:
  filter index
  geometric transformation of filter coefficients

## Slide 3: Proposed two-classifier method
One out of 2 classifiers can be selected - one bit is signaled per filter set
First classifier is identical to ECM-1.0 classifier
Second classifier does not apply geometric transformation of filter coefficients
  5 options are tested
 |  | All intra |  |  | Random access |  |  | Low delay B |  | 
 | Second classifier | BD-rate Y | EncT | DecT | BD-rate Y | EncT | DecT | BD-rate Y | EncT | DecT
1) | 1 filter (no classification) | -0.05% | 100% | 97% | -0.18% | 99% | 99% | -0.29% | 102% | 98%
2) | ECM-1.0 classifier | -0.09% | 105% | 96% | -0.30% | 103% | 99% | -0.44% | 110% | 101%
3) | (sum of 2x2 block * 8) >> (bit depth + 2) | -0.11% | 100% | 97% | -0.26% | 100% | 99% | -0.44% | 100% | 99%
4) | (sum of 2x2 block * 25) >> (bit depth + 2) | -0.14% | 106% | 97% | -0.36% | 104% | 99% | -0.60% | 110% | 98%
4) enc. |  | -0.14% | 102% | 97% | -0.35% | 101% | 100% | -0.61% | 102% | 100%
5) | (sample value* 25) >> (bit depth) | -0.22% | 101% | 96% | -0.43% | 100% | 99% | -0.73% | 101% | 96%

## Slide 4: Test 4
Second classifier:
  (sum * 25) >> (sample bit depth + 2)
  sum: sum of samples for 2x2 block
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.04% | 0.04% | 108% | 98%
Class A2 | -0.09% | 0.03% | 0.03% | 104% | 98%
Class B | -0.16% | 0.04% | 0.04% | 104% | 96%
Class C | -0.18% | 0.00% | 0.00% | 106% | 97%
Class E | -0.12% | 0.06% | 0.06% | 110% | 97%
Overall | -0.14% | 0.03% | 0.03% | 106% | 97%
Class D | -0.03% | 0.00% | 0.00% | 109% | 101%
Class F | -0.17% | 0.07% | 0.07% | 106% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.29% | -0.01% | 0.00% | 102% | 100%
Class A2 | -0.29% | 0.08% | 0.06% | 102% | 99%
Class B | -0.55% | 0.10% | 0.23% | 103% | 100%
Class C | -0.21% | 0.01% | -0.11% | 106% | 99%
Class E |  |  |  |  | 
Overall | -0.36% | 0.05% | 0.06% | 104% | 99%
Class D | -0.09% | -0.04% | 0.19% | 113% | 99%
Class F | -0.21% | 0.00% | 0.13% | 110% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.91% | -0.30% | -0.35% | 106% | 99%
Class C | -0.29% | -0.56% | -0.14% | 110% | 97%
Class E | -0.49% | 0.11% | -0.12% | 116% | 99%
Overall | -0.60% | -0.28% | -0.22% | 110% | 98%
Class D | -0.08% | 0.48% | 0.17% | 120% | 102%
Class F | -0.47% | -0.12% | -0.55% | 114% | 99%

## Slide 5: Test 4 – with encoder optimization
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.04% | 0.04% | 105% | 99%
Class A2 | -0.09% | 0.03% | 0.03% | 102% | 97%
Class B | -0.16% | 0.04% | 0.04% | 101% | 98%
Class C | -0.18% | 0.00% | 0.00% | 100% | 96%
Class E | -0.12% | 0.06% | 0.06% | 101% | 98%
Overall | -0.14% | 0.03% | 0.03% | 102% | 97%
Class D | -0.03% | 0.00% | 0.00% | 98% | 97%
Class F | -0.16% | 0.07% | 0.07% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.29% | -0.02% | -0.02% | 103% | 102%
Class A2 | -0.29% | 0.10% | 0.12% | 102% | 101%
Class B | -0.54% | 0.14% | 0.17% | 101% | 100%
Class C | -0.21% | 0.01% | -0.09% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.35% | 0.07% | 0.05% | 101% | 100%
Class D | -0.09% | -0.03% | 0.19% | 96% | 97%
Class F | -0.21% | -0.02% | 0.03% | 103% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.95% | -0.23% | -0.06% | 102% | 100%
Class C | -0.29% | -0.62% | -0.20% | 100% | 101%
Class E | -0.48% | 0.15% | -0.19% | 106% | 99%
Overall | -0.61% | -0.26% | -0.14% | 102% | 100%
Class D | -0.07% | 0.35% | 0.25% | 98% | 102%
Class F | -0.49% | -0.06% | -0.34% | 102% | 98%
Second classifier:
  (sum * 25) >> (sample bit depth + 2)
  sum: sum of samples for 2x2 block

## Slide 6: Test 5
Second classifier:
  Sample-based
  (sample value * 25) >> (sample bit depth)
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | 0.06% | 0.06% | 104% | 96%
Class A2 | -0.16% | 0.04% | 0.04% | 101% | 99%
Class B | -0.25% | 0.08% | 0.08% | 100% | 96%
Class C | -0.21% | 0.01% | 0.01% | 99% | 93%
Class E | -0.25% | 0.14% | 0.13% | 101% | 97%
Overall | -0.22% | 0.06% | 0.06% | 101% | 96%
Class D | -0.06% | 0.03% | 0.03% | 97% | 99%
Class F | -0.90% | 0.30% | 0.30% | 101% | 99%
 | Random access Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.36% | 0.05% | 0.06% | 101% | 99%
Class A2 | -0.40% | 0.16% | 0.09% | 101% | 100%
Class B | -0.66% | 0.32% | 0.33% | 100% | 99%
Class C | -0.23% | 0.07% | 0.06% | 98% | 98%
Class E |  |  |  |  | 
Overall | -0.43% | 0.17% | 0.15% | 100% | 99%
Class D | -0.08% | 0.30% | 0.26% | 94% | 98%
Class F | -0.89% | 0.19% | 0.22% | 101% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.11% | -0.12% | -0.03% | 103% | 102%
Class C | -0.32% | -0.43% | -0.08% | 96% | 91%
Class E | -0.64% | -0.10% | -0.37% | 103% | 95%
Overall | -0.73% | -0.22% | -0.13% | 101% | 96%
Class D | -0.21% | -0.16% | 0.11% | 94% | 101%
Class F | -1.10% | -0.57% | -0.31% | 100% | 98%

## Slide 7: Test 1
Second classifier
  Only one filter is signaled
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.03% | -0.03% | 104% | 99%
Class A2 | 0.00% | -0.01% | -0.01% | 102% | 97%
Class B | -0.03% | -0.06% | -0.06% | 99% | 95%
Class C | -0.17% | -0.03% | -0.03% | 98% | 95%
Class E | -0.05% | -0.05% | -0.05% | 100% | 99%
Overall | -0.05% | -0.04% | -0.04% | 100% | 97%
Class D | -0.03% | -0.02% | -0.02% | 99% | 98%
Class F | -0.04% | -0.05% | -0.05% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.15% | -0.02% | 101% | 99%
Class A2 | -0.02% | 0.02% | 0.02% | 101% | 99%
Class B | -0.32% | 0.00% | 0.03% | 99% | 99%
Class C | -0.17% | -0.01% | -0.16% | 97% | 97%
Class E |  |  |  |  | 
Overall | -0.18% | -0.03% | -0.03% | 99% | 99%
Class D | -0.05% | 0.04% | 0.14% | 98% | 98%
Class F | -0.07% | -0.13% | -0.03% | 102% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.41% | -0.19% | -0.34% | 103% | 101%
Class C | -0.22% | -0.44% | -0.18% | 98% | 96%
Class E | -0.21% | -0.07% | -0.43% | 105% | 95%
Overall | -0.29% | -0.24% | -0.31% | 102% | 98%
Class D | 0.03% | 0.07% | -0.23% | 102% | 103%
Class F | -0.17% | 0.07% | -0.41% | 103% | 97%

## Slide 8: Test 2
Second classifier
  Same as the classifier in ECM-1.0
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.00% | 0.00% | 108% | 99%
Class A2 | -0.01% | 0.00% | 0.00% | 103% | 101%
Class B | -0.11% | 0.02% | 0.02% | 105% | 96%
Class C | -0.19% | 0.00% | 0.00% | 103% | 92%
Class E | -0.08% | 0.01% | 0.01% | 108% | 97%
Overall | -0.09% | 0.01% | 0.01% | 105% | 96%
Class D | -0.03% | 0.00% | 0.00% | 108% | 98%
Class F | -0.13% | 0.03% | 0.03% | 104% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.21% | -0.15% | -0.01% | 102% | 100%
Class A2 | -0.18% | 0.08% | 0.03% | 102% | 100%
Class B | -0.51% | 0.13% | 0.16% | 104% | 100%
Class C | -0.20% | 0.08% | -0.07% | 105% | 98%
Class E |  |  |  |  | 
Overall | -0.30% | 0.05% | 0.04% | 103% | 99%
Class D | -0.07% | 0.16% | 0.13% | 111% | 96%
Class F | -0.11% | -0.05% | 0.10% | 107% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.61% | -0.20% | 0.15% | 106% | 102%
Class C | -0.27% | -0.55% | -0.27% | 110% | 101%
Class E | -0.37% | -0.34% | -0.02% | 115% | 100%
Overall | -0.44% | -0.35% | -0.03% | 110% | 101%
Class D | 0.01% | 0.04% | 0.02% | 117% | 99%
Class F | -0.22% | -0.80% | -0.63% | 110% | 96%

## Slide 9: Test 3
Second classifier
  (sum * 8) >> (sample bit depth + 2)
  sum: sum of samples for 2x2 block
 | All Intra Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.01% | 0.00% | 104% | 97%
Class A2 | -0.03% | -0.02% | -0.02% | 101% | 96%
Class B | -0.11% | -0.02% | -0.02% | 99% | 96%
Class C | -0.16% | -0.02% | -0.02% | 99% | 97%
Class E | -0.11% | 0.04% | 0.04% | 102% | 102%
Overall | -0.11% | -0.01% | -0.01% | 100% | 97%
Class D | -0.03% | 0.00% | 0.00% | 99% | 100%
Class F | -0.08% | -0.02% | -0.03% | 100% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | 0.05% | -0.09% | 101% | 99%
Class A2 | -0.15% | 0.07% | 0.03% | 101% | 99%
Class B | -0.41% | 0.05% | 0.02% | 100% | 99%
Class C | -0.17% | 0.01% | -0.16% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.26% | 0.04% | -0.05% | 100% | 99%
Class D | -0.09% | 0.05% | 0.16% | 99% | 97%
Class F | -0.12% | -0.08% | 0.06% | 103% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.68% | -0.39% | -0.21% | 101% | 100%
Class C | -0.20% | -0.31% | -0.31% | 100% | 98%
Class E | -0.35% | -0.75% | -0.15% | 108% | 101%
Overall | -0.44% | -0.45% | -0.23% | 102% | 100%
Class D | -0.07% | 0.77% | 0.19% | 103% | 104%
Class F | -0.41% | 0.12% | -0.11% | 101% | 94%