## Slide 1
AHG11: MPEG NNR compressed bias update for the CNN based post-filter of EE1-1.1
M. Santamaria, J. Lainema, F. Cricri, R. G. Youvalari, H. Zhang, A. Zare, G. Rangu, H. R. Tavakoli, H. Afrabandpey, M. Hannuksela

## Slide 2
Introduction
Content-adaptive CNN based post-processing filter
Weight-update with MPEG NNR’s NCTM
  Lossy compression
  Out-of-band
  Included in bitrate and BD-rate computations
Signalling
  Scaling factor as slice parameter
  CTU on/off per channel type
Implemented using TensorFlow C API 2.3.1

## Slide 3
Neural Network Structure
Input:
  Decoded YUV patches and frame QP
  YUV420 converted into YUV444
ResNet-style block:
  2D-convolution, bias terms, LeakyReLU, skip connection
  Convolutional kernels: 64
Convolutional layers only trained in pre-training stage
AHG11: MPEG NNR compressed bias update for the CNN based post-filter of EE1-1.1

## Slide 4
Inference details
AHG11: MPEG NNR compressed bias update for the CNN based post-filter of EE1-1.1

## Slide 5
Results

## Slide 6
Remarks
CNN post-processing filter is adapted according to the test video sequence
The weight-update is lossy coded with MPEG NNR’s NCTM
The coding performance is improved when compared against JVET-X0110 where the weight-update is lossless coded with LZMA2