## Slide 1: JVET-X0135: Non-EE2: Adaptive Intra MTS
Bappaditya Ray, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2
Non-DCT2 Cands
{T0, T1, T2, T3, T4, T5}
Set1: {T0}
Set2: {T0, T1, T2, T3}.
Set3: {T0, T1, T2, T3, T4, T5}.
lastScanPos <=TH[0]
TH[0] < lastScanPos <=TH[1]
lastScanPos >=TH[1]
In ECM-2.0:
Total 5 MTS candidates: DCT2 (mts_idx = 0) and 4 non-DCT2 (mts_idx = [1, 4]).
Non-DCT2 options are intra mode and TU size dependent,
  Vertical and horizontal kernels chosen from {DST7, DCT8, DCT5, DST4, DST1, Identity}.
Non-DCT2 options only activated when scan position of last sig coeff (lastScanPos) is greater than 0.
Number of non-DCT2 options fixed.
Proposal:
Flexible number of non-DCT2 options (1, 4, or 6) based on lastScanPos value.
  Lower number of candidates lastScanPos is small, and vice versa.

## Slide 3
mts_idx > 0?
[1, TH[0]]
(TH[0], TH[1]]
(TH[1], inf]
mts_idx = 1
No signaling
mts_idx = [1,4]
TB signaling
mts_idx = [1,6]
TB signaling
TH[0] = 6, TH[1] =32

## Slide 5
Conclusion:
Variable number of non-DCT2 candidates (1, 4 or 6) based on lastScanPos value.
BDR-Y/Enc/Dec:
AI  (-0.10%/100%/99%)
RA  (-0.03%/95%/99%)
LDB  (-0.10%/101%/98%)
Thanks Alibaba for crosscheck!