## Slide 1: JVET-X0138
G. Martin-Cocher, K. Nasser, T. Poirier, S. Puri

## Slide 2: Defining a low latency & controlled complexity CTC
Motivation
  To align with operating points widely used in the industry for LLCC scenarios
  Examples:
  Being sufficiently different than LD-B to allow testing of tools in different conditions
Recommended NVENC settings for various use-cases | 
Use-case | Recommended settings for optimal quality and performance
Low-latency use cases like game-streaming, video conferencing etc. | Ultra-low latency or low latency Tuning Info Rate control mode = CBR Multi Pass – Quarter/Full (evaluate and decide) Very low VBV buffer size (e.g. single frame = bitrate/framerate) No B Frames Infinite GOP length Adaptive quantization (AQ) enabled** Long term reference pictures*** Intra refresh*** Non-reference P frames*** Force IDR***
[2] Nvidia nvenc-video-encoder-api-prog-guide
[3] Dissecting cloud game streaming platforms

## Slide 3: Defining a low latency & controlled complexity CTC
Agree to work on an LLCC configuration:
  as a modification to current ECM LDP + class F cfg, aiming to be quite different than LDB and replacing LDP in the long term.
  With GDR enabled by default (when implemented)
  Adopt some of the tools ON/OFF from the four tested options as a starting point.
Set-up an ad-hoc group to refine the LLCC configuration.
Mandate testing ECM LD-P for class F sequences for now?

## Slide 4: 4 tested configurations
Config | TEST | Class | BDR Y | BDR U | BDR V | Enc | Dec
LLCC option 1 (latency centric) | TEST 1: Sign-hiding ON IBC ON DQ, RDOQ, ALF OFF | Class F | 9.58% | 17.21% | 16.37% | 74.34% | 71.72%
 |  | Class TGM | 7.55% | 13.30% | 13.81% | 76.78% | 66.69%
LLCC option 2 (decoder complexity) | TEST 2: TEST 1 DIMD and DMVD, TIMD, IntraTMP OFF | Class F | 11.01% | 19.20% | 17.78% | 67.06% | 70.71%
 |  | Class TGM | 8.56% | 14.59% | 15.01% | 69.77% | 64.19%
LLCC option 3 (encoder complexity) | TEST 3: TEST 1 MTT=0, min QT size = 4 MTSImplicit ON MTS OFF | Class F | 33.67% | 51.37% | 51.02% | 30.28% | 76.77%
 |  | Class TGM | 31.73% | 43.77% | 44.30% | 41.43% | 80.47%
LLCC option 4 (trade-off performance) | TEST 4 TEST 2 MTSImplicit ON MTS OFF CIIP/ /ISP/PROF/SBT/SbTMVP/ OBMC OFF | Class F | 15.75% | 24.56% | 22.94% | 60.08% | 59.84%
 |  | Class TGM | 6.11% | 12.51% | 13.09% | 58.64% | 59.02%

## Slide 5: Tools consideration
Implementing GDR by default
  ECM results expected to be similar than in VTM for the same benefits
    Flat QP versus CTC (-9.97% Y, -18.78%U, -16.06% V)
    GDR versus IDR (-6.82% Y, -11.09% U,-11.18%V in class F)
  AU/DU both useful.
ALF / RDOQ
  A per CTU ALF implementation would be beneficial. ALF is OFF in all tests.
  RDOQ is turned off: other tools are often used.
Decoder complexity, option 2
  DIMD and DMVD, TIMD, IntraTMP are off
  Note: Control/Macro are currently not available in config files. This applies as well to LIC and OBMC.
Affine
  It is reported that AffineMVP has a low gain/complexity ratio. It is suggested to modify the current affine implementation to enable/disable AffineMVP independently from Affine in order to perform further tests.
Splitting
  Full MTT is unlikely in LLCC scenario.
  A configuration closer to HEVC: MTT and MTS Off, MTS implicit ON. Minimum QT size set to 4.
Per tool trade-off in LDP/class F

## Slide 6: Additional data

## Slide 7: ECM vs VTM vs HM – LDP – Class F
Class F | BDR Y | BDR U | BDR V | Enc | Dec
ECM-2.0-LDP-10_vs_VTM-11.0 | -13.75% | -20.53% | -20.53% | 1.80 | 2.10
ECM-2.0-LDP-10_vs_HM-16.22 | -48.06% | -52.84% | -52.99% | 13.11 | 2.87
ECM_test3-LDP-10_vs_HM-16.22 | -31.68% | -30.97% | -31.99% | 3.97 | 2.21

## Slide 8: ECM - On/Off tools
Tool OFF | BDRY | BDRU | BDRV | Enc | Dec
CIIP | 0.12% | 1.00% | 0.41% | 98% | 101%
ISP | 0.03% | -0.03% | -0.19% | 97% | 100%
PROF | 0.24% | 0.93% | 0.27% | 96% | 97%
SBT | 0.17% | 0.30% | 0.34% | 96% | 100%
SbTMVP | 0.28% | 0.68% | 0.68% | 97% | 96%
DIMD | 0.07% | 0.62% | 0.26% | 103% | 103%
DMVD | 0.61% | 0.32% | 0.32% | 93% | 98%
TIMD | 0.02% | -0.48% | -0.66% | 94% | 96%
Anchor: ECM 2.0, one intra period, Class F and TGM.

## Slide 9: GDR results
Anchor: VTM IDR every second, flat QP
Tested: GDR every second
  Different frame rate for Slide editing/slideshow

## Slide 10: Thanks!