## Slide 1: AHG12:EnHANCED SIGN PREDICTION
Xiaoyu Xiu, Yi-Wen Chen, Ning Yan, Che-Wei Kuo, Hong-Jheng Jhu, Wei Chen, Xianglin Wang

## Slide 2: Introduction
Sign prediction in ECM-2.0
  Estimating the signs of the coefficients in one transform block (TB) by minimizing the difference between its border samples and their spatial neighbors
  Only the signs of the TBs using only primary transforms can be predicted, i.e., the sign prediction is always disabled for the TBs with LFNST
  Up to 8 coefficients from the top-left 4X4 region of the TB are selected based on raster scan order
  Multiple pre-defined hypothesis templates are used to generate the reconstructed border samples to avoid doing inverse transforms

## Slide 3: Proposal
Two proposed enhancements
  Extending the sign prediction to LFNST TBs
    The signs of at maximum 4 coefficients in the top-left 4X4 region of the TB can be predicted
  Adaptive coefficient selection
    Select the coefficients for the sign prediction based on their impact on the reconstructed border samples
    The selection area is kept unchanged, i.e., top-left 4X4 region
represents the transform coefficient at coordinate in the TB
represents the template that corresponds to the transform coefficient

## Slide 4: Performance evaluation

## Slide 5: Summary
  Performance
  It is suggested to study the proposed modifications in the next EE.
 | Y | U | V | Enc | Dec
AI | -0.31% | -0.31% | -0.41% | 107% | 107%
RA | -0.23% | -0.22% | -0.11% | 101% | 102%
LDB | -0.16% | -0.17% | -0.27% | 100% | 101%
  Thanks to Tencent for the crosschecking!