## Slide 1: JVET-X0166 EE2-related: Combination of JVET-X0078 (Test 7/8), JVET-X0147 (Proposal-2), and GPM direct motion storage
Y. Kidani, H. Kato and K. Kawamura (KDDI)
H. Jang, S. Kim, J. Lim (LGE)
Z. Deng, K. Zhang, L. Zhang (Bytedance)

## Slide 2: Summary
Motivation
  Further coding gain compared to EE2-3.2 on GPM with intra and inter prediction (GPM-Intra/Inter)
Proposal
  Combination of GPM-Intra/Inter and GPM with MMVD and template matching (GPM-MMVD/TM)
  Restriction of GPM-Intra/Intra to the inter CU
  Adaptive intra prediction mode (IPM) derivation
  A direct motion vector (MV) and IPM storage on the GPM-blending area
Experimental results (tool-off)
  Test 7 (= 1+2+3)
  Test 8 (= 2+3)
  Test 10 (= 1+2+3+4)
  Test 11 (= 2+3+4)
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
EE2-3.2b | -0.02% | -0.22% | -0.10% | 101% | 100% | -0.08% | -0.54% | -0.40% | 101% | 100% | -0.45% | -1.16% | -1.18% | 105% | 100%
Test 7 | -0.13% | -0.39% | -0.30% | 102% | 100% | -0.24% | -0.77% | -0.87% | 102% | 100% | -0.77% | -2.14% | -1.79% | 121% | 101%
Test 8 | -0.09% | -0.30% | -0.20% | 101% | 101% | -0.24% | -0.60% | -0.58% | 102% | 100% | -0.66% | -1.71% | -1.55% | 106% | 100%
Test 10 | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
Test 11 | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD

## Slide 3: Proposal
Solution 1: Combination of GPM-Intra/Inter and GPM-MMVD/TM
  Note: GPM-Intra/Inter cannot be used together with GPM-MMVD/TM in EE2-3.3.
Solution 2: Restriction of GPM-Intra/Intra to the inter CU
  Avoidance of non-optimal IPM applied to GPM far from the reference
  Reduction of signalling for the pattern with low selectivity
Inter
Intra
Inter
(MMVD)
Intra
Inter
(TM)
Intra
Inter
Intra
Intra
Intra
Inter
Inter
×
Example of non-opt. IPM case in EE2-3.2

## Slide 4: Proposal (cont.)
Solution 3: Adaptive intra prediction mode (IPM) derivation
  Note: Neighbor IPM derived based on the table for GPM-TM
Solution 4: A direct MV & IPM storage on the GPM-blending area
IPM candidate
Para. angular
Perp. angular
Planar
0
1
2
IPM candidate
Para. angular
TIMD
DIMD
 Neighbor  Perp.  Planar
Intra
Inter
Parallel
Perpendicular
EE2-3.2: Pre-defined
Proposal: Adaptive
0
1
2
Angle | 0 | 2 | 3 | 4 | …
Part-0 | A | A | A | A | …
Part-1 | L+A | L+A | L+A | L | …
Part-0 (P0)
Part-1 (P1)
GPM-blending area
A
L
 | P0 | Blend. area | P1
EE2-3.3 | 1 (MVP0) | ~2 (MVP0, MVP1) | 1 (MVP1)
Proposal | 1 (MVP0) | 1 (MVP0 or MVP1) | 1 (MVP1)
 | P0 | Blend. area | P1
EE2-3.3 | IPMP0 | IPMMV | IPMMV
Proposal | IPMP0 | IPMP0 or IPMMV | IPMMV
GPM-Inter/Inter case
GPM-Intra/Inter case

## Slide 5: Supplemental results (tool-off)
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.02% | -0.28% | -0.06% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | 0.03% | -0.10% | 0.01% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
B | -0.01% | -0.26% | -0.22% | 101% | 100% | -0.13% | -0.39% | -0.34% | 100% | 100% | -0.38% | -1.30% | -1.08% | 105% | 100%
C | -0.06% | -0.20% | -0.07% | 101% | 100% | -0.25% | -0.72% | -0.50% | 100% | 99% | -0.67% | -1.53% | -1.45% | 106% | 99%
E |  |  |  |  |  | 0.26% | -0.53% | -0.37% | 102% | 101% | -0.29% | -0.42% | -1.00% | 106% | 101%
Overall | -0.02% | -0.22% | -0.10% | 101% | 100% | -0.08% | -0.54% | -0.40% | 101% | 100% | -0.45% | -1.16% | -1.18% | 105% | 100%
D | -0.02% | -0.06% | 0.15% | 101% | 100% | -0.01% | -0.51% | -0.37% | 101% | 100% | -0.23% | -1.18% | -2.01% | 105% | 101%
F | 0.03% | -0.05% | -0.08% | 100% | 99% | -0.19% | -0.22% | 0.08% | 100% | 100% | -0.34% | 0.11% | 0.23% | 103% | 100%
EE-2.3.2b

## Slide 6: Experimental results (tool-off)
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.12% | -0.35% | -0.29% | 102% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | -0.06% | -0.34% | -0.14% | 102% | 100% |  |  |  |  |  |  |  |  |  | 
B | -0.13% | -0.43% | -0.42% | 102% | 100% | -0.29% | -0.62% | -0.91% | 101% | 100% | -0.69% | -1.90% | -1.63% | 118% | 101%
C | -0.20% | -0.39% | -0.25% | 102% | 100% | -0.40% | -1.07% | -0.99% | 101% | 100% | -1.15% | -2.78% | -2.23% | 124% | 100%
E |  |  |  |  |  | 0.06% | -0.61% | -0.67% | 103% | 100% | -0.39% | -1.68% | -1.48% | 122% | 102%
Overall | -0.13% | -0.39% | -0.30% | 102% | 100% | -0.24% | -0.77% | -0.87% | 102% | 100% | -0.77% | -2.14% | -1.79% | 121% | 101%
D | -0.05% | -0.57% | -0.26% | 101% | 100% | -0.16% | -0.77% | -1.49% | 101% | 101% | -0.67% | -2.05% | -1.79% | 119% | 102%
F | -0.09% | -0.24% | -0.23% | 101% | 100% | -0.26% | -0.57% | 0.08% | 101% | 100% | -0.37% | -0.92% | -1.04% | 112% | 101%
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.10% | -0.15% | -0.24% | 101% | 101% |  |  |  |  |  |  |  |  |  | 
A2 | -0.02% | -0.22% | -0.06% | 101% | 100% |  |  |  |  |  |  |  |  |  | 
B | -0.09% | -0.33% | -0.26% | 101% | 101% | -0.29% | -0.41% | -0.65% | 101% | 100% | -0.60% | -1.54% | -1.64% | 105% | 100%
C | -0.14% | -0.42% | -0.20% | 101% | 101% | -0.39% | -1.00% | -0.68% | 102% | 100% | -0.99% | -2.17% | -1.71% | 106% | 100%
E |  |  |  |  |  | 0.05% | -0.38% | -0.35% | 102% | 101% | -0.32% | -1.38% | -1.20% | 108% | 101%
Overall | -0.09% | -0.30% | -0.20% | 101% | 101% | -0.24% | -0.60% | -0.58% | 102% | 100% | -0.66% | -1.71% | -1.55% | 106% | 100%
D | -0.03% | -0.18% | 0.07% | 101% | 100% | -0.01% | -0.20% | -1.01% | 101% | 101% | -0.46% | -1.34% | -1.90% | 106% | 101%
F | -0.05% | -0.08% | -0.01% | 100% | 100% | -0.41% | -0.39% | -0.69% | 100% | 100% | -0.59% | -1.24% | -0.96% | 103% | 100%
Test 8 (= Sol. 2 + Sol. 3)
Test 7 (= Sol. 1 + Sol. 2 + Sol. 3)

## Slide 7: Experimental results (tool-off) (cont.)
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | TBD | TBD | TBD | TBD | TBD |  |  |  |  |  |  |  |  |  | 
A2 | TBD | TBD | TBD | TBD | TBD |  |  |  |  |  |  |  |  |  | 
B | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
C | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
E |  |  |  |  |  | -0.15% | -0.89% | -1.32% | 102% | 101% | -0.39% | -1.14% | -1.02% | 122% | 101%
Overall | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
D | -0.17% | -0.47% | -0.14% | 102% | 100% | -0.31% | -1.42% | -0.87% | 102% | 100% | -0.59% | -1.82% | -1.93% | 119% | 102%
F | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | TBD | TBD | TBD | TBD | TBD |  |  |  |  |  |  |  |  |  | 
A2 | TBD | TBD | TBD | TBD | TBD |  |  |  |  |  |  |  |  |  | 
B | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
C | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
E |  |  |  |  |  | 0.08% | -0.67% | -0.68% | 102% | 100% | -0.42% | -1.39% | -1.08% | 109% | 101%
Overall | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
D | -0.13% | -0.36% | -0.23% | 101% | 100% | -0.25% | -0.80% | -0.56% | 100% | 100% | -0.55% | -1.31% | -1.25% | 105% | 101%
F | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
Test 8 (= Sol. 2 + Sol. 3 + Sol. 4)
Test 10 (= Sol. 1 + Sol. 2 + Sol. 3 + Sol. 4)

## Slide 8: Conclusion
Experimental results
  Test 7 (= 1+2+3)
  Test 8 (= 2+3)
  Test 10 (= 1+2+3+4)
  Test 11 (= 2+3+4)
Benefit
  Test 8/10: Coding gain in RA/LB/LP with minor run-time change
  Test 7/11: Further coding gain in RA/LP with another runtime change
It is recommended to adopt the proposal to ECM.
 |  |  | RA |  |  |  |  | LB |  |  |  |  | LP |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
EE2-3.2b | -0.02% | -0.22% | -0.10% | 101% | 100% | -0.08% | -0.54% | -0.40% | 101% | 100% | -0.45% | -1.16% | -1.18% | 105% | 100%
Test 7 | -0.13% | -0.39% | -0.30% | 102% | 100% | -0.24% | -0.77% | -0.87% | 102% | 100% | -0.77% | -2.14% | -1.79% | 121% | 101%
Test 8 | -0.09% | -0.30% | -0.20% | 101% | 101% | -0.24% | -0.60% | -0.58% | 102% | 100% | -0.66% | -1.71% | -1.55% | 106% | 100%
Test 10 | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD
Test 11 | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD