## Slide 1: Update on Ali266, the optimized VVC encoder implementation by Alibaba
X. Dong, S. Fang, Z. Huang, J. Liu, S. Xu, R. Yang, L. Yu, J. Chen, R.-L. Liao, Y. Ye
Alibaba
JVET-Y0066

## Slide 2: Ali266 review
Ali266, a software VVC encoder implementation developed by Alibaba
  first presented in JVET-W0127
  supporting two presets, with its fast preset aimed at real-time encoding applications
  achieving real-time encoding (37.7 fps) for 720p sequences in JVET-W0127
  further improvement that 8-bit real-time encoding (36.3 fps) of HD content was accomplished in JVET-X0104

## Slide 3: Main chenges since JVET-X0104
More fast encoding algorithms suitable for VVC encoder were employed.
More extensive SIMD instructions were used to reduce the required clock cycles, especially for the 10-bit internal bit depth.
Reduced memory consumption and improved memory access efficiency.
Better support of parallel encoding to reduce CPU idle time.
More predefined quality/speed presets to meet different application needs.

## Slide 4: Real-time encoding performance of Ali266
Class | RA |  |  |  |  |  |  |  | 
 | JVET-W0127 （Internal bit-depth = 8） |  |  | JVET-X0104 （Internal bit-depth = 8） |  |  | JVET-Y0066 （Internal bit-depth = 10） |  | 
 | YUV-PSNR | YUV-SSIM | Speed (fps) | YUV-PSNR | YUV-SSIM | Speed (fps) | YUV-PSNR | YUV-SSIM | Speed (fps)
1920x1080 | -34.99% | -39.59% | 19.99 | -40.58% | -43.00% | 39.13 | -43.90% | -44.84% | 34.30
1080x1920 | -36.58% | -37.06% | 18.61 | -36.86% | -40.69% | 33.46 | -40.52% | -42.39% | 30.62
1280x720 | -35.12% | -31.82% | 38.77 | -40.27% | -39.22% | 64.52 | -43.11% | -40.08% | 61.74
720x1280 | -34.73% | -40.04% | 36.66 | -34.68% | -41.50% | 62.23 | -40.52% | -44.30% | 58.01
Average | -35.35% | -37.13% | - | -38.10% | -41.10% | - | -42.01% | -42.90% | -
For Ali266 and x265, both of them performed 8-bit encoding in JVET-W0127 and JVET-X0104, but in JVET-Y0066, both of them performed 10-bit encoding.
Weights of Y, U, V are 6:1:1

## Slide 5: Ali266’s Quality/Speed Presets in comparison with x265

## Slide 6: Summary
Ali266 is a highly optimized VVC encoder implementation
  With Ali266’s faster preset, more than 42% of bitrate savings in terms of both YUV-PSNR and YUV-SSIM are achieved over x265 at the medium preset.
  with the average 10-bit encoding speed of 1080p sequences achieving 32.46 fps, we claim that 10-bit real-time encoding of HD content is accomplished.
  In addition to long-term efforts to improve encoding speed and performance, we are also committed to applying Ali266 to Alibaba’s various video businesses, starting with our collaborative effort with the Youku team as reported in JVET-Y0122.