## Slide 1: JVET-Y0091 Non-EE2: MVP refinement for regular AMVP mode

## Slide 2: Introduction
Derivation of MVP
In ECM regular AMVP mode,
An MVP candidate from AMVP list is determined based on template matching cost.
TM is performed only for this MVP candidate.

## Slide 3: Proposed Method
An MVP is derived as the following steps:
Select two candidates with two smallest template matching cost from AMVP list.
Extend the two candidates by a search pattern where the search positions are indicated by MMVD and derive TM costs for these extended MVPs.
Operate TM for the MVP with the minimum TM cost in the same manner in ECM.
Fig. 1

## Slide 4: Proposed Method
Notes: The search pattern is illustrated in Fig. 1, where 8 directions and 9 positions along each direction are defined in Table 1.

## Slide 5
Only if the motion vector resolution of current CU is 1/4-pel or 1-pel, the proposed method is applied.
In step 2,
Set each of the two selected candidates (candMv0 and candMv1) as starting point respectively, and operate template-based searching at the search positions indicated by Distance = {1, 2, 4, 8} along 8 directions to derive the corresponding TM costs for each search position.
If thus far the minimum TM cost for the searched positions is larger than either of the TM costs of candMv0 or candMv1, the template-based searching process for the remaining Distance = {12, 16, 24, 32, 64} along 8 directions is terminated. Otherwise, if the searched position with the minimum TM cost is starting with candMv0 (or candMv1) as the center, then only the remaining search positions around candMv0 (or candMv1) are searched.
Simplified Method

## Slide 6
Results
Under CTC
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.23% | -0.06% |  | 
Class C | -0.11% | -0.11% | -0.16% | 108% | 103%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.09% | -0.09% | -0.08% | 108% | 103%
Class F | -0.06% | -0.01% | -0.15% | 103% | 100%
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.14% | -0.07% |  | 
Class C | -0.10% | -0.12% | -0.13% | 107% | 103%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.08% | -0.20% | -0.06% | 107% | 103%
Class F | -0.07% | -0.09% | -0.16% | 103% | 100%
Test3: If NoBackwardPredFlag equals to 1, Test 2 is applied
Test2: Simplified method
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.12% | -0.18% | -0.20% | 111% | 103%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.07% | 0.06% | -0.17% | 110% | 104%
Class F | -0.09% | -0.21% | -0.15% | 105% | 100%
Test 1
Test 2
Test 3

## Slide 7
Results
The test result of ParkRuning3 for QP 22 is copied from anchor.
Except class C and D, timings of the remaining classes are not accurate.
Non-CTC results of Test2
1. Not using per-class configuration provided in the cfg/per-class folder for random access condition.
2. The test duration is 10 seconds for low delay condition.
 | RA |  |  |  |  | LD |  |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | 
Class A1 | -0.15% | -0.30% | -0.40% | xx | x x |  |  |  |  |  | 
Class A2 | -0.13% | -0.19% | -0.24% |  |  |  |  |  |  |  | 
Class B | -0.09% | -0.21% | -0.24% | x x | xx |  |  |  |  |  | 
Class C | -0.11% | -0.21% | -0.19% | 107% | 102% | -0.20% | -0.19% | -0.42% | 124% | 103% | 
Class E |  |  |  |  |  | -0.27% | -0.07% | -0.15% | xx | xx | 
Overall | -0.12% | -0.22% | -0.26% | xx | xx |  |  |  |  |  | 
Class D | -0.09% | -0.04% | -0.01% | 107% | 101% | -0.12% | -0.16% | 0.16% | 124% | 103% | 
Class F | -0.06% | -0.01% | -0.15% | 103% | 100% |  |  |  |  |  | 
 | RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.23% | -0.06% |  | 
Class C | -0.11% | -0.11% | -0.16% | 108% | 103%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.09% | -0.09% | -0.08% | 108% | 103%
Class F | -0.06% | -0.01% | -0.15% | 103% | 100%

## Slide 8
Conclusion
This contribution proposes an MVP refinement scheme for regular AMVP mode.
Simulation results of non-ctc show about 0.12% coding gain in RA configuration.
It is recommended to study in EE2.
Thanks Alibaba for cross-checking!

## Slide 9
THANK
YOU