## Slide 1
JVET-Y0105: AHG10: An improved VVC rate control scheme
Guangjie Ren, Jianghao Jia, Jiwei Wang, Zhenzhong Chen (Wuhan University)
Zizheng Liu (Tencent)

## Slide 2
Introduction
Proposed a combined method composed by three parts including CTU-level bit allocation for skip and non-skip CTU, adaptive smooth window size setting based on the GOP size and Intra Period, and extension of the quality dependency factor (QDF) to low frame rate based on JVET-M0600/T0062.
Compared with the current rate control algorithm in VTM 14.0, the proposed method has -0.65%/-0.65%/-0.51%, -1.38%/-1.59%/-1.63% for Y/U/V coding efficiency improvements in low delay B, and random access (GOP Size=32) configuration.

## Slide 3
Proposed Method -- CTU-level bit allocation
In VTM 14.0, the initial bit weight for each CTU is determined by frame-level and content related parameters and :
Current
Proposed
The bit allocation of skip CTU and non-skip CTU are carried out separately.
Skip CTU:
0.4
number of pixels of skip CTU
Notes: The first is about CTU bit allocation.
In the current CTU-level bit allocation, the initial bit weight for each CTU is determined by frame-level 𝜆 and content related parameters 𝛼 and 𝛽, like this formula. The equation is based on R-D model. But, it is not suitable for skip CTUs.
So, in this contribution, the bit allocation of skip CTU and non-skip CTU are carried out separately. First, the bits of skip CTU is calculated by bpp, number of pixels of skip CTU, and a scale parameter which is set as 0.4 according to our experiments.

## Slide 4
Proposed Method -- CTU bit allocation
Non-Skip CTU:
The bit allocation problem of non-skip CTUs can be described as:
which can be converted by introducing a Lagrange multiplier:
solved by Newton method
Notes: The bit allocation of non-skip CTUs needs to solve the constrained optimization problem. And it can be converted by introducing a Lagrange multiplier. The 𝜆_(𝑛𝑜𝑛−𝑠𝑘𝑖𝑝) will be solved by Newton method to achieve optimal solution.

## Slide 5
Proposed Method -- CTU bit allocation
Non-Skip CTU:
The optimal bit allocation for non-skip CTUs is:
Current
Proposed
Notes: When Newton method is used, we set the max iteration as 20, and the early terminal condition is to make sure the absolute value of 𝜆 difference between iterations less than 0.001. And finally, we can get the bits and weight for non-skip CTUs.

## Slide 6
Proposed Method -- smooth window size
The variable SW is the size of a smooth window used to make the bit rate change smoother. SW will influence the GOP-level and frame-level target bits:
Due to the influence of the Intra frame bits, is usually calculated as a negative value, causing GOP-level target bits to be clipped to 200.
Notes: The second part is an adaptive smooth window size setting.
SW is the size of a smooth window used to make the bit rate change smoother. And SW will influence the GOP-level and frame-level target bits.
However, due to the influence of the Intra frame bits, 𝑇_𝑃𝑖𝑐𝐴𝑣𝑔 is usually calculated as a negative value, causing GOP-level target bits to be clipped to 200.

## Slide 7
Proposed Method -- smooth window size
Current
Proposed
LD: GOP Size = 4
RA: GOP Size = 8
SW Size = 40
HM
LD: GOP Size = 8
RA: GOP Size = 32
SW Size = 40
VTM
Use GOP size and IntraPeriod (IP) to set the smooth window size:
20
60

## Slide 8
Proposed Method -- extension of QDF
Current
The condition is changed to extend the QDF to low frame rate sequences:
m_encRCSeq->getAdaptiveBits() > 0 &&
m_listRCPictures.size() >= m_encRCSeq->getGOPSize()
Proposed
In VTM14.0, the judgment condition for using the QDF based rate control is:
if (encRCSeq->getAdaptiveBits() > 0 && encRCSeq->getLastLambda() > 0.1)
never > 0.1 when GOP Size = IntraPeriod
default value is 2
[1] Z. Liu, Z. Chen, Y. Li, Y. Wu, S. Liu, “AHG10: Quality dependency factor-based rate control for VVC”, JVET-M0600, Jan. 2019.
[2] F. Liu, Z. Liu, Z. Chen, Y. Li, Z. Chen, “AHG10: Extension of rate control to support random access configuration with GOP size of 32”JVET-T0062, October. 2020.

## Slide 9
Simulation Results -- Proposed vs. RC
 | Over VTM-14.0 with Rate Control |  |  |  |  |  |  |  |  |  |  | 
 | Random access Main10 (GOP size = 32) |  |  |  | Low delay B Main10 |  |  |  | Random access Main10 (GOP size = 16) |  |  | 
 | Y | U | V | Bitrate error | Y | U | V | Bitrate error | Y | U | V | Bitrate error
Class A1 | -3.81% | -2.86% | -3.89% | 0.12% |  |  |  |  |  |  |  | 
Class A2 | -1.07% | -2.52% | -2.19% | 0.03% |  |  |  |  |  |  |  | 
Class B | -1.02% | -1.45% | -1.22% | 0.07% | -0.29% | -0.56% | -0.45% | 0.00% | -0.52% | -1.36% | -1.25% | 0.10%
Class C | -0.23% | -0.13% | -0.03% | 0.10% | -0.25% | -0.35% | -0.43% | 0.00% | 0.16% | -0.25% | -0.02% | 0.07%
Class E |  |  |  |  | -1.78% | -1.21% | -0.73% | 0.01% |  |  |  | 
Overall | -1.38% | -1.59% | -1.63% | 0.08% | -0.65% | -0.65% | -0.51% | 0.00% |  |  |  | 
Class D | -0.29% | -0.05% | -0.33% | 0.22% | -0.38% | -0.03% | -0.08% | 0.01% | -0.17% | 0.34% | 0.46% | 0.06%
Class F | 0.79% | -1.74% | -2.09% | 1.14% | -2.44% | -1.33% | -2.33% | 1.90% | -0.57% | -0.23% | -0.02% | 0.74%

## Slide 10
Simulation Results -- Proposed vs. RC

## Slide 11
Simulation Results -- Proposed vs. RC
 | Random access Main10 (GOP size = 32) |  | 
 | Over VTM-14.0 with Rate Control |  | 
 | Y | U | V
Campfire (Class A1) | -8.05% | -4.24% | -7.53%
The result of our proposed method on Campfire sequence in Class A1 (4K) with random access (GOP size=32) configuration:

## Slide 12
THANKS!
Notes: 𝑇ℎ𝑎𝑛𝑘𝑠 𝐵𝑦𝑡𝑒𝐷𝑎𝑛𝑐𝑒 𝑓𝑜𝑟 𝑐𝑟𝑜𝑠𝑠𝑐ℎ𝑒𝑐𝑘. Any comments ……