## Slide 1: JVET-Y0133 EE2-related: BVP candidate adjustment based on IBC reference region implemented on top of test EE2-3.13
Damian Ruiz Coll, Alexey Filippov,
Vasily Rufitskiy, Tae Meon Bae

## Slide 2: BVP candidates clipping
  Some of the BVP candidates belonging to the neighbor blocks could be pointed out of the IBC reference region, becoming invalids and consequently being dropped from the IBC Merge/AMVP list.
    Method:
    Simple clipping of the BVP candidates to adjust the BVP to the nearest border of the IBC reference region
    Clipping is applied to candidates before being tested for validity, in the IBC Merge/AMVP list construction
    Become an invalid BVP candidate in a valid predictor, similar to the MVP clipping to the picture boundaries for the Inter prediction

## Slide 3: Zero-padding vector replacement
  When the IBC Merge/AMVP list is not complete, the list is padded with one or more zero vectors until the maximum number of candidates is encountered, which are invalid in IBC mode.
  At the beginning of a picture encoding the IBC list has only one invalid candidate BVP(0,0)
    Method:
    At the end of the list construction, the padding is modified to include a full set of valid VBP candidates
    Padding with 3 candidates located on the nearest corners of the reference region to the current block.
    Padding with 3 candidates are in the middle of the three sub-regions (A, B, and C)

## Slide 4: Results
On top of ECM-3.1 and combined with EE2-3.13:
Table 1. TEST.1: Candidate BVP clipping
Table 2. TEST.2: IBC Merge/AMVP list padding

## Slide 5: Results
On top of ECM-3.1 and combined with EE2-3.13
Table 3. TEST.3: Combined clipping and paddling techniques

## Slide 6: Conclusion
Simple BVP candidates clipping to the IBC reference region boundaries, no additional memory or complex processing required.
Simple replacement of the zero-padding vector for a valid candidate.
Reports some gain in AI and RA (combined with EE2 3.13):
Could provide some gain pooled with other IBC tools (JVET-Y0088, JVET-Y0160, JVET-Y0124)
Recommend studying both techniques in EE2
AI: Class F -0.54% Class TGM -1.21% | RA: Class F -0.38% Class TGM -1.08%