## Slide 1: JVET-Z0067
Non-EE2: RPR bug fixes and new results of RPR with luma-only re-scaling
P.Bordes, F. Galpin, H.Guermoud, E.Francois

## Slide 2: RPR bug fixes (ECM-4.0) (MR105)
JVET_Y0065_GPM_INTRA: modification of spanGeoMotionInfo() for re-scaled pictures:
  In case of GPM-intra/inter, at the intra mode propagation stage for inter sub-partitions, the location of the intra mode stored into the IPM reference buffer is re-scaled using the scaling ratio of the current picture, as done for other inter modes (see spanIpmInfoInter() function).
JVET_Y0067_ENHANCED_MMVD_MVD_SIGN_PRED: modification of sortInterMergeMMVDCandidates() and sortAffineMergeCandidates() for re-scaled pictures:
  The estimation of the candidate costs for Inter Merge MMVD, Affine Merge and MVD/SMVD sign is by-passed (use default max cost) if the current picture is re-scaled.

## Slide 3: Proposal: luma-only RPR
RPR may have BD-rate gains in luma but loss in chroma
  RPR performs an additional down-scaling filtering on samples that were already filtered from the original canonical 4:4:4 content to create the 4:2:0 format.
Proposal: Luma-only RPR
  increase the flexibility of RPR by allowing down-scaling luma only
  the codec may switch dynamically resolution and/or chroma format which is signaled in PPS
  still benefit from the CC tools (intra prediction, CC-SAO, CC-ALF)
  RPR luma-only feature is limited to down-scaling by 2 both horizontally and vertically, so that the chroma format of the reconstructed pictures may be 4:2:0 (no-RPR or regular RPR) or 4:4:4 (luma-only RPR)
Previous meeting: super-resolution only [Y0095]
  Y0095 didn’t test dynamic RPR.

## Slide 4: Test: dynamic re-scaling
RPR common test conditions for VVC [JVET-Q2015]
  LDB scenarios with 0.5 sec.
  resolution switching interval
  RPR 2x.
Tests - Luma-only RPR
  luma-only RPR without any constraint on CU size
  luma-only RPR with number of color samples of CU constrained to be less or equal to the maximum number of color samples of one CU in 4:2:0 format
  QP chroma offset is used to balance the quality between luma and chroma components to align with regular RPR

## Slide 5: Results: luma-only RPR (PSNR2)
Thank you Qualcomm for cross-checking

## Slide 6: Examples
D_RaceHorses (qp=32)
Original
Regular RPR
Luma-only RPR

## Slide 7: Examples
BQTerrace (qp=37)
Original
Regular RPR
Luma-only RPR

## Slide 8: Examples
C_PartyScene (qp=37)
Original
Regular RPR
Luma-only RPR

## Slide 9: Examples
F_SlideEditing (qp=37)
Original
Regular RPR
Luma-only RPR

## Slide 10: Proposal
Adopt RPR bug fixes (MR105)
Study luma-only RPR in EE