## Slide 1: JVET-Z0115
AHG13: proposed film grain synthesis reference model

## Slide 2: Why ?
Considering mandatory film grain synthesis and soft-conformance
  Need a reference model
RDD5-based implementations as in VTM have complexity issues
Some hardware vendors already have an implementation to comply with AOM specs (e.g. AV1)
  Less costly (no line buffers, single pattern)
  We understand the benefit of leveraging it as much as possible
  But it is lacking features (e.g. locally adaptive grain shape)
 Proposing a feature-complete model, widely compatible, and paying attention to hardware complexity

## Slide 3: Film grain use cases
Artistic intent
Artifact hiding

## Slide 4: Use case #1: artistic intent
Studios add grain for various reasons (historic setting, camera match, purely subjective)
Video coders, especially VTM are outstandingly efficient at removing it.
Coding grain would require unrealistic bitrates
 We need the decoder to recreate it

## Slide 5: Use case #1: artistic intent (example)
original
decoded
+ synthetic grain

## Slide 6: Use case #2: artifact hiding
Grain/noise is good at hiding defects (e.g. in flat areas) + can give a textured feeling to compensate a lack of detail.
We have an example of spec (AV1) where film grain processing can be mandatory, with that being well received by the market
 We need the decoder to create it

## Slide 7: Use case #2: artifact hiding (example)
original
decoded
+ synthetic grain

## Slide 8: Proposed implementation
Architecture overview
RDD5/AOM differences
Supporting SEI.FF, SEI.AR, AOM parameters
Strong randomization, but no modulo
Multiple patterns
No line buffer at all

## Slide 9: Architecture overview
Get a set of film grain patterns
Generate random block offset
Select pattern
Apply scaling factor
Deblock
Split image into blocks
Blend with target picture
cfg
Offline / firmware
Randomization
Content-adpatation
64x64
Need deblock
May need deblock
May need deblock

## Slide 10: Feature comparison
Feature | SEI / RDD5 | AOM
Master pattern generation (init, firmware) | Frequency-based (gaussian, inverse DCT), or AR (6 symmetric coefficients, half-diamond shape) | AR (up to 25 coefficients, rectangle-shaped)
Master patterns (on-chip memory) | 64x64, up to 10 (shared by luma & chroma) | 64x64 luma + 2x 32x32 chroma (4:2:0 mode) or 64x64 (4:4:4 mode)
Pattern selection | Intensity-based (8x8 block average). Per-color. | Fixed: per color plane
Pseudo-noise generator | 31-bit (32-bit register) | 16-bit
Randomization | Pseudo-random x/y offset within pattern, every 16x16 block + flip sign | Pseudo-random x/y offset within pattern, every 32x32 block (or 16x16 for chroma)
Scaling | Intensity-based (8x8 block average), stepwise function. Per-color. | Luma or color-mix based, (pixel-based), piecewise-linear function.
Deblocking | 8x8, mix of pre-computed attenuation (horizontal edges) and live filtering (vertical edges, ¼ ½ ¼) | 2-pixel overlap (right & bottom) = live filtering, per 32x32 block. Non-trivial coefficients (17/27 or 22/23)
Clipping | Fixed (full range) | Flexible (full/legal)

## Slide 11: SEI.FF, SEI.AR or AOM paramters
Non-issue as pattern generation can be done in firmware
  Also: converting frequency-based to AR is possible
Non-issue for scaling function too (converted to LUT)
  Also: converting step-wise to piecewise-linear is possible
Output of configuration decoding/pattern generation stage:
  A set of 8 64x64 patterns for luma, and a set of 8 patterns for chroma (32x32 in 4:2:0 mode)
  Scaling LUTs (one per color component)
  Pattern selection LUTs (one per color component)
 Focus effort on low-level (hardware)

## Slide 12: Randomization comparison
RDD5
AOM
Test above on 640x480 picture. Visible repetitions in AOM.
Worse in color: chroma synchronized in AOM, independent in RDD5
Not improved in video mode (vs still), maybe even worse
same pattern

## Slide 13: Proposed randomization
16x16 blocks (32x32 is too large)
32-bit random generator (RDD5: a single XOR)
Modulo too complex  use another trick
  Multiply (simple factor) + mask
Random flip sign as in RDD5
Offset alignment (4-pixel): lower timing constraints for pattern memory + scrambles more

## Slide 14: Actual film: grain size vs exposure
original
denoised
diff
FFT cloud
Kodak Vision 250D, 1 pixel = 17um (color film; just showing luma here)
Both grain amplitude and size/sharpness depend on exposure
 Need multiple patterns within a picture

## Slide 15: Actual film: grain size vs exposure #2
4000 dpi scanner output
1 pix = 6.4 μm
Fuji S400 film (still picture)
Raw negative
150x microscope view
1 pix = 0.6 μm
Raw negative
500x microscope view
1 pix = 0.16 μm
1mm
100 μm
10 μm

## Slide 16: Proposed multi-pattern design
Pixel-wise  no line buffer
Patterns have to be correlated at generation time (same seed, or incremental layers, etc)
  Easy for both frequency-based and AR
Adapt pattern number to what device supports :
  Just signal them by order of importance
  We recommend 8 patterns for luma + 8 for chroma.
  Could reduce to 4 + interpolation

## Slide 17: Scaling & deblock: no line buffers
Scaling also pixel-wise (no issue, actually better than block-wise)
Horizontal deblock: filter
  Overlap could be more complex here
Vertical deblock: overlap
  Need 2x random gen (save upper line seed) + dual read access memory (blend two random offsets from the same pattern)
  Could simplify coefficients (currently 17/27 & 22/23 as in AOM)