## Slide 1
JVET-Z0137: Non-EE2: Adaptive Blending for GPM
Han Gao, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Che-Wei Kuo, Ning Yan, Xianglin Wang

## Slide 2: Introduction
Blending area width is fixed as
Weighting depends on distance
Fixed blending isn’t optimal to fix all contents

## Slide 3: Proposed method
Blending area width is adaptively selected at CU-level as
The blending strength index is signaled into the bitstream
Shiftable value based make sure that current equation is reusable

## Slide 4: Experimental results
Experimental results shows
  0.14%/0.17% RA/LDB gain for nature content
  1.90%/2.61% RA/LDB gain for TGM
Proposed to be included in the next EE
 | Random Access Main 10 |  |  |  | 
 | Over ECM3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.58% | -0.14% | 102% | 99%
Class A2 | 0.02% | -0.03% | 0.02% | 98% | 100%
Class B | -0.13% | -0.23% | -0.16% | 103% | 100%
Class C | -0.28% | -0.18% | -0.14% | 101% | 103%
Class E |  |  |  |  | 
Overall | -0.14% | -0.25% | -0.12% | 101% | 100%
Class D | -0.18% | -0.28% | 0.05% | 100% | 102%
Class F | -0.62% | -0.68% | -0.57% | 105% | 98%
Class TGM | -1.90% | -1.30% | -1.26% | 101% | 98%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.10% | 0.04% | 0.09% | 103% | 101%
Class C | -0.31% | -0.05% | -0.54% | 105% | 102%
Class E | -0.08% | -0.18% | 0.66% | 99% | 98%
Overall | -0.17% | -0.04% | 0.02% | 102% | 100%
Class D | -0.30% | 0.05% | -0.12% | 102% | 102%
Class F | -0.69% | 0.09% | -0.88% | 102% | 99%
Class TGM | -2.61% | -2.11% | -2.12% | 102% | 98%
Thanks KDDI for the crosschecking!

## Slide 5: Experimental results
Experimental results shows
  One PPS flag is used to completely disable the blending process (which is equivalent to set to 0) for the GPM
Thanks KDDI for the crosschecking!

## Slide 6: Thank you!