## Slide 1
JVET-Z0219:
Non-EE2: SPS flag to control
TM-based merge/amvp and multi-pass DMVR separately.
Hyeongmun Jang (hm.jang@lge.com)
LG Electronics Inc.

## Slide 2
Summary
In order to support “pure” TM-off functionality in ECM-4.0,
Suggest to add one SPS to control TM MRG/AMVP separately with multi-pass DMVR
Suggest low-level modification to enable bm merge when the TM MRG is disabled by the SPS flag.

## Slide 3
Background
In ECM-4.0, DMVD flag in SPS controls TM based merge/amvp and multi-pass DMVR together.
Hence, disabling “pure” TM based coding tool is impossible while multi-pass DMVR is enabled.
For the investigation of future coding tools,
  It is also important that investigate compression benefits without template matching.
  Some specific applications might demand disabling the template matching for the purpose of low delay and low latency.

## Slide 4
Proposed aspect 1 (SPS flag)
Add one SPS flag to separately control TM MRG/AMVP and multi-pass DMVR.
The proposed SPS flag control TM MRG/AMVP
Conventional DMVD SPS flag control multi-pass DMVR.

## Slide 5
Proposed aspect 2
Low-level modification is required in order to avoid disabling bm-merge when tm-merge is disabled in SPS
bm_merge_flag only can be signalled when tm_merge_flag is equal to 1. even though tm-merge and bm-merge is mutually exclusive.
The problem is bm_merge_flag can not be parsed and forcefully disabled when TM is disabled by SPS flag.

## Slide 6
Proposed aspect 2(method 1)
Method 1 modifies bm_merge_flag parsing condition
bm_merge_flag is parsed when tm_merge_flag is equal to 0. because this coding tools are mutually exculive.

## Slide 7
Proposed aspect 2(method 2 : without bitstream change)
To avoid bitstream change by low-level modification, alternative implementation is applied in method 2.

## Slide 8
Simulation results with CTC
ind
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 CTC |  |  |  |  | Over ECM-4.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class B | 0.02% | 0.03% | 0.02% | 100% | 99% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.03% | 0.16% | 0.12% | 101% | 101% | 0.00% | 0.00% | 0.00% | 99% | 97%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 98% | 97%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.00% | -0.11% | 0.02% | 101% | 101% | 0.00% | 0.00% | 0.00% | 102% | 101%
Class F | 0.00% | 0.01% | 0.04% | 100% | 100% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
The proposed method 1 changes bitstream by low-level modification while the proposed method 2 does not.
Therefore, the results of proposed method with CTC configuration is reported.
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 CTC |  |  |  |  | Over ECM-4.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Simulation result : SPS flag + low-level change method 1
Simulation result : SPS flag + low-level change method 2

## Slide 9
Simulation results with non-CTC(TM-off configuration)
ind
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 CTC |  |  |  |  | Over ECM-4.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class B | 2.39% | 2.54% | 2.44% | 90% | 84% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 2.54% | 2.57% | 2.77% | 89% | 78% | 2.62% | 2.33% | 2.33% | 83% | 72%
Class E |  |  |  |  |  | 2.39% | 1.74% | 1.46% | 88% | 85%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 2.34% | 2.22% | 2.38% | 89% | 78% | 2.70% | 2.42% | 2.88% | 83% | 70%
Class F | 1.48% | 1.47% | 1.47% | 94% | 88% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Describe test condition to know current performance without “pure” tm processing
DMVD : 1
AML : 0
MVSD : 0
MMVD : 0
AffineMMVD : 0
TM : 0 # proposed SPS flag, if this value is equal to 0, tm based merge/amvp is disabled.
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 CTC |  |  |  |  | Over ECM-4.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  |  |  |  | 
Class B | 2.36% | 2.59% | 2.44% | 90% | 84% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 2.49% | 2.61% | 2.77% | 89% | 78% | 2.62% | 2.33% | 2.33% | 83% | 71%
Class E |  |  |  |  |  | 2.39% | 1.74% | 1.46% | 88% | 84%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 2.34% | 2.32% | 2.53% | 88% | 77% | 2.70% | 2.42% | 2.88% | 83% | 70%
Class F | 1.45% | 1.41% | 1.45% | 93% | 87% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Simulation result : SPS flag + low-level change method 1
Simulation result : SPS flag + low-level change method 2

## Slide 10
Conclusion
ind
It is recommend to consider to provide TM off functionality in ECM