## Slide 1: JVET-AA0099 AHG9: On subpictures order
Hendry, Seung Hwan Kim, and Sangheon Lee
LG Electronics.

## Slide 2: Overview
In the current VVC spec, availability rule applies to subpicture and its order in the bitstream ensure that they can be decoded properly
“It is a requirement of bitstream conformance that the shapes of the subpictures shall be such that each subpicture, when decoded, shall have its entire left boundary and entire top boundary consisting of picture boundaries or consisting of boundaries of previously decoded subpictures.”
In addition to the availability rule, the following constraint also applies to subpicture order:

## Slide 3: Problem description (1)
Even with the existing constraints, the order of subpicture can be not in raster scan order even in a regular shaped subpicture structure.
  It depends how the structure is signalled in SPS
Examples of possibilities:
  Raster-scan order (Structure on the right top)
  Non raster-scan order. (Structure on the right bottom)
Dealing with non-raster scan ordered subpicture requires additional complexity in the implementation
  Particularly when loop filters across subpicture is allowed

## Slide 4: Problem description (2)
Decoder stores column buffer. After decoding SP 1, column buffer is updated with the reconstructed pels of the right most column.
This column buffer is updated after completion of SP 2, then SP 3, and so forth.
For decoding SP 5, particularly block E, block A is needed. For that, a simple method can be used by moving the data from line buffer to column buffer. Same goes to handle block F and so forth.
This works because we know exactly the order of the subpictures. What will come next after the current subpicture.

## Slide 5: Problem description (3)
Based on the current spec, different bitstream my have different order of subpicture, depending on how it is signalled.
The simple method for the implementation cannot be used anymore.
Moving / copying data from line buffer to column buffer cannot be done since we don’t know which subpicture will come next.

## Slide 6: Observation
Allowing non-raster scan order of subpicture is needed since subpicture structure can be irregular.
Current use-case scenarios where subpicture is needed only need regular shaped subpictures (e.g., use-cases in 3600 videos, teleconferencing, etc)

## Slide 7: Proposal (1)
Considering that handling non-raster scan subpicture order requires additional complexity in the implementation, non-raster scan subpicture order should be allowed in the case when raster scan order is not possible.
To do that, we suggest two options:
  Add a constraint
  Add a GCI flag

## Slide 8: Proposal: Option 1

## Slide 9: Proposal: Option 2
Certain application use, this flag can be required to be a certain value so that implementation can be certain. For example, for application that handles 3600 with subpictures for cubemap projection, this flag can be required to be equal to 1 so that the current implementation can be used without worries