## Slide 1: JVET-A0102 AHG9: SEI processing order SEI message
P. Yin, S. McCarthy, W. Husak, K. Konstantinos, T. Lu, F. Pu, A. Arora, T. Shao (Dolby)
Joint Video Experts Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29
27th Meeting, by teleconference, 13–22 July 2022

## Slide 2: Summary
Proposal: SEI message for carrying information on the preferred order of processing SEI messages. Proposed for next version of VVC.
Introduction: An encoder (i.e., content producer) could use an SEI manifest SEI message to indicate the following:
that some SEI messages are likely to be present in the CVS, and
that their interpretation is “necessary” to enable an adequate user experience
Problem statement:
the order of processing “necessary” SEI messages may also be “necessary” to enable an adequate user experience (e.g., neural-network post-filtering, colour transform, film grain synthesis)
The SEI manifest SEI messages cannot carry information on the preferred order of processing SEI messages
A similar proposal for order of applying neural-network post-filters indicated by the neural-network post-filter activation SEI message is presented in JVET-AA0101

## Slide 3: Example when the order of processing could affect user experience
YUV0
Film grain synthesis
NNPF
(resizing)
YUV2
YUV1
A
NNPF
SEI messages
FGC
SEI message
Film grain synthesis precedes resizing in processing order
Resizing precedes film grain synthesis in processing order
YUV0
NNPF
(resizing)
Film grain synthesis
YUV4
YUV3
B
FGC
SEI message
NNPF
SEI messages

## Slide 4: Proposed SEI processing order SEI message syntax

## Slide 5: Proposed SEI processing order SEI message semantics
SEI message processing order SEI message semantics
[Introduction is adapted from SEI manifest SEI message semantics]
po_num_sei_msg_types specifies the number of types of SEI messages for which information is provided in the SEI processing order SEI message.
po_sei_payload_type[ i ] specifies the value of payloadType for the i-th SEI message for which information is provided in the SEI processing order SEI message. The values of po_sei_payload_type[ m ] and po_sei_payload_type[ n ] shall not be identical when m is not equal to n.
po_sei_processing_order[ i ] indicates the preferred order of processing any SEI message with payloadType equal to po_sei_payload_type[ i ]. po_sei_processing_order[ m] greater than 0 and less than po_sei_processing_order[ n ] indicates any SEI message with payloadType equal to po_sei_payload_type[ m ], when present, should be processed before any SEI message with payloadType equal to po_sei_payload_type[ n ], when present. po_sei_processing_order[ i ] equal to 0 specifies that the preferred order of processing SEI messages with payloadType equal to po_sei_payload_type[ i ] is unknown or unspecified or determined by external means not specified in this Specification.

## Slide 6: VVC related aspects
In Annex D.8.2 SEI manifest SEI message semantic, the modify the following paragraph as highlighted in yellow:
An SEI NAL unit containing an SEI manifest SEI message shall not contain any other SEI messages other than SEI prefix indication SEI messages and an SEI processing order SEI message. When present in an SEI NAL unit, the SEI manifest SEI message shall be the first SEI message in the SEI NAL unit.
In Annex D.9.2 SEI prefix indication SEI message semantic, the modify the following paragraph as highlighted in yellow:
An SEI NAL unit containing an SEI prefix indication SEI message for a particular value of payloadType shall not contain any other SEI messages other than an SEI manifest SEI message, an SEI processing order SEI message, and SEI prefix indication SEI messages for other values of payloadType.
Proposed modifications of SEI manifest and SEI prefix indication SEI message semantics