## Slide 1
JVET-AB0084
EE1-2.3：A CNN-based Super Resolution Method with GOP Level Adaptive Resolution
Renjie Chang, Liqiang Wang, Xiaozhong Xu, Shan Liu (Tencent)
Junghak Nam, Sunmi Yoo, Jaehyun Lim, Seung Hwan Kim (LGE)

## Slide 2
This proposal reports the EE1-2.3 test results, which is a combination of JVET-AA0084 and JVET-Y0068
adaptively select a scale factor from ×1.0 and ×2.0 at the GOP level and designed CNN-based super-resolution will be used for the latter case.
experimental results show {-3.63%, -2.40%, -2.07%} and {-3.47%, 0.61%, -0.15%} BD-rate savings for {Y, Cb, Cr} under RA and AI configurations
Introdouction
1

## Slide 3
GOP level encoding resolution decision
Scale factors: ×2.0 (half size) and ×1.0 (original size)
Select a scale factor in the GOP level
QP adjustment for the target bitrate: QP − 6 for ×2.0
Scale factor decision:
Proposed Method
1

## Slide 4
Fig. 1: The super resolution network architecture for luma
Fig. 2: The super resolution network architecture for chroma
Proposed Method
1
CNN-based super-resolution
The designed super resolution network architectures for luma and chroma are shown in Fig. 1 and Fig. 2 respectively.

## Slide 5
Results on NNVC-2.0
1
 | Random access Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-2.0 |  |  |  | 
sequences | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | -6.20% | -5.69% | -4.83% | 131% | 3104%
Class A2 | -1.06% | 0.89% | 0.68% | 127% | 303%
Class B | -0.40% | 0.00% | -0.30% | 128% | 279%
Class C | 0.00% | 0.00% | 0.00% | 115% | 108%
Class E |  |  |  |  | 
Average on A1 and A2 | -3.63% | -2.40% | -2.07% | 129% | 1704%
Overall | -1.58% | -0.96% | -0.93% | 125% | 357%
Class D | 0.00% | 0.00% | 0.00% | 114% | 109%
Class F | 0.00% | 0.00% | 0.00% | 144% | 113%
 | All Intra Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-2.0 |  |  |  | 
sequences | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | -4.23% | -1.52% | -1.73% | 189% | 997%
Class A2 | -2.71% | 2.74% | 1.43% | 136% | 384%
Class B | -0.75% | 0.03% | -0.30% | 129% | 292%
Class C | 0.00% | 0.00% | 0.00% | 112% | 105%
Class E | 0.00% | 0.00% | 0.00% | 129% | 103%
Average on A1 and A2 | -3.47% | 0.61% | -0.15% | 163% | 691%
Overall | -1.37% | 0.21% | -0.13% | 134% | 251%
Class D | 0.00% | 0.00% | 0.00% | 108% | 112%
Class F | 0.00% | 0.00% | 0.00% | 110% | 104%
Table 1. Performance of the proposed method (RA)
Table 2. Performance of the proposed method (AI)

## Slide 6
In this contribution, a combination of CNN-based super-resolution and adaptive GOP level encoding resolution decision is tested.
The adaptive encoding resolution decision enables the encoder to adaptively select the encoding resolution between an original size and a half size.
This proposed method shows a promising coding gains.
Conclusions
1
Thank Ericsson for crosscheck

## Slide 7
Notes: That is all. Thanks.