## Slide 1
JVET-AB0110
EE2-1.15-related: Improvements on planar horizontal and planar vertical mode
K. Kim (Kyle), D. Kim, J. Son, J. Kwak
October, 2022
WILUS Inc.

## Slide 2: Introduction
In JVET-AA0104 [1], two new additional planar modes was proposed where only the horizontal interpolation or only the vertical interpolation are used to obtain the predicted samples.
  For planar horizontal mode, only the horizontal linear interpolation is performed based on the left reference sample and the top-right reference sample to predict the current sample as:
  For planar vertical mode, only the vertical linear interpolation is performed based on the above reference sample and the bottom-left reference sample to predict the current sample as:

## Slide 3: Proposed method
The residual characteristics of the two additional planar modes may be similar to the residual characteristics of the horizontal and vertical direction mode.
Therefore, for the planar horizontal/vertical mode, this contribution proposes to use vertical/horizontal direction mode to derive a transform kernel in MTS set and LFNST set as shown in this figure.
planar vertical mode ?
planar horizontal mode ?
Horizontal mode
is used to derive a transform kernel.
Vertical mode
is used to derive a transform kernel.
Planar mode
is used to derive a transform kernel.
no
no
yes
yes
Intra prediction mode
planar mode ?
no
yes
The inputted intra prediction mode
is used to derive a transform kernel.
Proposed method

## Slide 4: Proposed method
To reduce the complexity, two new additional planar modes are only applied in the following restrictions:
  width * height > 64
  width <= 128
  height <= 128
This restriction is also applied in parsing stage.

## Slide 5: Experimental results
Anchor: ECM-6.0
  Under CTC
Test 1. a derivation method of a transform kernel for planar horizontal /vertical mode.
Test 2. Test 1 + block size restriction
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.13% | -0.01% | 114% | 98%
Class A2 | -0.15% | -0.01% | -0.08% | 113% | 97%
Class B | -0.13% | 0.04% | 0.04% | 116% | 98%
Class C | -0.11% | 0.00% | -0.05% | 116% | 99%
Class E | -0.21% | -0.08% | -0.14% | 116% | 99%
Overall | -0.14% | -0.03% | -0.04% | 115% | 98%
Class D | -0.08% | 0.02% | 0.00% | 115% | 100%
Class F | -0.11% | -0.13% | 0.11% | 108% | 98%
Class TGM | 0.02% | 0.03% | 0.05% | 108% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.04% | 0.07% | -0.13% | 102% | 99%
Class C | -0.04% | -0.05% | 0.25% | 102% | 99%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.02% | 0.00% | -0.18% | 103% | 100%
Class F | -0.02% | -0.24% | 0.00% | 102% | 100%
Class TGM | 0.06% | -0.04% | 0.05% | 102% | 99%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class E | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.04% | 0.08% | -0.03% | 105% | 98%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Test 1
Test 2

## Slide 6: Conclusion
This contribution proposes a derivation method of a transform kernel for planar horizontal & vertical mode and block size restriction.
It is recommended to further study this proposal in EE2.
Thank Alibaba for crosscheck.

## Slide 7: THANK YOU

## Slide 8: Experimental results
Anchor: EE2_1.15
  Under CTC
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0_EE2_1.15 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.01% | -0.09% | 100% | 100%
Class A2 | -0.05% | -0.08% | -0.11% | 100% | 100%
Class B | -0.06% | -0.08% | -0.04% | 100% | 100%
Class C | -0.05% | -0.09% | -0.11% | 100% | 100%
Class E | -0.08% | -0.16% | -0.20% | 100% | 100%
Overall | -0.06% | -0.08% | -0.10% | 100% | 100%
Class D | -0.05% | -0.11% | 0.01% | 100% | 100%
Class F | -0.02% | -0.08% | 0.00% | 100% | 99%
Class TGM | 0.03% | -0.03% | 0.04% | 100% | 100%