## Slide 1: m60757 Ericsson Machine Vision Codec
Christopher Hollmann
Jacob Ström
Per Wennersten
Lukasz Litwic
Rickard Sjöberg
Mitra Damghanian
Christopher Hollmann
Ericsson Research
2022-10-17

## Slide 2: Agenda
Introduction
Ericsson Machine Vision Codec
  Overview
  The encoder
  The configuration
  The decoder
Test results
Requirements
Conclusion and discussion

## Slide 3: 1. Introduction
Call for Proposals issued in April 2022
Reference point is VTM-12
Off-the-shelf VTM is not ideal for VCM
  Optimized for PSNR and HVS
  Not what VCM is looking for
Introducing Ericsson Machine Vision Codec: VVC optimized for VCM

## Slide 4: 2.a) EMVC: Overview
Input video is fed into an analyzer
  Neural network such as Faster R-CNN, Mask R-CNN or JDE-1088x608
Analyzer produces a list of objects
  Contains description of all objects in each frame
Input video and list of objects are fed into the encoder
Encoder uses an algorithm to determine QP offset for each CTU
QP offset signaled with delta QP mechanism
VVC-compliant bitstreams
  Can be decoded with any VVC decoder
Video frames
Analyzer
Encoder
List of objects
Bitstream

## Slide 5: 2.b) EMVC: Encoder changes
Algorithm to categorize each CTU in each frame
Two thresholds:
  TC : certainty threshold: objects with score less than TC are ignored
  TL: large object threshold: if the objects covers more pixels than TL, it is considered large
Assign QP offset based on category
Default values:
  TC: 0.5
  TL : 150,000
Assign all CTUs in the current picture to category A.
Iterate over all objects in the current picture:
  If the score is less than TC, continue with the next object.
  Determine the size of the object and determine whether it is a large or a small object by comparing it against TL.
  Iterate over all CTUs in the current picture:
    If the object has no overlap with the current CTU, continue with the next CTU.
    If the object is a large object and the CTU is assigned category B, continue with the next CTU.
    If the object is a large object and the CTU is assigned category A, change the assignment to category B and continue with the next CTU.
    Change the assignment of the current CTU to category C and continue with the next CTU.
Assign the following QP offsets to each CTU:
  Category A: +4
  Category B: +2
  Category C: 0

## Slide 6: 2.c) EMVC: Configuration
All Intra: no changes
Random Access:
  Increase QP offset by 5 for frames on temporal layer 2 and higher
  No changes on temporal layers 0 and 1
  For GOP32: 30 frames coded with higher QP
Temporal layer | Frames | Original config (anchor) | Modified config (EMVC)
0 | 32 | -1 | -1
1 | 16 | 0 | 0
2 | 8, 24 | 0 | 5
3 | 4, 12, 20, 28 | 3 | 8
4 | 2, 6, 10, 14, 18, 22, 24, 28 | 5 | 10
5 | 1, 3, 5, 7, 9, 11, 13, 15, 17, 18, 19, 21, 23, 25, 27, 29, 31 | 6 | 11

## Slide 7: 2.d) The decoder
No changes made!
No postprocessing
EMVC bitstreams can be decoded with any VVC decoder

## Slide 8: 3. Test results
Only mandatory results included
  No downscaled results
Per task:
  Detection: -23.65%
  Segmentation: -24.34%
  Tracking: -22.92%
Per source type:
  Video: -23.42%
  Image: -23.87%
EMVC result | Detection | Segmentation | Tracking
OpenImages | -8.65% | -10.96% | --
TVD | -31.20% | -37.72% | -22.92%
FLIR | -30.84% * | -- | --
SFU-HW | -23.92% | -- | --
Enc time | Detection | Segmentation | Tracking
OpenImages | 0.82 | 0.89 | --
TVD | 0.83 | 0.83 | 0.67
FLIR | 1.03 | -- | --
SFU-HW | 0.78 | -- | --
Dec time | Detection | Segmentation | Tracking
OpenImages | 0.96 | 1.00 | --
TVD | 1.05 | 1.05 | 0.95
FLIR | 0.99 | -- | --
SFU-HW | 0.85 | -- | --
For FLIR, the result only includes the four lowest ratepoints, as including the highest two does not produce a monotonic RD-curve

## Slide 9: But wait, there’s more!
What happens if we use a different analyzer?
  YOLOv3 off-the-shelf
  Not retrained or changed
Tested for SFU-HW and TVD-tracking
Dataset | YOLOv3 | Original analyzer
SFU-HW-objects-v1 | -22.6% | -23.9%
TVD (object tracking) | -24.8% | -22.9%

## Slide 10: 4. Requirements
Requirement | Fulfillment | Reasoning
a) VCM shall support video coding for machine task consumption purposes. | ☒ | Decoded video can be used as input for a multitude of task networks.
b) VCM shall support feature coding. | ☒ | If features are represented in YCbCr or RGB format, EMVC can compress them.
c) VCM shall support a coding efficiency improvement for at least 30% BD-rate over the VVC standard on machine vision tasks. | ☒ | For several datasets and machine vision tasks the compression performance exceeds 30%.
d) VCM shall support a broad spectrum of encoding rates. | ☒ | When using the default configuration, EMVC uses QP to encode at different bitrates.
e) VCM shall support various degrees of delay configuration. | ☒ | JVET has defined different common test conditions for different delay configurations.
f) VCM shall be agnostic to network models. | ☒ | As the output of EMVC is decoded video, there is no restriction on the network model.
g) VCM shall be agnostic to machine task types. | ☒ | As the output of EMVC is decoded video, there is no restriction on the machine task type.
h) VCM shall provide description of the meaning or the recommended way of using the decoded data. | ☒ | As the output of EMVC is decoded video, the recommended way of using the data is trivial.

## Slide 11: 4. Requirements continued
Requirement | Fulfillment | Reasoning
i) VCM should support the use and inclusion of information such as descriptors in its bitstream. | ☒ | Descriptors can for example be included using the Supplemental Enhancement Information (SEI) mechanism.
j) A single VCM bitstream shall support any number of instances of machine tasks. | ☒ | There is no limitation as the usage of the decoded data is outside the scope of EMVC.
k) VCM shall support at least the following colour formats; monochrome, RGB, and YUV (YCbCr). | ☒ | Monochrome, RGB and YCbCr are supported by EMVC.
l) VCM shall support at least the following input bit depths: 8-bit and 10-bit. | ☒ | 8-bit and 10-bit encoding and decoding are supported, along with higher bit depths.
m) VCM complexity shall allow for feasible implementation within the constraints of the available technology at the expected time of usage. | ☒ | The complexity of EMVC is assumed to be reasonable for implementation.
n) VCM shall support rectangular picture format up to 7680x4320 pixels (8K). | ☒ | 8k input data is supported.
o) VCM shall support fixed and variable rational frame rates for video inputs. | ☒ | Various frame rates are supported.
p) VCM shall support any input source from video or image. | ☒ | Images can either be treated as a sequence with a frame count of one or using a separate All Intra configuration.
q) VCM shall support privacy and security. | ☒ | Privacy measures need to be taken before encoding video using EMVC (e.g., blurring of faces).

## Slide 12: 5. Discussion & conclusion
Presented EMVC, an optimized version of VTM
Achieves gains of around 24% across all datasets
More realistic showcase of what VVC can do in terms of video compression for machine vision
  Additional reference point besides the anchor
  Proposals should outperform not only the anchors but EMVC as well to be considered as starting point for a standardization activity
Staying compliant to VVC:
  Hardware support starting to roll out
  Complexity can be chosen by implementer

## Slide 13
Thank you for your attention!