## Slide 1: JVET-AC0180 AHG7 – Reference frame padding for GDR
Tangi Poirier, Franck Aumont

## Slide 2: Reference frame for GDR in ECM-7.0
For the CUs in the clean area of the GDR/recovering picture,
  the reconstructed pixels in the dirty areas of reference pictures are set to pre-determined values which have no correlation with the Clean Area
Virtual Boundary

## Slide 3: Reference frame for GDR in this proposal
In our contribution, it is proposed to pad samples horizontally from the clean region to the dirty region
This is performed during the reference frame padding.
With on-the-fly implementation, no complexity is added
Virtual Boundary

## Slide 4
Simulation results
Low delay B Main 10 Over ECM-7.0 with GDR |  |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.12% | 0.10% | 0.03% | 94% | 91%
Class C | -0.19% | 0.07% | -0.17% | 101% | 100%
Class E | -0.38% | -0.73% | -0.21% | 99% | 99%
Overall | -0.21% | -0.12% | -0.09% | 97% | 96%
Class D | -0.28% | 0.01% | -0.52% | 100% | 101%
Class F | -0.04% | -0.07% | -0.18% | 101% | 98%
Thanks Nokia for crosschecking