## Slide 1: JVET-AD0083 Non-EE2: Improvement over IBC-LIC
Zhihuang Xie, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction
In ECM8.0, Intra block copy with local illumination compensation (IBC-LIC) is a coding tool which compensates the local illumination variation within a picture between the CU coded with IBC and its prediction block with a linear model.
The parameters of the linear model are derived using the same method as LIC for inter prediction except that the reference template is generated using a block vector in IBC-LIC.
In ECM8.0, IBC-LIC only applies to the CU whose block size is larger than or equal to 32 and smaller than or equal to 256.
Fig.1 IBC-LIC
Current block
Reference block
Current template
Reference template

## Slide 3: Proposed
It is proposed to extend IBC-LIC with different template-shape and multiple models.
Fig.2 different template for IBC-LIC
Current block
Reference block
Current template
Reference template
Current block
Reference block
Current template
Reference template
(a) above-template IBC-LIC
(b) left-template IBC-LIC
Signalling table
Value | Mode
0 | Not IBC-LIC
100 | Default IBC-LIC
101 | Multi-models IBC-LIC
110 | Top-only IBC-LIC
111 | Left-only IBC-LIC
It is also proposed to remove the larger block-size constraint. In the proposed method, IBC-LIC and the proposed additional modes can be applied to the CU whose block size is larger than 32.

## Slide 4: Simulation results
The proposed method is implemented on top of ECM-8.0.
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.50% | -0.67% | -0.54% | 101% | 99%
Class TGM | -0.11% | -0.10% | -0.07% | 102% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.47% | -0.74% | -0.48% | 100% | 99%
Class TGM | -0.03% | -0.03% | -0.07% | 102% | 100%

## Slide 5: Conclusion
It is proposed to extend IBC-LIC with different template-shape and multiple-models to further improve the coding performance.
On top of ECM-8.0, the proposed method can provide
  AI: -0.50%(Y) for class F and -0.11%(Y) for class TGM.
  RA: -0.47%(Y) for class F and -0.03%(Y) for class TGM.
It is suggested to include this contribution in EE2 for further investigation.
Thanks to Bytedance for crosschecking!