## Slide 1: JVET-AD0128 Ahg 12: modified CTC proposal for low delay
Fabrice Le Léannec, Franck Galpin, Tangi Poirier, Edouard François

## Slide 2: Observation
ECM encoding time is becoming problematic for investigating new coding tools
Worst case encoding time = QP 22 of LDB class B and class F Arena Of Valor
LDB BQTerrace QP 22 = around 14 days of computation to get full results

## Slide 3: Proposal
Change encoder configuration as follows:
  MaxBTLumaISlice=128
  MaxBTChromaISlice=128
  MaxTTLumaISlice=128
  MaxTTChromaISlice=128
  MaxMTTHierarchyDepthISliceL=4
  MaxMTTHierarchyDepthISliceC=4
  Only for class B and class F Arena Of Valor:
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222
Similar to JVET-AA0098 (adopted to reduce worst case RA class A)

## Slide 4: Impact on performances
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,03% | -0,79% | -0,76% | 91% | 100%
Class C | -0,14% | -0,12% | -0,52% | 100% | 100%
Class E | -0,64% | -0,74% | -2,39% | 102% | 99%
Overall | -0,22% | -0,55% | -1,09% | 97% | 100%
Class D | -0,10% | -0,93% | 0,04% | 100% | 98%
Class F | -0,34% | -0,97% | -0,58% | 107% | 96%
Class TGM |  |  |  |  | 
 | Low delay P Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,01% | -0,36% | -0,66% | 93% | 98%
Class C | -0,11% | -0,14% | -0,45% | 105% | 101%
Class E | -0,52% | -2,04% | -2,77% | 105% | 102%
Overall | -0,16% | -0,71% | -1,12% | 100% | 100%
Class D | -0,08% | -0,52% | 0,79% | 103% | 102%
Class F | -0,21% | -0,65% | -0,25% | 110% | 101%
Class TGM |  |  |  |  | 

## Slide 5: Impact on LDB and LDP worst cases
 | ECM-8.0, low-delay B, QP=22 |  |  |  |  | 
 | Reference |  | Test |  |  | 
Sequence | Enc T [h] | Enc T [d] | Enc T [h] | Enc T [d] | ΔEnc T [d] | EncR
MarketPlace | 259,20 | 10,80 | 173,61 | 7,23 | -3,57 | 0,67
RitualDance | 171,69 | 7,15 | 118,90 | 4,95 | -2,20 | 0,69
Cactus | 213,74 | 8,91 | 139,82 | 5,83 | -3,08 | 0,65
BasketballDrive | 267,10 | 11,13 | 171,89 | 7,16 | -3,97 | 0,64
BQTerrace | 331,04 | 13,79 | 216,93 | 9,04 | -4,75 | 0,66
ArenaOfValor | 223,05 | 9,29 | 184,90 | 7,70 | -2,25 | 0,00
 | ECM-8.0, low-delay P, QP=22 |  |  |  |  | 
 | Reference |  | Test |  |  | 
Sequence | Enc T [h] | Enc T [d] | Enc T [h] | Enc T [d] | ΔEnc T [d] | EncR
MarketPlace | 182,26 | 7,59 | 136,98 | 5,71 | -1,89 | 0,75
RitualDance | 114,60 | 4,77 | 83,03 | 3,46 | -1,32 | 0,72
Cactus | 137,81 | 5,74 | 98,26 | 4,09 | -1,65 | 0,71
BasketballDrive | 180,35 | 7,51 | 126,26 | 5,26 | -2,25 | 0,70
BQTerrace | 225,59 | 9,40 | 164,41 | 6,85 | -2,55 | 0,73
ArenaOfValor | 165,32 | 6,89 | 129,60 | 5,40 | -1,49 | 0,78

## Slide 6: Applying proposed changes to VTM11-ECM8 anchor
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,07% | 1,17% | 0,05% | 84% | 101%
Class C | -0,20% | -0,06% | -0,24% | 99% | 99%
Class E | -0,38% | -1,34% | 0,32% | 99% | 97%
Overall | -0,13% | 0,13% | 0,02% | 92% | 99%
Class D | -0,08% | 0,41% | 0,29% | 98% | 102%
Class F | -0,09% | -0,25% | -0,03% | 99% | 102%
Class TGM |  |  |  |  | 
 | Low delay P Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,05% | 1,28% | 0,62% | 81% | 97%
Class C | -0,15% | -0,20% | -0,29% | 99% | 91%
Class E | -0,40% | -0,36% | -0,06% | 98% | 100%
Overall | -0,13% | 0,38% | 0,14% | 91% | 96%
Class D | -0,03% | 0,67% | -0,74% | 99% | 97%
Class F | -0,39% | -0,35% | 0,04% | 102% | 101%
Class TGM |  |  |  |  | 
Tested VTM11-ECM8 encoder configuration:
  MaxBTLumaISlice=128
  MaxBTChromaISlice=64
  MaxTTLumaISlice=64
  MaxTTChromaISlice=64
  MaxMTTHierarchyDepthISliceL=4
  MaxMTTHierarchyDepthISliceC=4
  MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222 (class B and F HD only)
Worst case reduction = 50%

## Slide 7: Conclusion
A modification of EE2 CTCs is proposed to
  Significantly reduce the worst-case encoding time of ECM in LDB and LDP
  Improve the trade-off between encoding time and coding efficiency
ECM test set is made more convenient to use in practice
Propose to adopt proposed CTC modifications for next JVET cycles
Thanks to Xiaomi for cross-checking

## Slide 8: Bakup information: worst cases in Ahg 12 CTCs
0 14d22h ctc-ldb_BQTerrace_1920x1080_60Hz_8bit_P420_22_all.log
1 11d12h ctc-ldb_BasketballDrive_1920x1080_50Hz_8bit_P420_22_all.log
2 11d00h ctc-ldb_MarketPlace_1920x1080_60Hz_10bit_P420_22_all.log
3 10d01h ctc-ldb_F_TencentAOV5_1920x1080_60Hz_8bit_P420_22_all.log
4 9d18h ctc-ra_ParkRunning3_3840x2160_50Hz_10bit_P420_22_P4.log
5 9d13h ctc-ra_ParkRunning3_3840x2160_50Hz_10bit_P420_22_P3.log
6 9d11h ctc-ra_ParkRunning3_3840x2160_50Hz_10bit_P420_22_P2.log
7 9d11h ctc-ra_ParkRunning3_3840x2160_50Hz_10bit_P420_22_P1.log
8 8d22h ctc-ldb_Cactus_1920x1080_50Hz_8bit_P420_22_all.log
9 8d19h ctc-ra_DaylightRoad2_3840x2160_60Hz_10bit_P420_709_22_P1.log
10 8d13h ctc-ra_DaylightRoad2_3840x2160_60Hz_10bit_P420_709_22_P2.log
11 8d02h ctc-ra_A1_Tango2_3840x2160_60Hz_10bit_P420_22_P1.log