## Slide 1: AHG10: Lambda-QP Relationship Fix for Slice-level Multi-QP Optimization
Junqi Liao, Li Li, Dong Liu, Houqiang Li, Feng Wu
University of Science and Technology of China
JVET-AD0133

## Slide 2: Multi-QP optimization in VTM
Lambda and QP are usually assumed to have a fixed relationship in a codec.
However, the lambda-QP relationship is content-dependent. Frame-level multi-QP optimization is used to determine different QPs for frames with different content by applying RDO to the QPs used for each frame.

## Slide 3: Framework of multi-QP optimization
Get the QP RDO range
(SliceQp±DeltaQpRD)
Get basic lambda
(=)
Encode the current frame using the QP being traversed
Calculate the RD-cost and update the best QP.
All QPs in RDO range are traversed?
N
Y
Return the best QP

## Slide 4: Problems in the original implementation
Get the QP RDO range
(SliceQp±DeltaQpRD)
Get basic lambda
(=)
Encode the current frame using the QP being traversed
Calculate the RD-cost and update the best QP.
All QPs in RDO range are traversed?
N
Y
Return the best QP
The QP-lambda relationship used for calculating lambda here is not aligned with the QP-lambda relationship used in other parts of VTM, and an outdated version of the QP-lambda relationship is being used.
We propose to fix it.

## Slide 5: Problems in the original implementation
Get the QP RDO range
(SliceQp±DeltaQpRD)
Get basic lambda
(=)
Encode the current frame using the QP being traversed
Calculate the RD-cost and update the best QP.
All QPs in RDO range are traversed?
N
Y
Return the best QP
Since we want to obtain an appropriate frame-level QP, lambda should not vary during the RDO process. However, in the current implementation, lambda varies with the traversed QP during the RDO process.
We propose to fix it.

## Slide 6: Our improvements to the frame-level multi-QP optimization.
We propose to align the QP-lambda relationship used in multi-QP optimization with the QP-lambda relationship used in other parts of VTM.
We propose that in the RDO process of frame-level multi-QP optimization, lambda should not vary with the traversed QP, but should be fixed using the lambda corresponding to SliceQp.
Since we have observed cache conflicts when frame-level multi-QP optimization and REUSE_CU_RESULTS are enabled at the same time, we propose to disable REUSE_CU_RESULTS when frame-level multi-QP optimization is being used.

## Slide 7: Test results
All intra
Random access
Low delay B
Low delay P
 | Over VTM19.2 multiQP_anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -9.18% | 2.85% | -1.59% | 100% | 99%
Class A2 | -9.38% | -4.13% | -4.38% | 100% | 101%
Class B | -8.31% | -7.76% | -6.98% | 100% | 100%
Class C | -7.20% | -9.09% | -8.54% | 99% | 101%
Class E | -7.51% | -7.77% | -7.03% | 100% | 101%
Overall | -8.25% | -5.68% | -6.00% | 100% | 100%
Class D | -7.61% | -8.35% | -8.60% | 100% | 101%
Class F (optional) |  |  |  |  | 
 | Over VTM19.2 multiQP_anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -11.15% | -6.58% | -6.58% | 100% | 100%
Class C | -10.49% | -7.26% | -9.33% | 100% | 99%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class D | -10.20% | -7.54% | -7.61% | 99% | 101%
Class F (optional) |  |  |  |  | 
 | Over VTM19.2 multiQP_anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -8.22% | -6.97% | -6.04% | 100% | 100%
Class C | -3.48% | -5.86% | -7.32% | 100% | 100%
Class E | -2.78% | 3.61% | 6.49% | 100% | 100%
Overall | -5.28% | -3.96% | -3.34% | 100% | 100%
Class D | -4.81% | -3.40% | -4.08% | 100% | 101%
Class F (optional) |  |  |  |  | 
 | Over VTM19.2 multiQP_anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -7.91% | -6.97% | -6.20% | 100% | 100%
Class C | -2.51% | -4.50% | -6.37% | 101% | 100%
Class E | -2.09% | 4.79% | 7.87% | 100% | 100%
Overall | -4.65% | -3.21% | -2.74% | 100% | 100%
Class D | -4.42% | -2.43% | -3.47% | 100% | 100%
Class F (optional) |  |  |  |  | 

## Slide 8: Thank you!