## Slide 1
JVET-AD0218 AHG12:
CCSAO with extended edge classifiers and history offsets
Che-Wei Kuo, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Ning Yan,
Changyue Ma, and Xianglin Wang

## Slide 2: Introduction
In ECM-8.0, CCSAO enhances the reconstructive quality of samples by
  classifying them into different categories
  adding one offset to the reconstructed samples for each category
Support band classifier and edge classifier, switch in CTB level
  maximum 4 classifiers per slice
  encoder derives and signals parameters/offsets for each slice independently
Band classifier
  uses the band indices of 3 collocated samples to classify one sample

## Slide 3: Introduction
Edge classifier
  combines luma edge and the band index of a collocated sample to classify one sample
  number of edge categories: 16
  number of band categories: 1 to 4
  edge direction, , , are decided by encoder and signaled in SH
, ,
edge index of the luma samples (a, b)
band index of the collocated sample
selected collocated component sample
numbers of equally divided bands
signaled threshold

## Slide 4: Extended Edge Classifiers
Propose 3 extended edge classifiers
  subset of the original one with less edge categories
  gives encoder flexibility for more edge/band combinations
  number of edge categories: 16 to 4
  number of corresponding maximum band categories: 4 to 16
  the component used for edge classification can be selected from one of all 3 components
Selected edge classifier/edge component are decided by encoder and signaled in SH

## Slide 5: History Offsets
There is strong temporal correlation among the CCSAO offsets and classifier parameters of different frames
To reduce the signaling overhead, it is proposed to store the offsets/parameters of the current frame which can be referenced for the CCSAO process of future frames
Similar to the APS design in VVC, an index is signaled in SH to indicate which set of stored offsets/parameters is inherited in the current slice

## Slide 6: Simulation Results
Unavailable points copied from anchor

## Slide 7: Conclusion
Propose two modifications to improve the coding efficiency of CCSAO
  extended edge classifier with multiple combinations
  temporal historical offsets/parameters for the usage of future frames
Coding gains with marginal cost
  classification-based sample operation
Suggest to study in EE