## Slide 1: JVET-AF0071, EE1-related: Further complexity reduction on the joint EE1-0 (LOP.2) unified filter
October, 2023
Tong Shao, Peng Yin, Sean McCarthy (Dolby)
Jay N. Shingala, Ajay Shyam, Ajat Suneja, Siddarth P. Badya (Ittiam)

## Slide 2: Outline
Proposed model: Residual block fusion in unified LOP2
  Improved LOP2 backbone layer which enables fusion of adjacent 1x1 convolution layers.
Complexity reduction:
  Reduce the complexity of the unified LOP2.3 from 17.05 kMac/Pixel to 16.56 kMac/Pixel
  Reduce the number of convolutional layers by 13%.
Fast Stage 3 training, compared to the best LOP2.3 training results in JVET-AF0043
  fp32 {0.00%, 0.71%, 0.99%} under AI, {-0.09%, 1.55%, 1.49%} under RA
  int16 {0.00%, 0.78%, 1.06%} under AI and {-0.08%, 1.76%, 2.04%} under RA
  Actual decoding time is reduced by ~5% compared to the best LOP2.3.
Fast Stage 3 training, compared to the NNVC-6.0 VTM anchor
  fp32 is {-4.77%, -9.14%, -9.13%} under AI and {-5.46%, -9.31%, -9.20%} under RA
  int16 is {-4.74%, -9.09%, -9.17%} under AI and {-5.38%, -9.41%, -8.57%} under RA
Conclusions: further study in EE1.

## Slide 3: Current NNVC LOP1.0 anchor
16.2 kMac/Pixel
Fusion of adjacent 1x1 conv. layers
No skip connection in backbone: Absence of residual blocks enables fusion of adjacent 1x1 layers

## Slide 4: Unified LOP 2.3 in JVET-AF0043
Split luma/chroma paths
Skip connection in backbone block
  Fusion of 1x1 conv. layers impossible
  LOP-2 backbone ends up with an extra 1x1 conv. layer compared to LOP-1
[C,h,w]
CONV 1  1 C1+C
CONV 1  1 CC1
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
CONV 1  1 C1+C
CONV 1  1 CC1
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
1x1 fusion is not possible due to skip connection

## Slide 5: Proposed Residual block fusion architecture
Same parameters and number of backbone blocks as LOP2.3
Adjust the order of layers within backbone block
Fusion is then possible and performed.
Wide activation layers are preserved
Additional 1x1 conv layer before the first backbone and after the last backbone layer to match channel dimensions
[C,h,w]
CONV 1  1 C1+C
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
CONV 1  1 CC1
CONV 1  1 CC1
fusion

## Slide 6: Revised back bone structure
After 1x1 fusion, new back bone structure has 4 conv layers compared to 5 conv layers in old back bone structure
Kmac is reduced by CxC in each backbone layer
Wide activation layers are preserved
[C,h,w]
CONV 1  1 C1+C
sepCONV 1  3 CC21
sepCONV 3  1 C21C
PReLU
Back Bone Block C
[C,h,w]
CONV 1  1 CC
CONV 1  1 CC1
CONV 1  1 CC1
fusion
Old Backbone structure
New Backbone structure

## Slide 7: Complexity reduction
Complexity of the unified LOP2.3 from 17.05 kMac/Pixel to 16.56 kMac/Pixel
Reduce the number of convolutional layers by 13%.

## Slide 8: Training information
Fast Stage 3 training
The same training scheduler as LOP2.3 except batchsize=64 (LOP2.3’s is 128)
"stage3" : { "training" : { "mse_epoch" : 58, "max_epochs" : 60, "component_loss_weightings" : [12, 2], "dataloader": {"batch_size": 64 }, "optimizer": {"lr": 0.0004, }, "lr_scheduler" : {"milestones" : [55, 57, 58] } } }

## Slide 9: Compared to best trained LOP2.3, SADL ft32
{0.00%, 0.71%, 0.99%} under AI
{-0.09%, 1.55%, 1.49%} under RA

## Slide 10: Compared to best trained LOP2.3, SADL int16
{0.00%, 0.78%, 1.06%} under AI
{-0.08%, 1.76%, 2.04%} under RA
~5% decoding time reduction

## Slide 11: Compared to our trained LOP2.3 with batchsize=64, SADL ft32
{-0.11%, -0.31%, -0.33%} under AI
{-0.14%, 0.66%, -1.56%} under RA
A fairer ablation study.
Batchsize=64. All others are the same as LOP2.3 training strategy.

## Slide 12: Compared to NNVC-6.0 VTM anchor, SADL ft32
{-4.77%, -9.14%, -9.13%} under AI
{-5.46%, -9.31%, -9.20%} under RA

## Slide 13: Compared to NNVC-6.0 VTM anchor, SADL int16
{-4.74%, -9.09%, -9.17%} under AI
{-5.38%, -9.41%, -8.57%} under RA

## Slide 14: Conclusions
New residual block fusion architecture
Complexity of the unified LOP2.3 reduced from 17.05 kMac/Pixel to 16.56 kMac/Pixel
Reduce the number of convolutional layers by 13%.
Actual decoding time is reduced by ~5% compared to LOP2.3
Improved BD-Rate in our ablation tests (LOP2.3 bs-64) for both luma and chroma components
Slightly improved Luma compared to best trained LOP2.3, with some loss in Chroma.
Propose to further study in the next EE1.
Thanks Qualcomm for crosscheck.

## Slide 15: Q&A Thanks!

## Slide 16: Training and Inference Stage Information
Network Information in Training Stage |  | 
Mandatory | GPU Type | Nvidia GeForce RTX4090
 | Framework: | Pytorch v2.0.1
 | Number of GPUs per Task | 1
 | Epoch: | 60 (fast stage3 trained using LOP2.3 stage3 dataset)
 | Batch size: | 64
 | Loss function: | L1, L2
 | Training time (for 1 model): | ~7 days
 | Training data information: | DIV2K, TVD, BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | 
Optional |  | 
 | Number of iterations | 
 | Patch size | 144x144
 | Learning rate: | 4e-4
 | Learning rate update strategy | Stage2/3: 55, 57, 58. mse-epoch:58
 | Optimizer: | ADAM
 | Preprocessing: | flipped, rotated
 | Mini-batch selection process: | random cropped
 | Training data update strategy: | 
 | Other information: | 
Network Information in Inference Stage |  | 
 | HW environment: | 
 | GPU Type | CPU only
 | Framework: | SADL float
 | Number of GPUs per Task | 0
 | Number of Parameters (Each Model) | 49556
 | Total Parameter Number | 49556
 | Parameter Precision (Bits) | Floating (32 bits)
 | Memory Parameter (MB) | 0.223 (float)
 | MAC/Pixel (Kilo) | 16.56
 | Total Conv. Layers | 92
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 128128, 256256
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage | 
 | Peak Memory Usage (per Model) | 
 | Other information: | 
Network Information in Inference Stage |  | 
 | HW environment: | 
 | GPU Type | CPU only
 | Framework: | SADL float
 | Number of GPUs per Task | 0
 | Number of Parameters (Each Model) | 49556
 | Total Parameter Number | 49556
 | Parameter Precision (Bits) | Floating (32 bits)
 | Memory Parameter (MB) | 0.223 (float)
 | MAC/Pixel (Kilo) | 16.56
 | Total Conv. Layers | 92
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage | 
 | Peak Memory Usage (per Model) | 
 | Other information: |