## Slide 1: JVET-AG0069 AhG11: LOP with inputs transformed
Du Liu, Jacob Ström, Mitra Damghanian, Per Wennersten
Ericsson

## Slide 2: Overview
Current LOP.2: 17 kMAC/pixel, 0.05M parameters
Proposed modification
  Apply a 2x2 DCT-II transform and reshaping to the inputs of LOP
  Apply an inverse DCT-II and inverse reshaping to the output of LOP
  Increase the number of backbone blocks and channels
The proposed model has a complexity of 16.9 kMAC/pixel and 0.2M parameters
Compared to NNVC-7.1 anchor (NN Intra + LOP.2)
  Float: RA {-0.48%, -3.94%, -3.51%}, AI {-0.17%, -4.16%, -4.55%}, LDB {-0.21%, -0.03%, 0.53%}
  Int16: RA {-0.44%, -3.37%, -3.42%}, AI {-0.18%, -4.07%, -4.57%}, LDB {-0.03%, 0.61%, 1.75%}

## Slide 3: Current LOP.2 architecture
144x144x3
144x144x3
144x144x3
144x144x1
144x144x1
144x144x1
72x72x(CY+CUV)

## Slide 4: Proposed inputs with DCT transform
Current
Proposed inputs using 2x2 DCT
RecEXTY
RecEXTUV
2↑
Rec
conv 3x3, d1
144x144x3
144x144x1
72x72x2
…
144x144xd1
RecEXTY
RecEXTUV
2↑
DCT-II
conv 3x3, d1
72x72x6
144x144x1
72x72x2
…
2↓
Rec
72x72x4
72x72x2
72x72xd1

## Slide 5: Proposed model with inputs transformed
CONV 1x1 CxC1
PReLU
CONV 1x1 C1xC
sepCONV 1x3 CxC21
sepCONV 3x1 C21xC
CONV 1x1 CxC
[C,h,w]
[C,h,w]
Backbone block C
NUV
Rec
Pred
BS
QPbase
QPslice
IPB
CONV 3x3,d1
CONV 3x3,d2
CONV 1x1,d3
CONV 1x1,d4
CONV 1x1,d4
CONV 1x1,d5
CONV 1x1,d6
PReLU
CONV 2↓ 3x3,CY+CUV
PReLU
Backbone Block CY
Backbone Block CY
…
Backbone Block CUV
Backbone Block CUV
…
NY
72x72x6
72x72x6
72x72x6
72x72x1
72x72x1
72x72x4
72x72xd6
36x36x(CY+CUV)
sepCONV 1x3 CYxCY21
sepCONV 3x1 CY21xCY
sepCONV 1x3 CUVxCUV21
sepCONV 3x1 CUV21xCuv
CONV 1x1,CY
CONV 1x1,CUV
PReLU
PReLU
CONV 3x3,16
CONV 3x3,8
36x36x16
Pixel Shuffle
IDCT
72x72x4
IDCT
36x36x8
RecEXTY
RecEXTUV
DCT
Crop
Crop
Rec Y
Rec UV
72x72x2
2↑, 2↓
144x144x1

## Slide 6: Complexity
Spatial dimension going through the backbone is 36x36 instead of 72x72
Spatial resolution inside the network is reduced by a factor of four
While the final output still has the same number of pixels (=128x128)
Complexity is reduced
  LOP.2 17 kMAC/pixel  4.6 kMAC/pixel
Parameters 51258  54416 (0.05M)
Further adjustment to meet 17 kMAC/pixel
Head d1: 12  16 d2: 8 d3: 4 d4: 2 d5: 2 d6: 24  48 | Backbone NY: 14  18 NUV: 4  7 C: 16  32 C1Y: 64  96 C1UV: 32  48 C21: 16  32
16.9 kMAC/pixel
Parameters 208107 (0.2M)

## Slide 7: Training
Stage 1
  DIV2K
  lr 1e-4, batch size 64, weights 6:1:1, 40 epochs, 6 days
  Model is HOP with inputs transformed (126 kMAC/pixel)
Stage 2
  RA data generated using stage 1 model + DIV2K
  lr 1e-4, batch size 64, weights 6:1:1, 20 epochs, 3 days
  Model is HOP with inputs transformed and reduced complexity (18 kMAC/pixel)
Stage 3
  RA data generated using stage 2 model + DIV2K
  lr 4e-4, batch size 128, weights 6:1:1, 60 epochs, 6.5 days
  Model is the proposed model (16.9 kMAC/pixel)
Table 1. Network Information for the input-transformed model in training. |  | 
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: NVIDIA A100-PCIE-40GB
 | Framework: | PyTorch v1.9
 | Number of GPUs per Task | 1
 | Epoch: | Stage1: 40 Stage2: 20 Stage3: 60
 | Batch size: | Stage1/2: 64 Stage3: 128
 | Loss function: | L1 and MSE
 | Training time: | Stage1: 6 days Stage2: 3 days Stage3: 6.5 days
 | Training data information: | DIV2K, BVI-DVC, TVD
 | Training configurations for generating compressed training data (if different to VTM CTC): | NNVC-5.1 using the input-transformed model
Optional |  | 
 | Number of iterations | 
 | Patch size | 144x144
 | Learning rate: | Stage1: 1e-4, milestones [30, 34] Stage2: 1e-4, milestones [15, 17, 18] Stage3: 4e-4, milestones [55, 57, 58]
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | 

## Slide 8: Results over NNVC-7.1 anchor (NNIntra+LOP.2)
The proposed input-transformed model (NNIntra enabled) vs. NNVC-7.1, float
The proposed input-transformed model (NNIntra enabled) vs. NNVC-7.1, int16 Model is quantized with 12 bits
 | Random access |  | 
 | BD-rate Over NNVC-7.1 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.16% | -6.06% | -5.97%
Class A2 | -0.85% | -3.88% | -1.87%
Class B | -0.31% | -3.84% | -4.19%
Class C | 0.08% | -2.51% | -2.05%
Class E |  |  | 
Overall | -0.48% | -3.94% | -3.51%
Class D | 0.60% | -1.42% | -1.19%
Class F | 0.00% | -1.39% | -0.20%
 | All Intra |  | 
 | BD-rate Over NNVC-7.1 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.60% | -5.04% | -6.75%
Class A2 | -0.30% | -4.28% | -2.34%
Class B | -0.12% | -4.20% | -5.16%
Class C | 0.19% | -2.63% | -2.81%
Class E | -0.15% | -5.15% | -5.83%
Overall | -0.17% | -4.16% | -4.55%
Class D | 0.45% | -2.01% | -1.06%
Class F | 0.04% | -1.18% | -1.85%
 | Low delay B |  | 
 | BD-rate Over NNVC-7.1 float anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.46% | 1.34% | -0.72%
Class C | 0.01% | -1.39% | 2.18%
Class E | -0.09% | -0.52% | 0.40%
Overall | -0.21% | -0.03% | 0.53%
Class D | 0.33% | 1.02% | -0.46%
Class F | 0.04% | -1.20% | 2.69%
 | Random access |  | 
 | BD-rate Over NNVC-7.1 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.24% | -5.29% | -5.77%
Class A2 | -0.76% | -2.93% | -1.67%
Class B | -0.26% | -3.38% | -4.14%
Class C | 0.16% | -2.27% | -2.06%
Class E |  |  | 
Overall | -0.44% | -3.37% | -3.42%
Class D | 0.61% | -1.21% | -1.29%
Class F | 0.01% | -1.24% | -0.05%
 | All Intra |  | 
 | BD-rate Over NNVC-7.1 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.68% | -4.92% | -7.23%
Class A2 | -0.29% | -4.11% | -2.24%
Class B | -0.12% | -4.12% | -5.05%
Class C | 0.18% | -2.62% | -2.86%
Class E | -0.15% | -5.02% | -5.69%
Overall | -0.18% | -4.07% | -4.57%
Class D | 0.43% | -1.87% | -1.11%
Class F | 0.01% | -1.14% | -1.68%
 | Low delay B |  | 
 | BD-rate Over NNVC-7.1 int anchor |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 |  |  | 
Class A2 |  |  | 
Class B | -0.38% | 1.40% | 0.30%
Class C | 0.10% | -0.64% | 2.16%
Class E | 0.41% | 0.95% | 3.61%
Overall | -0.03% | 0.61% | 1.75%
Class D | 0.44% | 0.35% | 1.88%
Class F | 0.07% | -1.20% | 3.37%

## Slide 9: Supplementary tests vs. proposed model, float
Sup. 1: The input-transformed model trained with weights 1211 instead of 611 at stage 3.
Sup. 2: The input-transformed model trained with weights 611 but using the LOP training data at stage 3.
Sup. 3: The model has inputs and output reshaped, with increased number of parameters, but without the DCT transform.
 | Random access |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | 0.12% | 2.90% | 3.29%
Class A2 | 0.19% | 1.76% | 1.86%
Class B | 0.02% | 1.81% | 3.03%
Class C | -0.01% | 1.82% | 3.00%
Class E |  |  | 
Overall | 0.07% | 2.02% | 2.84%
Class D | -0.08% | 1.29% | 2.68%
Class F | -0.10% | 1.40% | 1.83%
 | All Intra |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.02% | 2.08% | 3.68%
Class A2 | -0.04% | 1.52% | 1.77%
Class B | -0.10% | 1.58% | 2.68%
Class C | -0.11% | 1.53% | 2.80%
Class E | -0.13% | 2.08% | 3.28%
Overall | -0.08% | 1.73% | 2.82%
Class D | -0.09% | 1.49% | 2.79%
Class F | -0.10% | 0.79% | 2.69%
Sup. 1
Sup. 2
Sup. 3
 | Random access |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | 0.36% | 0.09% | -0.78%
Class A2 | 0.44% | 0.19% | 0.37%
Class B | 0.27% | 0.34% | 0.25%
Class C | 0.14% | 0.26% | 0.29%
Class E |  |  | 
Overall | 0.29% | 0.24% | 0.08%
Class D | 0.10% | -0.29% | 0.35%
Class F | 0.07% | 1.00% | 0.79%
 | All Intra |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | 0.09% | -0.52% | -0.03%
Class A2 | 0.02% | -0.33% | -0.15%
Class B | 0.01% | -0.13% | -0.25%
Class C | 0.01% | -0.19% | -0.03%
Class E | -0.01% | -0.74% | -0.48%
Overall | 0.02% | -0.34% | -0.18%
Class D | -0.05% | -0.38% | -0.32%
Class F | 0.02% | 0.56% | 0.72%
 | Random access |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | 0.27% | 0.09% | -0.75%
Class A2 | 0.22% | 0.19% | -0.44%
Class B | 0.13% | 0.07% | 0.67%
Class C | 0.09% | -0.07% | 0.00%
Class E |  |  | 
Overall | 0.16% | 0.06% | -0.01%
Class D | 0.06% | -0.74% | -0.29%
Class F | -0.02% | 0.33% | -0.10%
 | All Intra |  | 
 | BD-rate Over Proposed float model |  | 
 | Y-PSNR | U-PSNR | V-PSNR
Class A1 | 0.01% | 0.13% | 0.18%
Class A2 | 0.02% | 0.23% | 0.31%
Class B | 0.01% | 0.22% | 0.78%
Class C | 0.08% | 0.16% | 0.42%
Class E | 0.08% | 0.54% | 0.80%
Overall | 0.04% | 0.25% | 0.53%
Class D | 0.10% | -0.26% | 0.47%
Class F | 0.05% | 0.34% | 1.36%

## Slide 10: Conclusions
It is proposed to
  Apply a 2x2 DCT-II transform and reshaping to the inputs of LOP
  Apply an inverse DCT-II and inverse reshaping to the output of LOP
  Increase the number of backbone blocks and channels
The proposed model has a complexity of 16.9 kMAC/pixel and 0.2M parameters
BD-rate PSNR impact over NNVC-7.1 is
  Float: RA {-0.48%, -3.94%, -3.51%}, AI {-0.17%, -4.16%, -4.55%}, LDB {-0.21%, -0.03%, 0.53%}
  Int16: RA {-0.44%, -3.37%, -3.42%}, AI {-0.18%, -4.07%, -4.57%}, LDB {-0.03%, 0.61%, 1.75%}
It is proposed to study the input-transformed model in the next EE
Thanks to Qualcomm for crosschecking