## Slide 1: JVET-AG0074 Non-EE2: IntraTMP with HMVP Candidates
Ce Zhu, Gang Li, Tong Tang, Lei Luo, Hongwei Guo (UESTC)
Yongkai Huo, Yutian Liu (Transsion)

## Slide 2: Introduction
In ECM11.0, IntraTMP and IBC BV will be stored to the history BV list.
The history BV list will be referenced by IBC AMVP, IBC merge, and chroma DBV modes.
However, IntraTMP does not use the history BV list even though it also uses block vectors to generate prediction.

## Slide 3: Proposal
HMVP list will also be used in IntraTMP mode.
The HMVP list used in our proposal is the same as the HMVP list used in IBC mode.
For added BV candidates that are not within the predefined search range, expanding their refinement search window to 5x5.

## Slide 4: Result
Based on the platform in ECM11.0
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class F | -0.06% | 0.03% | 0.16% | 99.7% | 99.4% | 100.0% | 100.0%
Class TGM | -0.10% | -0.07% | -0.05% | 97.9% | 99.5% | 100.0% | 100.0%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class F | 0.00% | 0.02% | 0.05% | 99.8% | 100.0% | 99.4% | 100.0%
Class TGM | -0.13% | -0.35% | -0.30% | 93.8% | 99.7% | 100.1% | 100.2%

## Slide 5: Conclusion
Extending the IntraTMP candidate list with the HMVP candidate block vectors is proposed.
On top of ECM-11.0, the proposed method can provide -0.06% Luma gains for class F and -0.10% Luma gains for TGM in AI configuration with no additional encoder or decoder complexity.
It is recommended to study the proposal in the next round of EE2.
Thanks to InterDigital for crosschecking!

## Slide 6: Thanks
www.transsion.com