## Slide 1: JVET-AG0113 Non-EE2: FIBC Extension
Jiyoung Kim, Jaeha Kang, Heeji Han, Haechul Choi (HNU) Woong Lim, Sung-Chang Lim (ETRI)

## Slide 2: Summary
ECM-11.0
  IBC-LIC supports multiple template shapes and multiple models.
  FIBC supports only the L-shape template and does not support multiple models.
Proposal
  An extension method for FIBC, similar to IBC-LIC, supporting multiple template shapes and multiple models in FIBC.
Experimental results
 |  | Y | U | V | EncT | DecT
AI | Class F | -0.03% | -0.11% | 0.26% | 103.9% | 99.9%
 | Class TGM | -0.07% | -0.03% | -0.03% | 104.3% | 99.9%
RA | Class F | -0.09% | -0.21% | -0.10% | 101.7% | 99.6%
 | Class TGM | -0.07% | -0.08% | -0.02% | 100.9% | 100.3%

## Slide 3: IBC-LIC in ECM-11.0
IBC-LIC and FIBC are supported for IBC prediction blocks to compensate for local illumination variation.
Bin string | Mode
00 | Not IBC-LIC
0100 | L-shaped IBC-LIC
0101 | Multi-model IBC-LIC
0110 | Top-only IBC-LIC
0111 | Left-only IBC-LIC
1 | L-shaped FIBC
IBC-LIC and FIBC signalling
[ IBC-LIC ]
  Using a linear model:
  Supporting multiple template shapes
  Supporting multiple models
L-shaped IBC-LIC mode
Reference block
or
Current block
L-shaped template
Reference block
or
Current block
Top-only template
Top-only IBC-LIC mode
Reference block
or
Current block
Left-only template
Left-only IBC-LIC mode
Multi-model IBC-LIC mode

## Slide 4: FIBC in ECM-11.0
IBC-LIC and FIBC are supported for IBC prediction blocks to compensate for local illumination variation.
Bin string | Mode
00 | Not IBC-LIC
0100 | L-shaped IBC-LIC
0101 | Multi-model IBC-LIC
0110 | Top-only IBC-LIC
0111 | Left-only IBC-LIC
1 | L-shaped FIBC
IBC-LIC and FIBC signalling
[ FIBC ]
  Using a 7-tap filter and L-shape template only
  Not supporting multiple template shapes and multiple models
,where P = ( C*C + midVal ) >> bitDepth and B= 512 for 10-bit
L-shaped FIBC mode
Reference block
or
Current block
L-shaped template

## Slide 5: Proposal
FIBC mode is straightforwardly extended like IBC-LIC, which supports multiple template shapes and multiple models.
  Proposed multiple template shapes for FIBC
  Proposed multiple models for FIBC
If ,
Otherwise,
,where is an average of the reference block’s template samples
Multi-model FIBC mode
L-shaped FIBC mode
Reference block
or
Current block
L-shaped template
Reference block
or
Current block
Top-only template
Top-only FIBC mode
Reference block
or
Current block
Left-only template
Left-only FIBC mode

## Slide 6: Proposal
Proposed signalling for IBC AMVP mode
  To support Multi-model FIBC, Top-only FIBC, and Left-only FIBC, the additional modes are signaled as follows:
Bin string | Mode
00 | Not IBC-LIC
0100 | L-shaped IBC-LIC
0101 | Multi-model IBC-LIC
0110 | Top-only IBC-LIC
0111 | Left-only IBC-LIC
100 | L-shaped FIBC
101 | Multi-model FIBC
110 | Top-only FIBC
111 | Left-only FIBC

## Slide 7: Proposal
Proposed inheritance for IBC merge mode
  FIBC model information, which indicates whether multi-model are used or not, is inherited from a merge candidate.
  The template shape is not inherited, and only L-shaped template is allowed by default.
... | ...
Bv | (x,y)
FIBC_flag | True
FIBC_mode | Top-only FIBC
... | ....
current block
... | ...
Bv | (x,y)
FIBC_flag | True
FIBC_mode | L-shaped FIBC (default)
... | ....
... | ...
Bv | (x,y)
FIBC_flag | True
FIBC_mode | Multi-model FIBC
... | ....
... | ...
Bv | (x,y)
FIBC_flag | True
FIBC_mode | Multi-model FIBC
... | ....
current block
IBC merge candidate
IBC merge candidate
X
Model information is inherited
Template shape information is not inherited

## Slide 8: Experimental results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class F | -0.03% | -0.11% | 0.26% | 103.9% | 99.9% | 96.9% | 100.4%
Class TGM | -0.07% | -0.03% | -0.03% | 104.3% | 99.9% | 99.9% | 100.4%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class F | -0.09% | -0.21% | -0.10% | 101.7% | 99.6% | 100.8% | 100.5%
Class TGM | -0.07% | -0.08% | -0.02% | 100.9% | 100.3% | 100.7% | 101.6%

## Slide 9: Experimental results
Additional test #1: Inheritance of template shape information only from IBC merge candidate
AI | Class F | BasketballDrillText | -0.03% | 0.03% | 0.19%
 |  | ArenaOfValor | #VALUE! | #VALUE! | #VALUE
 |  | SlideEditing | -0.14% | -0.19% | -0.15%
 |  | SlideShow | -0.04% | -0.08% | 0.63%
 | Class TGM | FlyingGraphic | -0.09% | -0.05% | -0.03%
 |  | Desktop | 0.02% | 0.10% | 0.06%
 |  | Console | -0.06% | -0.08% | -0.06%
 |  | ChineseEditing | -0.10% | 0.00% | -0.12%
AI | Class F | BasketballDrillText | 0.01% | -0.01% | 0.26%
 |  | ArenaOfValor | -0.02% | 0.08% | -0.05%
 |  | SlideEditing | -0.03% | -0.03% | -0.02%
 |  | SlideShow | -0.08% | -0.47% | 0.86%
 | Class TGM | FlyingGraphic | -0.02% | -0.01% | -0.01%
 |  | Desktop | -0.04% | 0.08% | 0.07%
 |  | Console | -0.13% | -0.10% | -0.07%
 |  | ChineseEditing | -0.10% | -0.09% | -0.11%
Inheritance of model information only from IBC merge candidate

## Slide 10: Experimental results
Additional test #2: Inheritance of both template shape information and model information from IBC merge candidate
  Same concept as proposed method in JVET-AG0186
AI | Class F | BasketballDrillText | 0.01% | -0.01% | 0.26%
 |  | ArenaOfValor | -0.02% | 0.08% | -0.05%
 |  | SlideEditing | -0.03% | -0.03% | -0.02%
 |  | SlideShow | -0.08% | -0.47% | 0.86%
 | Class TGM | FlyingGraphic | -0.02% | -0.01% | -0.01%
 |  | Desktop | -0.04% | 0.08% | 0.07%
 |  | Console | -0.13% | -0.10% | -0.07%
 |  | ChineseEditing | -0.10% | -0.09% | -0.11%
Inheritance of model information only from IBC merge candidate
AI | Class F | BasketballDrillText | -0.03% | 0.03% | 0.19%
 |  | ArenaOfValor | #VALUE! | #VALUE! | #VALUE
 |  | SlideEditing | -0.09% | -0.27% | -0.16%
 |  | SlideShow | -0.08% | -0.09% | 0.52%
 | Class TGM | FlyingGraphic | -0.04% | 0.06% | 0.03%
 |  | Desktop | 0.03% | 0.10% | 0.02%
 |  | Console | -0.08% | -0.09% | -0.09%
 |  | ChineseEditing | -0.08% | 0.02% | -0.10%

## Slide 11: Conclusion
Proposal
  A straightforward extension for FIBC to support multiple template shapes and multiple models.
Experimental results
It is recommended to study the proposed method in the next round of EE.
JVET-AG0186 (Non-EE2: FIBC Extension) is very similar to ours
 |  | Y | U | V | EncT | DecT
AI | Class F | -0.03% | -0.11% | 0.26% | 103.9% | 99.9%
 | Class TGM | -0.07% | -0.03% | -0.03% | 104.3% | 99.9%
RA | Class F | -0.09% | -0.21% | -0.10% | 101.7% | 99.6%
 | Class TGM | -0.07% | -0.08% | -0.02% | 100.9% | 100.3%

## Slide 12: Thank you