## Slide 1: JVET-AG0121: Non-EE2: Block vector guided LUT for chroma prediction
Junyan Huo, Xue Hao,
Minzhe Chen, Nengfu Qiu, Zhenyao Zhang,
Yanzhuo Ma, Fuzheng Yang,
January. 2024

## Slide 2: Proposed Method
ECM11.0 includes a method of chroma prediction in MODE_PLT.
  In dual tree partition
    the prediction process of palette is applied for luma and chroma components separately
    ignore cross-component correlations
Existed cross-component models
  CCLM、MMLM、CCCM and more models
  No discrete cross-component model
BVG-LUT method
  The block vector guided look-up table (BVG-LUT) method is proposed to improve the coding efficiency of chroma prediction for screen content.

## Slide 3: BVG-LUT method
  For chroma components when dual-tree partition is activated in I slice
    Find the luma blocks in MODE_IBC and intraTMP, and obtain their block vectors bvLs
    Scale bvLs to get the BV’s list depending on the chroma format sampling structure
    Use the BV’s list to construct the cross-component LUT
  The prediction process
    Obtain the down-sampled luma value with multi-filter
    Find chroma value by mapping the cross-component LUT with the down-sampled luma
  The Encoder
    Encoder tries the candidate down-sampling filters and signals an index of the best filter to the decoder.

## Slide 4: Experimental results
Anchor: ECM-11.0 under CTC
All Intra Main 10 |  |  |  |  | 
 |  |  | Over ECM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class F | -0.02% | -0.49% | -0.44% | 103.4% | 101.5%
Class TGM | -0.59% | -1.01% | -1.35% | 102.6% | 98.8%
Random Access Main10 |  |  |  |  | 
 |  |  | Over ECM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class F | -0.04% | -0.22% | -0.20% | 101.0% | 99.8%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!

## Slide 5: Conclusion
Propose a block vector guided LUT (BVG-LUT) method
  This contribution proposes a method to improve the coding efficiency of chroma intra prediction for screen content.
On top of ECM-11.0
  AI: F: -0.02%, -0.49 %, -0.44 % TGM : -0.59 %, -1.01 %, -1.35 %
  RA: F: -0.04 %, -0.22%, -0.20 % TGM: xxx %, xxx %, xxx %
Recommend to investigate in EE2
Thanks Alibaba for crosscheck !

## Slide 6
Thank you