## Slide 1
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3
JVET-AG0209 AHG8: A suggestion for the performance evaluation of VCM
Shurun Wang, Jie Chen, Yan Ye, Shiqi Wang
Jan. 2024

## Slide 2: Outline
Introduction
Test1
Test2
Conclusion

## Slide 3: Introduction
A variety of machine vision models proposed, even for a specific machine task
  Object detection
  Object tracking
However, in current common test conditions (CTC) of VCM
  Only a single machine vision model is used to evaluate the VCM performance
  VCM performance evaluation may not be stable
Data from Google scholar advanced search: allintitle: “object detection” or “object tracking.”
Over 1000 papers published for each task every year since 2012

## Slide 4: Introduction
To investigate the stability of the performance evaluation with a single model, two tests are designed
  Test1: One codec, two machine vision models for each task, compare the accuracies of two models
    Machine vision performance stability
  Test2: Two codecs, two machine vision models for each task, analyze the codec comparison results
    Compression efficiency stability
Codec | Detection |  | Tracking | 
VTM-22.2 | Faster-RCNN-X101-FPN (X101) | Faster-RCNN-R101-FPN (R101) | JDE-1088x608 | JDE-864x480
Codec | Detection |  | Tracking | 
Anchor: VTM-22.2 | X101 | R101 | JDE-1088x608 | JDE-864x480
Test: HM-18.0 | X101 | R101 | JDE-1088x608 | JDE-864x480
The model name in bold indicates the machine model used in CTC

## Slide 5: Outline
Introduction
Test1
Test2
Conclusion

## Slide 6: Test1
Investigate the machine vision performance stability
  Stable machine vision performance (for two machine vision models: A and B):
    If model A is better than model B on original video
    On compressed videos
        ✅For full bitrate range, model A is better than model B
        ✅For high bitrate range, model A is better than model B; for low bitrate range,
          model B is better than model A
        Otherwise, if model B is alternately better than model A across the bitrate range, machine vision performance is somewhat unstable
          Multiple intersections between two curves
Conduct experiments on object detection and object tracking respectively
Notes: Explain what is stable machine vision performance

## Slide 7: Test1-object detection RA
Showcases on SFU-HW dataset under random access (RA) configuration
Multiple intersections between the two rate-accuracy curves can be observed.
Similar for other configurations
  The intersections between two rate-accuracy curves are annotated with red square box in dashed lines, same below.

## Slide 8: Test1-object detection LD
Showcases on SFU-HW dataset under low delay (LD) configuration

## Slide 9: Test1-object detection AI
Showcases on SFU-HW dataset under all intra (AI) configuration

## Slide 10: Test1-object tracking
Similar cases could be observed for object tracking task on TVD dataset
Machine performances evaluated with different models are not stable
RA
LD
AI

## Slide 11: Outline
Introduction
Test1
Test2
Conclusion

## Slide 12: Test2-object detection: summary
Anchor: VTM-22.2
Test: HM-18.0
  Evaluate with R101 and X101, respectively.
  Compare R101 and X101 evaluation results
Dramatic performance difference between R101 and X101 (labeled in red, same below)
RA | R101 |  | X101 | 
SFU-HW | Pareto BD mAP | BD-mAP | Pareto BD mAP | BD-mAP
Class A | 294.17% | -2.19 | 85.43% | -1.82
Class B | 113.37% | -0.57 | 63.70% | -3.00
Class C | 37.82% | -2.53 | 26.30% | -1.66
Class D | 9.60% | -0.58 | 11.12% | -0.21
Avg | 72.10% | -1.30 | 37.68% | -1.64
LD | R101 |  | X101 | 
SFU-HW | Pareto BD mAP | BD-mAP | Pareto BD mAP | BD-mAP
Class A | 50.34% | -0.79 | -13.02% | 0.10
Class B | 66.45% | -3.11 | 51.08% | -4.63
Class C | 28.14% | -2.37 | 13.43% | -0.92
Class D | -9.04% | 0.39 | -4.61% | 0.20
Avg | 30.20% | -1.63 | 17.43% | -1.64
AI | R101 |  | X101 | 
SFU-HW | Pareto BD mAP | BD-mAP | Pareto BD mAP | BD-mAP
Class A | 2.24% | -0.20 | 39.71% | -1.63
Class B | 57.04% | -6.55 | 31.03% | -6.28
Class C | 16.05% | -1.20 | 19.02% | -1.50
Class D | 7.15% | -1.11 | 6.41% | -1.06
Avg | 24.86% | -2.74 | 20.43% | -2.85

## Slide 13: Test2-object detection: showcases
RA
  Obvious inconsistent rate-accuracy curves can be observed, under X101 and R101 evaluation.
  The performance metrics under X101 and R101 evaluation can also be dramatically different.
Similar cases listed below for other sequences with other configurations
Notes:   BasketballPass_416x240_50 sequence
    Under X101 evaluation
      HM-18.0 is better than VTM-22.2 at middle bitrate.
    Under R101 evaluation
      HM-18.0 is worse than VTM-22.2 at full bitrate.

## Slide 14: Test2-object detection: showcases
LD

## Slide 15: Test2-object detection: showcases
AI

## Slide 16: Test2-object tracking: summary
RA | JDE-864x480 |  | JDE-1088x640 | 
TVD | Pareto BD MOTA | BD-MOTA | Pareto BD MOTA | BD-MOTA
TVD-01-1 | 12.98% | -0.32 | 24.11% | -0.99
TVD-01-2 | 2.05% | -0.06 | 33.27% | 0.56
TVD-01-3 | -4.40% | 0.40 | 59.32% | -9.58
TVD-02-1 | 56.76% | -1.93 | 113.86% | -6.32
TVD-03-1 | 61.45% | -0.82 | 16.95% | -0.86
TVD-03-2 | -42.41% | #NUM! | -31.14% | 1.43
TVD-03-3 | 6.80% | -0.34 | -20.69% | 1.03
Avg | 13.32% | #NUM! | 27.95% | -2.10
Anchor: VTM-22.2
Test: HM-18.0
  Evaluate with JDE-864x480 and JDE-1088x640, respectively.
  Compare two machine model evaluation results.
Dramatic performance difference
LD | JDE-864x480 |  | JDE-1088x640 | 
TVD | Pareto BD MOTA | BD-MOTA | Pareto BD MOTA | BD-MOTA
TVD-01-1 | -1.75% | 0.15 | 110.04% | -5.17
TVD-01-2 | 112.07% | 0.20 | 164.91% | -4.27
TVD-01-3 | 129.55% | -0.93 | 65.67% | -3.45
TVD-02-1 | 51.32% | -1.91 | 137.08% | #NUM!
TVD-03-1 | -4.42% | 0.02 | 7.63% | -0.56
TVD-03-2 | -36.71% | 0.76 | 12.48% | 0.50
TVD-03-3 | 76.88% | -0.83 | -17.88% | 1.33
Avg | 46.70% | -0.36 | 68.56% | #NUM!
AI | JDE-864x480 |  | JDE-1088x640 | 
TVD | Pareto BD MOTA | BD-MOTA | Pareto BD MOTA | BD-MOTA
TVD-01-1 | -10.44% | 0.51 | 20.48% | -1.84
TVD-01-2 | -1.72% | 0.36 | 11.53% | -0.30
TVD-01-3 | -1.32% | 0.14 | 26.43% | -1.94
TVD-02-1 | 17.39% | -0.71 | 56.24% | -2.11
TVD-03-1 | -20.83% | 1.06 | -24.23% | 1.59
TVD-03-2 | -20.74% | 0.85 | -41.90% | 2.89
TVD-03-3 | -12.26% | #NUM! | -21.94% | 2.05
Avg | -7.13% | #NUM! | 3.80% | 0.05
#NUM! indicates the corresponding metric cannot be calculated due to the non-monotonicity of machine vision performance

## Slide 17: Test2-object tracking: showcases
RA

## Slide 18: Test2-object tracking: showcases
LD

## Slide 19: Test2-object tracking: showcases
AI

## Slide 20: Outline
Introduction
Test1
Test2
Conclusion

## Slide 21: Conclusion
Performance evaluation with a single machine vision model as in the current VCM CTC may be somewhat unstable.
Suggest to consider more machine vision models for inclusion in the VCM CTC.

## Slide 22
Thanks
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3

## Slide 23
Backup

## Slide 24: Stable machine vision performance
kbps
mAP
kbps
mAP
The example of stable machine vision performance
  In terms of the relationship between performances of model A and model B
Red line: model A
Blue line: model B

## Slide 25: Test2-object detection: summary
Dramatic Performance difference between R101 and X101 (labeled in red, same below)
RA | R101 |  |  |  | X101 |  |  | 
SFU-HW | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP
 | mAP | mAP (low4) | Pareto mAP |  | mAP | mAP (low4) | Pareto mAP | 
Class A | #NUM! | #NUM! | 294.17% | -2.19 | #NUM! | #NUM! | 85.43% | -1.82
Class B | #NUM! | #NUM! | 113.37% | -0.57 | #NUM! | 80.11% | 63.70% | -3.00
Class C | #NUM! | 41.92% | 37.82% | -2.53 | 26.30% | 33.67% | 26.30% | -1.66
Class D | #NUM! | 5.63% | 9.60% | -0.58 | #NUM! | #NUM! | 11.12% | -0.21
Avg | #NUM! | #NUM! | 72.10% | -1.30 | #NUM! | #NUM! | 37.68% | -1.64
LD | R101 |  |  |  | X101 |  |  | 
SFU-HW | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP
 | mAP | mAP (low4) | Pareto mAP |  | mAP | mAP (low4) | Pareto mAP | 
Class A | #NUM! | #NUM! | 50.34% | -0.79 | #NUM! | #NUM! | -13.02% | 0.10
Class B | #NUM! | #NUM! | 66.45% | -3.11 | #NUM! | #NUM! | 51.08% | -4.63
Class C | #NUM! | 29.89% | 28.14% | -2.37 | 13.43% | 23.68% | 13.43% | -0.92
Class D | -9.04% | #NUM! | -9.04% | 0.39 | #NUM! | #NUM! | -4.61% | 0.20
Avg | #NUM! | #NUM! | 30.20% | -1.63 | #NUM! | #NUM! | 17.43% | -1.64
AI | R101 |  |  |  | X101 |  |  | 
SFU-HW | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP | End-to-End BD-Rate [%] |  |  | End-to-End BD-mAP
 | mAP | mAP (low4) | Pareto mAP |  | mAP | mAP (low4) | Pareto mAP | 
Class A | #NUM! | #NUM! | 2.24% | -0.20 | 39.71% | 29.07% | 39.71% | -1.63
Class B | #NUM! | 62.15% | 57.04% | -6.55 | #NUM! | 38.38% | 31.03% | -6.28
Class C | 16.05% | 19.03% | 16.05% | -1.20 | 19.02% | 24.36% | 19.02% | -1.50
Class D | #NUM! | 6.68% | 7.15% | -1.11 | 6.41% | 5.00% | 6.41% | -1.06
Avg | #NUM! | #NUM! | 24.86% | -2.74 | #NUM! | 23.08% | 20.43% | -2.85
#NUM! indicates the corresponding metric cannot be calculated due to the non-monotonicity of machine vision performance

## Slide 26: Test2-object detection: showcases
RA
  Obvious inconsistent rate-accuracy curves can be observed, under X101 and R101 evaluation.
  The performance metrics under X101 and R101 evaluation can also be dramatically different.
Similar cases listed below for other sequences with other configurations
Notes:   BasketballPass_416x240_50 sequence
    Under X101 evaluation
      HM-18.0 is better than VTM-22.2 at middle bitrate.
    Under R101 evaluation
      HM-18.0 is worse than VTM-22.2 at full bitrate.

## Slide 27: Test2-object detection: showcases
LD

## Slide 28: Test2-object detection: showcases
AI

## Slide 29: Test2-object tracking: summary
LD | JDE-864x480 |  |  |  | JDE-1088x640 |  |  | 
TVD | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA
 | MOTA | MOTA (low4) | Pareto MOTA |  | MOTA | MOTA (low4) | Pareto MOTA | 
TVD-01-1 | #NUM! | #NUM! | -1.75% | 0.15 | 110.04% | 104.50% | 110.04% | -5.17
TVD-01-2 | #NUM! | 98.57% | 112.07% | 0.20 | #NUM! | 198.52% | 164.91% | -4.27
TVD-01-3 | #NUM! | #NUM! | 129.55% | -0.93 | #NUM! | 83.76% | 65.67% | -3.45
TVD-02-1 | 51.32% | 77.32% | 51.32% | -1.91 | #NUM! | #NUM! | 137.08% | #NUM!
TVD-03-1 | #NUM! | 0.80% | -4.42% | 0.02 | #NUM! | 31.82% | 7.63% | -0.56
TVD-03-2 | #NUM! | #NUM! | -36.71% | 0.76 | #NUM! | #NUM! | 12.48% | 0.50
TVD-03-3 | 76.88% | 44.26% | 76.88% | -0.83 | -17.88% | -32.37% | -17.88% | 1.33
Avg | #NUM! | #NUM! | 46.70% | -0.36 | #NUM! | #NUM! | 68.56% | #NUM!
RA | JDE-864x480 |  |  |  | JDE-1088x640 |  |  | 
TVD | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA
 | MOTA | MOTA (low4) | Pareto MOTA |  | MOTA | MOTA (low4) | Pareto MOTA | 
TVD-01-1 | #NUM! | #NUM! | 12.98% | -0.32 | #NUM! | #NUM! | 24.11% | -0.99
TVD-01-2 | 2.05% | 6.52% | 2.05% | -0.06 | #NUM! | #NUM! | 33.27% | 0.56
TVD-01-3 | #NUM! | 9.25% | -4.40% | 0.40 | #NUM! | 56.57% | 59.32% | -9.58
TVD-02-1 | #NUM! | 55.34% | 56.76% | -1.93 | #NUM! | #NUM! | 113.86% | -6.32
TVD-03-1 | #NUM! | 44.34% | 61.45% | -0.82 | #NUM! | 0.34% | 16.95% | -0.86
TVD-03-2 | #NUM! | -42.80% | -42.41% | #NUM! | #NUM! | #NUM! | -31.14% | 1.43
TVD-03-3 | #NUM! | -6.49% | 6.80% | -0.34 | -20.69% | -30.05% | -20.69% | 1.03
Avg | #NUM! | #NUM! | 13.32% | #NUM! | #NUM! | #NUM! | 27.95% | -2.10
LD | JDE-864x480 |  |  |  | JDE-1088x640 |  |  | 
TVD | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA | End-to-End BD-Rate [%] |  |  | End-to-End BD-MOTA
 | MOTA | MOTA (low4) | Pareto MOTA |  | MOTA | MOTA (low4) | Pareto MOTA | 
TVD-01-1 | #NUM! | 0.74% | -10.44% | 0.51 | 20.48% | 20.95% | 20.48% | -1.84
TVD-01-2 | #NUM! | 13.05% | -1.72% | 0.36 | #NUM! | 10.04% | 11.53% | -0.30
TVD-01-3 | -1.32% | 30.88% | -1.32% | 0.14 | #NUM! | 28.17% | 26.43% | -1.94
TVD-02-1 | 17.39% | 32.77% | 17.39% | -0.71 | 56.24% | 61.74% | 56.24% | -2.11
TVD-03-1 | #NUM! | #NUM! | -20.83% | 1.06 | #NUM! | -20.25% | -24.23% | 1.59
TVD-03-2 | -20.74% | -16.17% | -20.74% | 0.85 | -41.90% | -44.20% | -41.90% | 2.89
TVD-03-3 | #NUM! | -12.62% | -12.26% | #NUM! | -21.94% | -29.13% | -21.94% | 2.05
Avg | #NUM! | #NUM! | -7.13% | #NUM! | #NUM! | 3.91% | 3.80% | 0.05
Dramatic Performance difference

## Slide 30: Test2-object tracking: showcases
RA

## Slide 31: Test2-object tracking: showcases
LD

## Slide 32: Test2-object tracking: showcases
AI