## Slide 2: LCEVC Verification Test
Simone Ferrara (V-Nova)

## Slide 3: Outline
Overview
Development of the Verification Tests
Verification Tests Results
Compliance with NGVC Phase 2 Requirements

## Slide 4: Development of the Verification Tests

## Slide 5: Overview
The Verification Tests for LCEVC were run to verify the following requirements:
  When enhancing an n-th generation MPEG codec (e.g., AVC), compression efficiency for the aggregate stream is appreciably higher than that of the n-th generation MPEG codec used at full resolution and as close as possible to that of the (n+1)-th generation MPEG codec (e.g., HEVC) used at full resolution, at bandwidths and operating conditions relevant to mass market distribution
Preparations started in June 2020 with the final results presented in April 2021 (10 months)
  Run by MPEG Visual Assessment Group (AG5) and Video Group (WG4) with several dry-runs and subjective assessments
  Involving tens of companies and video experts, including:
    Alibaba
    Dolby (cross-checker)
    Fraunhofer HHI
    Interdigital
    Samsung (cross-checker)
    Sun Yat-sen University (cross-checker)
    Tencent (cross-checker)
    UNIVPM (cross-checker)
    V-Nova
    Zhejiang University (cross-checker)

## Slide 6: Initial set-up (Jun 2020)
18 sequences studied
  10 UHD (Class A): FoodMarket4, ParkRunning, Tango2, Toddlerfountain, Catrobot1, DaylightRoad2, Campfire, Petibato, Sedof, LupoPuppet
  8 HD (Class B): Cactus, BasketballDrive, RitualDance, BQTerrace, MarketPlace, Zoo, Starcraft, PierSeaside
Initial target bitrates
  UHD (Class A): 7Mbps to 20Mbps
  HD (Class B): 3Mbps to 10Mbps
Initial intention was to compare full-resolution base codecs (AVC, HEVC, EVC and VVC) versus LCEVC-enhanced versions of the same codecs
  Selection of the sequences, target bitrates and configurations based on BD-rates, subjective assessments and expert viewing (if needed)
  55” TV set, with OLED screen set with “standard” viewing option

## Slide 7: First dry-run and anchor selection (Jul 20 - Oct 20)
First dry-run (subjective assessment) performed by Test Chair in September 2020
Four UHD sequences selected for each base codec (9 in total)*
  AVC/HEVC: Tango2, CatRobot1, NeptuneFountain3, LupoPuppet
  EVC: BarScene, Netflix_DrivingPoV, Dancers, CatRobot1
  VVC: Marathon, MountainBay3, Netflix_DrivingPoV, NeptuneFountain3
Initial target bitrates and QPs for each anchor selected based on subjective assessment
  Bitrate range between 1.5Mbps and 19Mbps to “enable meaningful subjective testing of the anchors for each sequence in order to verify compliance with the requirements”
  QPs selected based on BD-rates (PSNR and VMAF) and then verified by Test Chair to “confirm that these QPs span a range of expected MOS between 3 and 8”
* Some sequences were discarded as they were used in the development phase, and some others were added for consideration based on the respective verification tests done for other codecs (NeptuneFountain3, Marathon, MountainBay3, Dancers, Netflix_DrivingPoV and BarScene)

## Slide 8: Additional changes and first VT pass (Oct 20 - Jan 21)
Request to add half-resolution anchors in addition to full-resolution anchors
  As a consequence, a set of new sequences was required “in order to enable check of the effect of the LCEVC scheme compared to a simple upsampling process”
  These two sequences were based on Driving PoV and a boxing sequence taken from Netflix El Fuente test set and modified with some overlay of logos and news/sports banners.
Furthermore, various changes were agreed
  Change the sequence “Dancers” for EVC and limit range of bitrates to avoid inflating BD-rates at saturation points*
  Fix LCEVC quantization parameters and anchor them to base QPs
A first pass of the Verification Tests (done only on AVC and VVC) was performed and presented in January 2021
* This was observed particularly in the verification tests for EVC

## Slide 9: Verification Tests set-up (Jan 21 - Apr 21)
The final verification test plan was agreed in January 2021*
Tests done comparing full and half-resolutions codecs (i.e., AVC, HEVC, EVC and VVC) vs. respective full-resolution LCEVC enhanced codecs
Six sequences tested for each codec:
  two Class A (UHD) sequences without particularly sharp details
  two Class A (UHD) sequences with some sharp details
  two Class B (HD) sequences with many sharp details
* For more information, please see “Updated Verification Test Plan for Low Complexity Enhancement Video Coding (LCEVC)”, January 2021, m20015/N0063, (https://dms.mpeg.expert/doc_end_user/documents/133_OnLine/wg11/MDS20015_WG04_N00063.zip)

## Slide 10: Verification Tests set-up (Jan 21 - Apr 21)
Example of sequence without particularly sharp details
Example of sequence with some sharp details

## Slide 11: Verification Tests set-up
Double-stimulus impairment scale (DSIS) test method [ITU-R BT.500-14]
Viewing distance: 2H
TV
  65”, OLED screen, 10bit
  Manufacturer default settings
  Model: LG OLED65CX6LA (released in 2020)
Participants
  50 viewers (20 women, 30 men)

## Slide 12: Timeline
June 2020
Initial set-up
First dry-run
October 2020
First verification test pass
January 2021
Final verification tests
April 2021
Sequence selection
18 initial sequences
9 UHD sequences
2 new sharp UHD sequences
6 sequences per codec
(24 sequences in total)
Key decisions
Full-resolution codecs vs LCEVC-enhanced versions
Lab set-up
Anchor selection
Add half-resolution anchors
Fix LCEVC quantization
Final sequence and parameters
Full and half-resolutions codecs vs. respective full-resolution LCEVC enhanced codecs
Configuration selection
UHD range: 7-20 Mbps
HD range: 3-10 Mbps
Anchor bitrate range: 1.5-19 Mbps
Selection to span 3-8 MOS range
LCEVC configurations selected
Events

## Slide 13: Verification Tests Results

## Slide 14: Verification Tests results (Apr 21)
LCEVC-enhanced full-resolution vs. full-resolution
  The average bit rate savings for LCEVC when enhancing AVC were determined to be approximately 46% for UHD and 28% for HD.
  The average bit rate savings for LCEVC when enhancing HEVC were determined to be approximately 31% for UHD and 24% for HD
  Numerical analysis of the average benefit of LCEVC and its statistical significance compared to the corresponding full resolution EVC or VVC codec was more difficult to interpret, due to several test points having overlapping confidence intervals. However, the test results tend to indicate an overall benefit when using LCEVC with these two codecs

## Slide 15: Verification Tests results (Apr 21)
LCEVC-enhanced full-resolution vs. half-resolution
  Comparing LCEVC full-resolution encoded sequences with the up-sampled half-resolution anchors, the average bit-rate savings when using LCEVC with AVC, HEVC, EVC, and VVC were calculated to be approximately 28%, 34%, 38%, and 33% respectively for UHD, and 27%, 26%, 21%, and 21% respectively for HD

## Slide 16: Verification Tests results (Apr 21)
Comparison of upsampled half-resolution base (left) vs. LCEVC-enhanced full resolution (right)*
* Screenshots taken from (https://dms.mpeg.expert/doc_end_user/documents/133_OnLine/wg11/MDS20015_WG04_N00063.zip)