## Slide 1: AHG13: Frequency domain Film Grain Objective Metric with Adaptive Region Selection
Xuewei Meng, Wenhao Zhang, Scott Labrozzi (Disney Streaming)
Jan. 2024

## Slide 2: Outline
Background: subband based film grain assessment (SFGA proposed in JVET-AF0209)
Proposed method: SFGA with adaptive region selection (SFGA-2.0)
Evaluation of film grain quality metrics
Conclusion

## Slide 3: Subband based film grain assessment (SFGA)

## Slide 4: Subband based film grain assessment (SFGA)
Framework

## Slide 5: Subband based film grain assessment (SFGA)
Shortcomings
  The SFGA is conducted on the grain-only image, which means that the clean/denoised image is needed. However, the clean image is usually unavailable, and the denoiser may be not strong enough to extract the film grain from the grainy image properly.
  The SFGA is performed on the manually selected flat regions. However, in the practical use cases, manually selecting all the flat regions for each image is unrealistic. So adaptive region selection is essential.

## Slide 6: SFGA investigation
Experimental settings
  Randomly select NxN blocks, and conduct SFGA on them
Conclusion 1: For grain-only input, the impact of selected regions on the SFGA performance is quite minor. SFGA is robust enough to be applied to all kinds of grain-only inputs.
Conclusion 2: For content+grain input, the region selection has a large impact on the performance of SFGA. So, flat region detection is important for content+grain inputs.
Manually selected flat region

## Slide 7: Proposed method

## Slide 8: Proposed method – SFGA 2.0
Framework

## Slide 9: Main modules
Edge detection is conducted on each non-overlapped 32x32(can be adjusted) block. For each block, determine if it is a flat block based on the gradient, variance, luma value and so on.
Flat region detection: select N flat MxM blocks from the flat map. Based on the experimental results, 256x256 and 128x128 block sizes are used for this step.
Score adaptive fusion: average the N scores
Input image
Edge map
Detected flat regions

## Slide 10: Evaluation of Film Grain Objective Metrics

## Slide 11: PLCC and SROCC of SFGA, and the proposed SFGA-2.0
The smaller the value, the stronger the correlation with the MOS score.
The proposed SFGA 2.0 shows better results compared to the SFGA.
 | SFGA in JVET-AF0209 |  | Proposed SFGA 2.0 | 
 | PLCC | SROCC | PLCC | SROCC
Image1 | -0.777 | -0.790 | -0.841 | -0.851
Image2 | -0.782 | -0.771 | -0.868 | -0.904
Image3 | -0.830 | -0.741 | -0.807 | -0.842
Image4 | -0.862 | -0.767 | -0.838 | -0.828
Image5 | -0.807 | -0.689 | -0.784 | -0.805
Image6 | -0.831 | -0.721 | -0.857 | -0.753
Average | -0.815 | -0.747 | -0.833 | -0.831
All images | -0.759 | -0.777 | -0.809 | -0.821
50 data points
300 data points

## Slide 12: PLCC and SROCC of SFGA, and the proposed SFGA 2.0
The proposed SFGA 2.0 shows better results compared to the SFGA.

## Slide 13: Conclusion
The film grain metric with region selection on content+grain (SFGA 2.0) has a better performance compared to the SFGA proposed in JVET-AF0209.
This also greatly improves the completeness of the SFGA method and expands the application scenarios.
It’s recommended to further study the proposed method and collect more data from JVET subjective viewing process to validate it.

## Slide 14: Thank you