## Slide 1: JVET-AG0310 EE2-2.14-related: EIP with bias and clipping
Jani Lainema, Pekka Astola

## Slide 2
Introduction
EE2-1.14: extrapolation filter-based intra prediction mode (EIP)
Uses one of three alternative filter shapes
Trains filter using neighboring samples
Applies the selected filter recursively

## Slide 3
Introduction
EE2-1.14 prediction is formed by multiplying derived filter coefficients with a set of input samples:
This may have challenges to represent some textures. For example, a linear gradient may get presented as:
or
When applying this kind of a filter recursively the result is not a linear gradient, but an exponential field with gain of gN after N steps.

## Slide 4
Proposed improvement
Adding bias and clipping to the filter
It is proposed to:
Substitute the last spatial sample value furthest away from the output sample with a bias term
  Using 2BitDepth-1 as the bias term
Clip the predicted samples to the range of reference samples instead of full bitdepth range
Proposed form of the filters:

## Slide 5
Coding efficiency
Compared to EE2-1.14b
 | All Intra Main 10 – Original EE2-1.14b |  |  |  |  |  | 
 | Over anchor |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVm | DecVm
Class A1 | -0.20% | -0.11% | -0.11% | 102.7% | 101.9% | 100.5% | 100.5%
Class A2 | -0.22% | -0.11% | -0.09% | 102.5% | 101.8% | 101.1% | 100.8%
Class B | -0.18% | -0.16% | -0.24% | 102.2% | 101.2% | 101.1% | 100.5%
Class C | -0.16% | -0.20% | -0.15% | 101.0% | 101.1% | 100.7% | 100.3%
Class E | -0.27% | -0.09% | -0.27% | 102.4% | 100.8% | 100.3% | 100.3%
Overall | -0.20% | -0.14% | -0.18% | 102.1% | 101.3% | 100.8% | 100.4%
Class D | -0.02% | -0.21% | -0.07% | 101.7% | 100.5% | 100.1% | 100.1%
Class F | -0.07% | -0.22% | 0.02% | 102.1% | 100.2% | 100.3% | 100.3%
TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
 | All Intra Main 10 – EE2-1.14b with bias and clipping |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVm | DecVm
Class A1 | -0.24 % | -0.13 % | -0.10 % | 100.6% | 99.5% | 100.5% | 100.7%
Class A2 | -0.29 % | -0.11 % | -0.09 % | 100.2% | 98.8% | 100.6% | 100.9%
Class B | -0.22 % | -0.08 % | -0.23 % | 100.0% | 99.8% | 99.6% | 100.5%
Class C | -0.21 % | -0.18 % | -0.14 % | 100.4% | 103.3% | 100.4% | 100.2%
Class E | -0.30 % | -0.27 % | -0.37 % | 101.1% | 99.2% | 100.3% | 100.3%
Overall | -0.25 % | -0.15 % | -0.19 % | 100.4% | 100.2% | 100.2% | 100.5%
Class D | -0.03 % | -0.14 % | -0.01 % | 99.7% | 110.0% | 100.4% | 100.1%
Class F | -0.12 % | -0.03 % | 0.24 % | 100.3% | 100.1% | 100.3% | 100.4%
TGM | -0.04 % | -0.01 % | -0.05 % | 99.2% | 97.4% | 100.3% | 100.6%

## Slide 6
Coding efficiency
Individual aspects
 | All Intra Main 10 – EE2.14b with bias |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVm | DecVm
Class A1 | -0.23 % | -0.09 % | -0.15 % | 100.9% | 102.1% | 100.5% | 100.7%
Class A2 | -0.27 % | -0.07 % | -0.08 % | 100.7% | 101.2% | 100.5% | 100.8%
Class B | -0.21 % | -0.08 % | -0.22 % | 99.7% | 100.7% | 101.1% | 100.4%
Class C | -0.19 % | -0.23 % | -0.16 % | 99.2% | 100.1% | 100.3% | 100.2%
Class E | -0.27 % | -0.14 % | -0.14 % | 99.8% | 99.6% | 100.3% | 100.2%
Overall | -0.23 % | -0.12 % | -0.16 % | 100.0% | 100.7% | 100.6% | 100.5%
Class D | -0.04 % | -0.13 % | 0.09 % | 100.4% | 103.6% | 100.3% | 100.1%
Class F | -0.07 % | 0.02 % | 0.15 % | 99.1% | 100.6% | 100.3% | 100.3%
TGM | -0.04 % | -0.01 % | -0.07 % | 99.1% | 99.8% | 100.3% | 100.4%
 | All Intra Main 10 with clipping |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVm | DecVm
Class A1 | -0.20 % | -0.16 % | -0.06 % | 99.9% | 98.7% | 100.5% | 100.7%
Class A2 | -0.20 % | -0.05 % | -0.12 % | 99.7% | 99.2% | 100.5% | 100.7%
Class B | -0.19 % | -0.07 % | -0.13 % | 99.6% | 98.5% | 100.4% | 100.5%
Class C | -0.17 % | -0.28 % | -0.08 % | 100.5% | 102.9% | 100.7% | 100.3%
Class E | -0.29 % | -0.30 % | -0.17 % | 100.7% | 98.9% | 100.3% | 100.2%
Overall | -0.21 % | -0.17 % | -0.11 % | 100.0% | 99.7% | 100.5% | 100.5%
Class D | -0.03 % | -0.19 % | 0.11 % | 99.3% | 107.5% | 100.2% | 100.1%
Class F | -0.14 % | -0.33 % | -0.09 % | 99.5% | 100.4% | 100.3% | 100.3%
TGM | -0.06 % | 0.05 % | -0.07 % | 99.1% | 98.2% | 100.3% | 100.7%

## Slide 7
Summary
Including a bias term and clipping to the EIP filters:
Consistent bitrate savings
    AI - {-0.20%, -0.14%, -0.18%} original EE2-1.14b AI - {-0.23%, -0.12%, -0.16%} EE2-1.14b with a bias term AI - {-0.21%, -0.17%, -0.11%} EE2-1.14b with clipping AI - {-0.25%, -0.15%, -0.19%} EE2-1.14b with both bias and clipping
No complexity or runtime impact
Proposed to study the technique in the next round of EEs.