## Slide 1
视频技术实验室
JVET-AI0196
AHG8: On combined pre- and post-processing
and ROI-based adaptive QP for machine vision
Shurun Wang, Binzhe Li, Jie Chen, Yan Ye (Alibaba group)
Shiqi Wang (City University of Hong Kong)

## Slide 2
Outline
Framework description
Experimental results
Proposal

## Slide 3
Framework description
In previous meetings
  JVET-AB0275: ROI-based adaptive QP method (ROIAQP) for encoding optimization
  JVET-AH0157: Pre- and post-processing method (PREPOST), including:
    JVET-AD0047: Pre-processing of foreground and background
    JVET-AG0212: Enhancement post-filtering
  Included in the technical report (TR) and AGH8 software branch
In this contribution, combine both methods (JOINT)
Figure 1 The experiment flowchart on combined pre- and post-processing and ROI-based adaptive QP

## Slide 4
Experimental results
Based on common test conditions (CTC) of AHG8, evaluate performance
  Object detection task on SFU-HW dataset
  Object tracking task on TVD dataset
Task | Dataset | Methods | RA | LD | AI
Detection | SFU-HW | PREPOST | -32.75% | -33.26% | -40.29%
 |  | ROIAQP | -11.21% | -4.09% | -9.03%
 |  | JOINT | -37.11% | -34.63% | -43.34%
Table 1 Overview of the averaged BD-rate performance for detection task in terms of mono-mAP
Task | Dataset | Methods | RA | LD | AI
Tracking | TVD | PREPOST | -52.05% | -39.40% | -65.45%
 |  | ROIAQP | -28.39% | -1.38% | xx
 |  | JOINT | -62.92% | -43.69% | -72.48%
Table 1 Overview of the averaged BD-rate performance for tracking in terms of mono-MOTA

## Slide 5
Experimental results
JOINT performance on SHU-HW dataset
 |  | End-to-End BD-rate (%) |  |  | Time | 
RA | Detection | Mono-mAP | mAP | BD-mAP | Enc | Dec
SFU-HW | Class A | -17.75% | / | 2.54 | 299.27% | 583.23%
 | Class B | -38.03% | / | 7.85 | 278.88% | 766.12%
 | Class C | -41.44% | -42.68% | 6.17 | 383.23% | 1170.83%
 | Class D | -36.70% | -37.76% | 4.14 | 650.05% | 2555.82%
 | Average | -37.11% | / | 5.78 | 401.17% | 1238.39%
LD | Detection | Mono-mAP | mAP | BD-mAP | Enc | Dec
SFU-HW | Class A | -35.94% | -35.25% | 10.23 |  | 
 | Class B | -30.24% | / | 6.01 |  | 
 | Class C | -37.18% | -35.06% | 5.77 |  | 
 | Class D | -36.15% | -36.44% | 4.56 |  | 
 | Average | -34.63% | / | 5.81 |  | 
AI | Detection | Mono-mAP | mAP | BD-mAP | Enc | Dec
SFU-HW | Class A | -45.67% | -45.14% | 15.04 | 113.55% | 461.72%
 | Class B | -51.31% | / | 13.73 | 120.31% | 510.81%
 | Class C | -46.27% | -46.63% | 9.14 | 133.45% | 644.28%
 | Class D | -31.87% | -31.87% | 5.18 | 171.01% | 1159.16%
 | Average | -43.34% | / | 9.79 | 137.79% | 700.50%
lease note “/” in the tables indicates the performance cannot be calculated validly, due to the nonmonotonic machine task performance or the non-overlap between rate-accuracy curves. Same below.

## Slide 6
Experimental results
JOINT performance on TVD dataset
lease note “/” in the tables indicates the performance cannot be calculated validly, due to the nonmonotonic machine task performance or the non-overlap between rate-accuracy curves. Same below.
RA | Object Tracking | End-to-End BD-Rate [%] |  | 
 |  | Mono-MOTA | MOTA | End-to-end BD-MOTA
TVD | TVD-01-1 | -65.98% | / | 10.62
 | TVD-01-2 | -77.09% | -76.32% | 8.45
 | TVD-01-3 | -52.26% | / | 6.16
 | TVD-02-1 | -35.37% | -36.30% | 3.58
 | TVD-03-1 | -54.12% | -55.29% | 7.84
 | TVD-03-2 | -73.27% | / | 7.94
 | TVD-03-3 | -82.37% | -83.50% | 10.48
 | Average | -62.92% | / | 7.87
LD | Object Tracking | Mono-MOTA | MOTA | End-to-end BD-MOTA
TVD | TVD-01-1 | -53.92% | -58.05% | 8.02
 | TVD-01-2 | -63.09% | / | 6.93
 | TVD-01-3 | -39.11% | / | 4.39
 | TVD-02-1 | 26.41% | / | -1.32
 | TVD-03-1 | -34.94% | -34.72% | 5.75
 | TVD-03-2 | -69.67% | / | 7.14
 | TVD-03-3 | -71.48% | -72.55% | 7.35
 | Average | -43.69% | / | 5.46
AI | Object Tracking | Mono-MOTA | MOTA | End-to-end BD-MOTA
TVD | TVD-01-1 | -79.70% | -79.40% | 21.57
 | TVD-01-2 | -88.09% | -87.90% | 17.90
 | TVD-01-3 | -65.47% | / | 9.72
 | TVD-02-1 | -41.32% | -44.69% | 4.03
 | TVD-03-1 | -70.21% | -70.28% | 15.16
 | TVD-03-2 | -77.08% | -78.26% | 13.30
 | TVD-03-3 | -85.52% | -86.34% | 17.64
 | Average | -72.48% | / | 14.19

## Slide 7
Proposal
Jointly applying pre- and post-processing and ROI-based adaptive QP can achieve obvious coding performance improvement compared with pre- and post-processing or ROI-based adaptive QP only.
It’s suggested to include the combined pre- and post-processing and ROI-based adaptive QP implementation into AHG8 software branch.

## Slide 8
Proposal
It’s also suggested to update the following text into section 5.1 of the next draft of technical report (TR)
  “It is noted that depending on specific use cases, the technologies outlined in this report can be implemented individually or in combination to optimize machine consumption performance within the constraints of the system capabilities. For example, a better performance can be achieved by applying a post-filtering being optimized towards object detection on the decoded video that was pre-processed with the method described in Annex A.2 and encoded with the ROI-based adaptive QP method described in Annex A.1. When employing multiple technologies simultaneously, it is important to consider that certain combinations can be impractical or infeasible due to inherent methodological constraints.”
Thanks for the crosscheck of Nokia

## Slide 9
实验室名称
Thanks！