## Slide 1: JVET-AI0280: Non-EE2: Reuse of ALF control information
Marta Karczewicz, Hongtao Wang, Nan Hu, Vadim Seregin

## Slide 2
ALF control information in ECM-13.0
  APS/filter usage information
    Picture level: number of APSs, APS indices
    CTU level: APS index, filter set/filter index
  on/off flag at both picture and CTU levels
Proposal
  Reuse of control information from previously encoded frames
  One flag is signalled at picture level
  If the flag is true, ALF control information for current picture is not signalled
Result
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.13% | -0.46% | -0.25% | 99.9% | 99.8% | 105.9% | 109.3%
Class A2 | -0.05% | -0.33% | -0.40% | 99.9% | 100.0% | 104.9% | 107.5%
Class B | -0.12% | -0.93% | -0.86% | 100.2% | 99.5% | 104.4% | 107.4%
Class C | -0.16% | -0.52% | -0.75% | 99.8% | 100.3% | 103.0% | 104.0%
Class E |  |  |  |  |  |  | 
Overall | -0.12% | -0.60% | -0.62% | 100.0% | 99.9% | 104.4% | 106.9%
Class D | -0.40% | -1.84% | -1.65% | 99.8% | 100.0% | 102.6% | 102.5%
Class F | -0.04% | 0.26% | -0.60% | 99.8% | 99.6% | 103.1% | 103.2%
QP22 and 27 of ParkRunning3 are copied from anchor